# Open Geospatial Consortium Inc.

# buildingSMART alliance

Date: 03/23/09

Version: 1.0

Category: Engineering Report

AECOO-1 Testbed

bSa Project 2008-STP-01

AECOO-1 Testbed Draft Information Delivery Manual (IDM) for Quantity Take-Off (QTO) Thread

Integrating Communication, Process and Decision Making (CPD)

# Copyright notice

Copyright © 2009 US General Services Administration (GSA). All Rights Reserved.

# Warning

This document is not an OGC or bSa Standard or Specification. This document presents a discussion of technology issues considered in an Interoperability Initiative of a joint buildingSMART alliance/ OGC Interoperability Program Initiative. The content of this document is presented to create discussion in the AECOO industry on this topic; the content of this document is not to be considered an adopted specification of any kind. This document does not represent the official position of the OGC or buildingSMART alliance nor of the OGC Technical Committee or any alliance partner engaged in this Initiative. It is subject to change without notice and may not be referred to as an OGC or other standards organization’s Standard or Specification. However, the discussions in this document could very well lead to the definition of a specification or standard.

Recipients of this document are invited to submit, with their comments, notification of any relevant patent rights of which they are aware and to provide supporting documentation.

Table of Contents

1	Process Model	3

1.1	Overview	3

1.1.1	Cyclical Design	3

1.1.1.1	Conceptual	4

1.1.1.2	Detailed	4

1.2	Specification of Process	5

1.2.1	Concept Design Phase Quantity Take-Off	5

1.2.1.1	Concept Design BIM Complete	6

1.2.1.2	Prepare/Adjust BIM for QTO/Cost Estimate [1.1]	6

1.2.1.3	Export BIM for Analysis [1.2]	6

1.2.1.4	Calculate Quantities & Costs [1.3]	7

1.2.1.5	Review Quantity/Cost Analysis Results [1.4]	7

1.2.1.6	Prepare Submission for Review/Approval [1.5]	7

1.2.1.7	Validate BIM for QTO [1.6]	7

1.2.1.8	Calculate Quantities & Costs [1.7]	7

1.2.1.9	Review Quantity/Cost Analysis Results [1.8]	8

1.2.1.10	Prepare Analysis Report [1.9]	8

1.2.1.11	Evaluate Quantities and Cost Breakdown [1.10]	8

1.2.1.12	Prepare Design Feedback [1.11]	8

1.2.2	Prepare/Adjust BIM for Quantity Take-Off	9

1.2.2.1	Create Project Space Types [1.1.1]	10

1.2.2.2	Assign Space Types to Occurrences [1.2.3]	10

1.2.2.3	Supplemental Space Data [1.1.4]	10

1.2.2.4	Modify Building Design/Geometry [1.1.4]	11

1.2.2.5	Create Project Construction Types [1.1.5]	11

1.2.2.6	Assign Construction Types to Occurrences [1.1.6]	11

1.2.2.7	Supplemental Construction Type Data [1.1.7]	11

1.2.2.8	Validate BIM for QTO [1.1.8]	12

1.3	Specification of Data Objects	12

1.3.1.1	Library Information for Objects Types	12

1.3.1.2	Industry Construction Type Library	14

1.3.1.3	Project Construction Type Library	14

1.3.1.4	Industry Space Type Library	15

1.3.1.5	Project Space Type Library	15

1.3.1.6	Industry Classification Library – UniFormat	15

1.3.1.7	Industry Classification Library - OmniClass	16

1.3.2	Exchange Requirement Data Objects	16

1.3.2.1	ER_Arch_Concept_to_QTO_Inputs_(concept)	16

1.4	Specification of Decision Point Gateways	17

1.4.1	Ready for Quantity/Cost Analysis	17

1.4.2	Valid Quantity/Cost Analysis BIM?	18

1.4.3	Results Acceptable?	18

1.4.4	Perform Client Quantity/Cost Analysis?	18

1.4.5	Results Complete per Client Request?	18

1.4.6	Quantity/Cost Analysis Accepted?	18

2	Exchange Requirements for Design to Quantity Take-Off	19

2.1	Overview	20

2.2	Exchange Requirements - Design to QTO (Concept)	20

3	Exchange Requirements for Quantity Take-Off Results to Design	28

3.1	Overview	29

3.2	Exchange Requirements - QTO to Design	29

# Process Model

| Name | OGC/bSa – Quantity Take-Off at Concept Design Phase |
| --- | --- |

| Change Log |
| --- |
| 5-Jan-09 | Initial creation of version 0.01, draft for internal review | Tom Wiggins |
| 4-Feb-09 | Edits creating version 0.02 | Tom Wiggins |
| 11-Feb-09 | Edits creating version 0.03 | Tom Wiggins |
| 18-Feb-09 | Edits for version 0.5 - adding 'ER QTO to Design' to the process diagram, expanding table for 'ER Design to QTO' | Richard See |
| 23-Feb-09 | Edits for version 0.6 -- expanded ER tables significantly | Richard See |
| 23-Mar-09 | Edits for version 1.0 – integrating public comments | Tom Wiggins |

## Overview

Quantity Take-Off is a precursor to completing a cost estimate to determine whether the design meets the project budget. In the early design (conceptual) design phase, quantities used for estimating are building or elemental level quantities as more detailed design information is not available. For example, the conceptual phase allows:

walls and slabs by area,

windows by count by size,

spaces by area,

structural system by facility area,

heating system by facility area,

cooling system by facility area,

The output of the quantity take-off may be the result of a report produced by the cost estimating application, which shows quantities. Other than a valid IFC file for use by cost estimating applications, the QTO process does not produce any output.

Throughout the estimating process the estimator typically communicates through various media with the design team, and perhaps the owner, to understand the design intent fully providing an appropriate estimate of building costs. Often, this post model output interaction among the various actors / roles is not captured formally. For Communication, Process and Decision (CPD) Making functionality, the BIM must be able to document the actors / roles interacting with the model. The various actors and roles mentioned specifically in the IDM are not indicative of all potential actors / roles at early design stages.

### Cyclical Design

The process of outputting a quantity take-off is cyclical to match the design submittal requirements. It supports the cost estimating requirements to verify that the project design is within the established budget. The quantity take-off will have increasing complexity as the design progresses from early concept through final design.

#### Conceptual

This is the analysis work undertaken during the programming and concept design stage of the project. It is about providing advice on the potential construction cost of a building to design roles and the client. The aim of this analysis is to determine the feasibility of concepts in a capital cost context. Conceptual analysis may be undertaken in the absence of detailed geometric information about the building layout, though frequently general spatial layout is included during this stage. Assumptions typically must be made at this stage, maintaining consistent assumptions between the options being evaluated allows for evaluation of relative cost performance.

#### Detailed

This is the analysis work undertaken during the schematic, design development and construction document stages of the project and assumes the availability of geometric and building system information for the design. The overall process is the same at each stage of work, the difference being simply about the extent of the information available and the level of certainty that can be applied to the information. These factors impact the analysis methods used, which may range from relatively simple area and elemental quantities at the earlier design stages to detailed quantity take-off at the later design stages.

Within this process map, the conceptual design phase of the project is shown. The process map generically refers to the Design Team, Client – Client Staff and Client – Technical Staff or Consultants. For CPD integration, OmniClass Table 33 Disciplines provides a classification for the actors and OmniClass Table 34 Organizational Roles provides a classification for the roles. Any specific project team may require expanding the generic roles shown in process map to define in greater detail the actors and roles of the project.

## Specification of Process

### Concept Design Phase Quantity Take-Off

#### Concept Design BIM Complete

| Type | Initial Concept BIM |
| --- | --- |
| Documentation | It is assumed at this point the architect has defined a building concept design complete with all the required building elements and space objects. This design provides a proposed building layout including functional and non-functional space configuration and placement of other geometric elements. Non-functional spaces such as technical spaces, circulation spaces, shafts, etc. must be defined by a space object and not left as unidentifiable voids surrounded by geometry. Spaces that represent multi-story spaces such as atria and vertical distribution routes such as shafts, stairways and elevator shafts should be represented as distinct spaces at each level of the building that are related to each other vertically (either via an opening in a slab or an element located at the opening for e.g. safety purposes). The Concept Design BIM should include: the site and building location the building orientation including its relationship to true north the site and building elevation above a reference datum the building story information 3D geometry of adjacent buildings 3D geometry of the building, including walls (exterior/interior), curtain walls, roofs, floors/slabs, ceilings, windows/skylights, doors, and shading devices space objects, including those defined by virtual space boundaries At the end of this task, the following exchange requirements from ER Arch Concept to QTO Inputs should be met: Project, Site, Building, and Building Stories. The following exchange requirements from ER Arch Concept to QTO Inputs should be partially met: Space, Wall, Slab, Opening, Beam, Column, Curtain Wall, Stair Flight, Ramp Flight, Equipment, Plumbing Fixtures, HVAC, Electrical, Hot Water Systems, Cold Water Systems and Vertical Transportation Systems. |

#### Prepare/Adjust BIM for QTO/Cost Estimate [1.1]

| Type | Sub-Process |
| --- | --- |
| Documentation | At this point, the Concept Design BIM is passed to the appropriate designer to prepare the BIM for quantity take-off. The designer may still be the architect, any other design consultant or any combination. Details of this sub-process are described in Section 1.2.2. |

#### Export BIM for Analysis [1.2]

| Type | Task |
| --- | --- |
| Documentation | Once the BIM has been prepared for quantity take-off and validated in Task 1.1, it is exported to IFC for quantity take-off. At this point, all the required exchange requirements in ER Arch Concept to QTO Inputs have been met. |

#### Calculate Quantities & Costs [1.3]

| Type | Task |
| --- | --- |
| Documentation | The designer is now almost ready to perform a quantity take-off in preparation for preparing the cost estimate. The actual cost estimating task is outside the scope of this Manual. The estimating application may use reference data such as Unit Cost Database and Construction Recipe Database to prepare the cost estimate. |

#### Review Quantity/Cost Analysis Results [1.4]

| Type | Task |
| --- | --- |
| Documentation | As the actual cost estimating task is outside the scope of this Manual, so is the review of a cost analysis. At this point, all the exchange requirements of the ER Arch Concept to QTO should be met. The results may be evaluated directly from the QTO/Cost Review Report prepared by a cost estimating application, or the results may be checked using a BIM model checker using the IFC file with the results written back to it. However, if a quantity/cost analysis is performed, the results of the quantity/cost analysis are obtained and evaluated against any cost targets that may exist. If the targets are not achieved, then the designer must go back to Task 1.1 and make further modifications to the building geometry, constructions, or some other building design variable. If the targets are achieved, the designer can move forward to Task 1.5. It is frequently the situation where the designer is evaluating a given design not just against its costs, but also against other performance targets such as energy performance, circulation efficiency, etc. If a design meets the cost targets, but falls short of energy performance targets, for example, and vice versa, then the design can be “failed” and designer will have to further iterate on the building design by returning to Task 1.1. |

#### Prepare Submission for Review/Approval [1.5]

| Type | Task |
| --- | --- |
| Documentation | Once the designer is satisfied with a design, they will prepare a submission package for client review/approval. The designer may insert URLs in the IFC BIM for the quantity and cost reports referencing the documents created in the quantity/cost analysis. |

#### Validate BIM for QTO [1.6]

| Type | Task |
| --- | --- |
| Documentation | After receipt of the IFC BIM complete with ER Arch Concept to QTO Inputs and Quantity/Cost Report (not in the scope of this Manual), the client will use a data validation tool to verify that the BIM meets the requirement of the MVD. |

#### Calculate Quantities & Costs [1.7]

| Type | Task |
| --- | --- |
| Documentation | As the actual cost estimating task is outside the scope of this Manual, so is the Calculate Quantities & Costs task. The client may use internal staff or hire an outside consultant to verify the designer’s quantity/cost results. The estimating application may use reference data such as Unit Cost Database and Construction Recipe Database to prepare the cost estimate. |

#### Review Quantity/Cost Analysis Results [1.8]

| Type | Task |
| --- | --- |
| Documentation | The results of the client quantity/cost analysis are obtained and evaluated. The results are reviewed to ensure accuracy and integrity. |

#### Prepare Analysis Report [1.9]

| Type | Task |
| --- | --- |
| Documentation | Once the client quantity/cost analysis results are verified and approved, an analysis report is prepared comparing the results of the client analysis with those of the designer. The client or consultants may insert URLs in the IFC BIM for the quantity and cost reports referencing the documents created in the quantity/cost analysis. |

#### Evaluate Quantities and Cost Breakdown [1.10]

| Type | Task |
| --- | --- |
| Documentation | The client will evaluate the analysis report submitted by their internal staff or consultant. Costs will be evaluated against the cost targets, resulting in a "go/no go" decision for the design. |

#### Prepare Design Feedback [1.11]

| Type | Task |
| --- | --- |
| Documentation | The client will document the resulting quantities and cost analysis (which may or may not include an independent quantities and cost analysis for comparison/validation), and recommendations for the design team. The design feedback package will be delivered back to the designer, and will include either an approval or rejection of the design originally submitted to the client by the designer. |

### Prepare/Adjust BIM for Quantity Take-Off

#### Create Project Space Types [1.1.1]

| Type | Task |
| --- | --- |
| Documentation | This process considers that an industry space type data library exists from which a project specific space type library can be derived. The industry space type library may be accessed from a server over the web or from directly within the BIM-authoring application. The project specific space type library contains only definitions of those space types that can be used on the project of concern. Ensure Valid Space Utilization Zones Where Space Utilization Zones are not otherwise available through the building information model, they need to be created for quantity take-off purposes. When defining the Space Utilization Zones, the following information is required: Relating space (the space which the boundary is to define for the building element) Related building element (the building element to which the space is related) Connection geometry (the form of the space boundary geometry; surface geometry should be used by preference to give the 2D topographical boundary and this should be for both horizontal and vertical boundaries. Physical or virtual boundary Internal or external space |

#### Assign Space Types to Occurrences [1.2.3]

| Type | Task |
| --- | --- |
| Documentation | Once the project space type library has been created, the designer may assign the space types to space occurrences, making a connection between the space occurrence and the type of space to which it conforms. |

#### Supplemental Space Data [1.1.4]

| Type | Task |
| --- | --- |
| Documentation | This task deals with individual spaces that may not be defined fully within the project space type library, or not defined to the designer’s satisfaction. Initial data may be taken from a library template, but is then updated (or added) for the particular space being dealt with. Upon completion, information about this space may be saved back to the project space type library for future application. At the end of this task, the following exchange requirements from ER Arch Concept to QTO Inputs should be met: Project, Site, Building, Building Stories, Spaces. The following exchange requirements from ER Arch Concept to QTO Inputs should be met partially: Beam, Column, Stair Flight, Ramp Flight, Equipment, Plumbing Fixtures, HVAC, Electrical, Hot Water Systems, Cold Water Systems and Vertical Transportation Systems. |

#### Modify Building Design/Geometry [1.1.4]

| Type | Task |
| --- | --- |
| Documentation | In this step, the designer makes any necessary modifications to the building geometry or any other building design parameter other than those addressed by project construction or space types. At the end of this task, the following exchange requirements from ER Arch Concept to QTO Inputs should be met: Project, Site, Site, Building, Building Stories, and Spaces. The following exchange requirements from ER Arch Concept to QTO Inputs should be met partially: Space, Beam, Column, Stair Flight, Ramp Flight, Equipment, Plumbing Fixtures, HVAC, Electrical, Hot Water Systems, Cold Water Systems and Vertical Transportation Systems. |

#### Create Project Construction Types [1.1.5]

| Type | Task |
| --- | --- |
| Documentation | This process considers that an industry construction type data library exists from which a project specific construction type library can be derived. The construction type selected for a building element impacts the capital cost of the project. The industry construction type library may come from a variety of sources. However, for the Testbed with GSA the BPEA Construction Types is used to align with the BPEA Thread. The industry construction type library may be accessed from a server over the web or from directly within the BIM-authoring application. The project specific construction type library contains only definitions of those construction types that can be used on the project of concern. A single construction object may have one, two, three, or more construction types assigned to it based on the needs of the client. The default assumptions based on the project construction type is meant to be a starting point only, and the values may be modified prior to running the simulation. |

#### Assign Construction Types to Occurrences [1.1.6]

| Type | Task |
| --- | --- |
| Documentation | Once the project space type library has been created, the designer may assign the construction types to building element occurrences, making a connection between the building element occurrence and the type of construction to which it conforms. |

#### Supplemental Construction Type Data [1.1.7]

| Type | Task |
| --- | --- |
| Documentation | This task deals with individual constructions that may not be defined fully within the project construction type library, or not defined to the designer’s satisfaction. Initial data may be taken from a library template but is then updated (or added) for the particular space being dealt with. Upon completion, information about this construction may be saved back to the project construction type library for future application. At the end of this task, the following exchange requirements from ER Arch Concept to QTO Inputs should be met: Project, Site, Building, Building Stories, Spaces, Beam, Column, Stair Flight, Ramp Flight, Equipment, Plumbing Fixtures, HVAC, Electrical, Hot Water Systems, Cold Water Systems and Vertical Transportation Systems. |

#### Validate BIM for QTO [1.1.8]

| Type | Task |
| --- | --- |
| Documentation | After geometry, construction type, space type, and any other modifications to the building are made, the BIM is ready to be validated for quantity and cost analysis. Validation will take place by exporting an IFC file and using a model checker to ensure the MVD requirements have been met. |

## Specification of Data Objects

#### Library Information for Objects Types

| Type | Data Object |
| --- | --- |
| Documentation | At the Concept design stage, designers have not modeled many of the building data objects, yet descriptive data provides useful information for preparing a cost estimate. Site Object The Industry Classification source is UniFormat. See Section 1.3.1.6 Industry Classification Library – UniFormat. Building Object The functional classification source is OmniClass Table 11 (construction entities by function). However, for the Testbed with GSA use the IBC classifications to align with BPEA. Building Story Object No recognized standard functional classification source is identified. Descriptors used by the model are sufficient. Above grade and below grade are common descriptors. Space Object See Section 1.3.1.4 Industry Space Type Library. Wall Object The Industry Classification source is UniFormat. See Section 1.3.1.6 Industry Classification Library – UniFormat. Each object shall have an indicator for load bearing or non-load bearing. Each object shall have an indicator for fire rating (including not applicable). The Testbed for GSA uses the BPEA Industry Construction Types Library to align with the BPEA Thread. Slab Object The Industry Classification source is UniFormat. See Section 1.3.1.6 Industry Classification Library – UniFormat. The Testbed for GSA uses the BPEA Industry Construction Types Library to align with the BPEA Thread. Beam Object The Industry Classification source is UniFormat. See Section 1.3.1.6 Industry Classification Library – UniFormat. Column Object The Industry Classification source is UniFormat. See Section 1.3.1.6 Industry Classification Library – UniFormat. Opening Object It does not require an Industry Classification. Door Object The Industry Classification source is UniFormat. See Section 1.3.1.6 Industry Classification Library – UniFormat. Each object shall have an indicator for fire rating (including not applicable). The Testbed for GSA uses the BPEA Industry Construction Types Library to align with the BPEA Thread. Window Object The Industry Classification source is UniFormat. See Section 1.3.1.6 Industry Classification Library – UniFormat. Each object shall have an indicator for fire rating (including not applicable). The Testbed for GSA uses the BPEA Industry Construction Types Library to align with the BPEA Thread. Curtain Wall Object The Industry Classification source is UniFormat. See Section 1.3.1.6 Industry Classification Library – UniFormat. Stair Flight Object The Industry Classification source is UniFormat. See Section 1.3.1.6 Industry Classification Library – UniFormat. Ramp Flight Object The Industry Classification source is UniFormat. See Section See Section 1.3.1.6 Industry Classification Library – UniFormat.. Equipment Object The Industry Classification source is OmniClass table 23, products. Plumbing Fixtures Object The Industry Classification source is UniFormat. See Section 1.3.1.6 Industry Classification Library – UniFormat. HVAC System Object The Industry Classification source is UniFormat. See Section 1.3.1.6 Industry Classification Library – UniFormat. Electrical System Object The Industry Classification source is UniFormat. See Section 1.3.1.6 Industry Classification Library – UniFormat. Hot Water System Object The Industry Classification source is UniFormat. See Section 1.3.1.6 Industry Classification Library – UniFormat. Cold Water System Object The Industry Classification source is UniFormat. See Section 1.3.1.6 Industry Classification Library – UniFormat. Vertical Circulation System Object The Industry Classification source is UniFormat. See Section 1.3.1.6 Industry Classification Library – UniFormat. |

#### Industry Construction Type Library

| Type | Data Object |
| --- | --- |
| Documentation | The industry construction type data library for the Testbed is the BPEA Thread construction type data. The BPEA industry construction type library comes from a variety of sources. The industry construction type library may be accessed from a server over the web or from directly within the BIM-authoring application. |

#### Project Construction Type Library

| Type | Data Object |
| --- | --- |
| Documentation | The project construction type data library is derived for the project from the industry construction type library, and reflects any modifications or additions the designer has made to the industry source data. |

#### Industry Space Type Library

| Type | Data Object |
| --- | --- |
| Documentation | The industry space type data library identifies space function using OmniClass table 13 (space by function). An optional second classification is by form using the OmniClass table 14 (space by form). However, for the Testbed with GSA use the BPEA space type library to align with the BPEA Thread. The industry space type library may be accessed from a server over the web or from directly within the BIM-authoring application. A single space object may have one, two, three, or more space types assigned to it based on the needs of the client. Multiple on-going projects between the GSA, Construction Specification Institute (CSI), the International Code Council (ICC), and others are working to map various naming classifications systems to each other. When this work is complete, consistent and transparent mapping of space names within BIM models will be possible. Spaces may be Interior or Exterior. |

#### Project Space Type Library

| Type | Data Object |
| --- | --- |
| Documentation | The project space type data library is derived for the project from the industry space type library, and reflects any modifications or additions the designer has made to the industry source data. |

#### Industry Classification Library – UniFormat

| Type | Data Object |
| --- | --- |
| Documentation | The Industry Classification for many Object Types is UniFormat. At the early design stage, designers will not model objects in sufficient detail or will not model the object. This only permits use of the higher level UniFormat element titles, which does not allow UniFormat to convey designer intent to the estimator. In a one-to-one mapping of modeled object and Industry Classification, some objects not modeled rely on a corresponding Level 2 UniFormat element title: HVAC System Object – D30 Heating, Ventilating and Air Conditioning, Electrical System Object – D50 Electrical, Vertical Circulation Object – D10 Conveying. The Site Object uses the Level 1 element title, G Building Sitework. Other objects, such as Hot Water System and Cold Water System, use Level 3 titles (D2020 Domestic Water Supply). Modeled objects have similar difficulties. Consider the Beam and Column Objects. Uniformat classifies beams and columns as sub-elements of larger building elements of: B1010 Floor Construction (Level 3) B1010._ Floor Structural Frame (unnumbered Level 4) B1020 Roof Construction B2010._ Roof Structural Frame There are unnumbered sub-headings for each unnumbered Level 4 heading that for Structural Frame suggest possible material types. UniFormat Elements for an Object Type may be in different major element sections of UniFormat. They may not be at the same level in the UniFormat structure. The Wall Object provides an example of both cases: A1010._ Wall Foundations has an unnumbered sub-heading of Foundation Walls A2020 Basement Walls B2010 Exterior Walls C1010 Partitions The ability to use child element titles, a one-to-many relationship, becomes useful as a checklist to convey intent of the designer – especially if accompanied by the ability to include notes as a narrative as well. However, this functionality moves beyond the intent of assigning an Industry Classification to each object. |

#### Industry Classification Library - OmniClass

| Type | Data Object |
| --- | --- |
| Documentation | The Industry Classification for some Object Types is various OmniClass tables. Specific tables referenced include: Table 11 Construction Entities by Function. Table 13 Space by Function. See Section 1.3.1.4 Industry Space Type Library. Table 14 Space by Form. See Section 1.3.1.4 Industry Space Type Library. Table 23 Products. This table include Equipment in section 23-40 00 00 Equipment and Furnishings. As with UniFormat, only higher level titles area useful at early design. Table 33 Disciplines. Specifying and estimating construction and maintenance costs for building elements, identifying workers and estimating associated labor costs needed in the performance of specified procedures, project management and planning. Table 34 Organizational Roles. Specifying and estimating construction and maintenance costs for building elements, identifying workers and estimating associated labor costs needed in the performance of specified procedures, project management and planning. |

### Exchange Requirement Data Objects

#### ER_Arch_Concept_to_QTO_Inputs_(concept)

| Type | Data Object |
| --- | --- |
| Name | ER_Arch_Concept_to_QTO_Inputs_(concept) |
| Documentation | Exchange of complete set of quantity take-off inputs for use in construction cost analysis. For CPD Correlation: NBIMS Section 4. 11 Capability Maturity Dimensions. The table below shows the possible matrix of interaction for the 11 CPD spheres of influence and the 10 project stages for the testbed. OmniClass Table 33 Disciplines provides an industry standard classification for the concept of actors used by CPD. OmniClass Table 34 Organizational Roles provides an industry standard classification for the concept of roles used by CPD. |

|  |  | Capability Maturity Level |
| --- | --- | --- |
|  |  | Customer Sphere | Staffing Sphere | Structure Sphere | Sales Sphere | Development Sphere | Operations Sphere | Finance Sphere | Strategy Sphere | Marketing Sphere | Leadership Sphere | Culture Sphere |
| Project Stage | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| 0 | Portfolio requirements |  |  |  |  |  |  |  |  |  |  |  |
| 1 | Conception of need |  |  |  |  |  |  |  |  |  |  |  |
| 2 | Outline feasibility |  |  |  |  |  |  |  |  |  |  |  |
| 3 | Substantive feasibility |  |  |  |  |  |  |  |  |  |  |  |
| 4 | Outline conceptual design |  |  |  |  |  |  |  |  |  |  |  |
| 5 | Full conceptual design |  |  |  |  |  |  |  |  |  |  |  |
| 6 | Coordinated design and procurement |  |  |  |  |  |  |  |  |  |  |  |
| 7 | Production information |  |  |  |  |  |  |  |  |  |  |  |
| 8 | Construction |  |  |  |  |  |  |  |  |  |  |  |
| 9 | Operation and maintenance |  |  |  |  |  |  |  |  |  |  |  |
| 10 | Disposal |  |  |  |  |  |  |  |  |  |  |  |

## Specification of Decision Point Gateways

### Ready for Quantity/Cost Analysis

| Type | Decision Point |
| --- | --- |
| Documentation | At this point the designer must decide if all the desired design changes have been made and the model is ready for QTO to support cost analysis. If so, the model is ready for simulation. If not, the designer must further modify the building design. |

### Valid Quantity/Cost Analysis BIM?

| Type | Decision Point |
| --- | --- |
| Documentation | After deciding that the model is ready for analysis, the designer uses a model checker to ensure that all the input exchange requirements have been met. This step also takes place when the client evaluates the BIM model submitted to them by the designer. If the BIM model meets the requirements set forth by the rule checking sets in the model checker, the BIM is valid. If not, it is invalid. |

### Results Acceptable?

| Type | Decision Point |
| --- | --- |
| Documentation | The designer evaluates the results of the quantity/cost analysis and compares them to the cost targets for the design. If the design meets the cost targets, as well as any other project performance metrics (such as energy performance), the results are acceptable. If not, the designer must further modify the building design. |

### Perform Client Quantity/Cost Analysis?

| Type | Decision Point |
| --- | --- |
| Documentation | The client may want to perform an independent quantity/cost analysis to validate the results of the designer’s analysis. This independent quantity/cost analysis may be executed by internal staff of the client, or by a consultant. |

### Results Complete per Client Request?

| Type | Decision Point |
| --- | --- |
| Documentation | The internal staff or consultant that is conducting the independent quantity/cost analysis decides of the results of their analysis are accurate and reliable, and conform to the client’s work order. |

### Quantity/Cost Analysis Accepted?

| Type | Decision Point |
| --- | --- |
| Documentation | The designer reviews the design feedback from the client for design approval or rejection. |

# Exchange Requirements for Design to Quantity Take-Off

| Name | Exchange of Design to Quantity Take-Off |
| --- | --- |

| Identifier | ER_Design_to_QTO |
| --- | --- |

| Change Log |
| --- |
| 5-Jan-09 | Initial creation of version 0.01, draft for internal review | Tom Wiggins |
| 4-Feb-09 | Edits creating version 0.02 | Tom Wiggins |
| 11-Feb-09 | Edits creating version 0.03 | Tom Wiggins |
| 18-Feb-09 | Edits for version 0.5 - adding 'ER QTO to Design' to the process diagram, expanding table for 'ER Design to QTO' | Richard See |
| 23-Feb-09 | Edits for version 0.6 -- expanded ER tables significantly | Richard See |
| 23-Mar-09 | Edits for version 1.0 – integrating public comments | Tom Wiggins |

| Project Stage | 0 | Portfolio requirements |  |
| --- | --- | --- | --- |
|  | 1 | Conception of need |  |
|  | 2 | Outline feasibility |  |
|  | 3 | Substantive feasibility |  |
|  | 4 | Outline conceptual design | ( |
|  | 5 | Full conceptual design | ( |
|  | 6 | Coordinated design and procurement |  |
|  | 7 | Production information |  |
|  | 8 | Construction |  |
|  | 9 | Operation and maintenance |  |
|  | 10 | Disposal |  |

## Overview

The scope of this exchange requirement is the exchange of information about building, space, elemental quantities and element descriptions intended for use in preparation of a cost estimate. The purpose of the exchange requirement is to support the coordination of model quantities with the needs of the cost estimator preparing the cost estimate.

The exchange requirement assumes that a building model is available from which relevant geometric information required for a conceptual cost estimate can be derived. It is anticipated that the building model will provide context information about the project including units to be used, coordinate systems to be adopted and the direction of true north.

The building model will provide specific information about:

the building, its location, composition, overall shape and orientation

the shape and location of adjacent buildings

building stories within the building

spatial configuration

The building model will provide conceptual information about:

the building services

the building structure

the site design

Information that is provided by this exchange requirement to enhance the initial set of building model information includes:

space type and function identification with type data being obtained from a project space type library (which is in turn derived from an industry space type library).

building elements construction type data with type data being obtained from a project construction type library (which is in turn derived from a industry construction type library).

## Exchange Requirements - Design to QTO (Concept)

| Type of Information | Information Needed | Required | Optional | Data Type | Units |
| --- | --- | --- | --- | --- | --- |
| Project | The following properties should be included: |  |  |  |  |
|  | Identification | X |  | String | n/a |
|  | Owner/Client information (name, address, phone, email address) |  | X | String | n/a |
|  | Model Author (name, address, phone, email address) |  | X | String | n/a |
| Site | The following properties should be included: |  |  |  |  |
|  | Address (including number, street, city, state, ZIP, and country) |  | X | String | n/a |
|  | Global Coordinates (Longitude & Latitude) | X |  | (2) triples | deg/min/sec |
|  | Site Elevation (datum)(relative to sea level) | X |  | Real | m |
| Building | The following properties should be included (if not known then probable values should be used): |  |  |  |  |
|  | Identification | X |  | String | n/a |
|  | Description |  | X | String | n/a |
|  | Functional Classification (OmniClass Table 11, but IBC for Testbed to match BEPA) |  | X | String | n/a |
|  | Location (relative to Site origin - defined by longitude & Latitude) | X |  | (2) triples | deg/min/sec |
|  | Orientation (deviation of building grid from true north, clockwise) | X | X | Real | Angular Degrees |
|  | Elevation (relative to the site datum) | X |  | Real | m |
|  | Building Height | X |  | Real | m |
| Building Story | The following properties should be included (if not known then probable values should be used): |  |  |  |  |
|  | Identification | X |  | String | n/a |
|  | Description |  | X | String | n/a |
|  | Elevation (relative to building datum) | X |  | Real | m |
|  | Building Story Height | X |  | Real | m |
|  | Building Story Perimeter | X |  | Real | m |
|  | Building Story Gross Area | X |  | Real | m |
| Space | The following properties should be included (if not known then probable values should be used): |  |  |  |  |
|  | Identification | X |  | String | n/a |
|  | Description |  | X | String | n/a |
|  | Functional Classification – OmniClass Table 13 |  | X | Relationship | n/a |
|  | Functional Classification – Client Space Type | X |  | Relationship | n/a |
|  | Form Classification – OmniClass Table 14 |  | X | Relationship | n/a |
|  | Inside or Outside space | X |  | Boolean |  |
|  | Space Height | X |  | Real | m |
|  | Space Gross Perimeter | X |  | Real | m |
|  | Space Net Perimeter |  | X | Real | m |
|  | Space Finished Ceiling Height |  | X | Real | m |
|  | Space Finished Floor Height |  | X | Real | m |
|  | Space Gross Floor Area | X |  | Real | m2 |
|  | Space Net Floor Area | X |  | Real | m2 |
|  | Space Net Volume |  | X | Real | m3 |
| Beam | The following properties should be included: |  |  |  |  |
|  | Identification |  | X | String | n/a |
|  | Construction type (i.e. beam type) | X |  | String | n/a |
|  | Classification - UniFormat |  | X | String | n/a |
|  | Exterior or Interior Element (i.e. Is Exterior) | X |  | Boolean | n/a |
|  | Beam Length | X |  | Real | m |
|  | Beam Height | X |  | Real | m |
|  | Beam Width | X |  | Real | m |
|  | Beam Net Surface Area - extruded sides | X |  | Real | m2 |
|  | Beam Gross Volume |  | X | Real | m3 |
|  | Beam Net Volume | X |  | Real | m3 |
| Column | The following properties should be included: |  |  |  |  |
|  | Identification |  | X | String | n/a |
|  | Construction type (i.e. column type) | X |  | String | n/a |
|  | Classification - UniFormat |  | X | String | n/a |
|  | Exterior or Interior Element (i.e. Is Exterior) | X |  | Boolean | n/a |
|  | Column Length | X |  | Real | m |
|  | Column Height | X |  | Real | m |
|  | Column Width | X |  | Real | m |
|  | Column Net Surface Area - extruded sides | X |  | Real | m2 |
|  | Column Gross Volume |  | X | Real | m3 |
|  | Column Net Volume | X |  | Real | m3 |
| Curtain Wall | The following properties should be included: |  |  |  |  |
|  | Identification |  | X | String | n/a |
|  | Construction type (i.e. curtain wall type) | X |  | String | n/a |
|  | Classification - UniFormat |  | X | String | n/a |
|  | Exterior or Interior Element (i.e. Is Exterior) | X |  | Boolean | n/a |
|  | Fire Rating |  | X | String | n/a |
|  | Curtain Wall Width |  | X | Real | m |
|  | Curtain Wall Height |  | X | Real | m |
|  | Curtain Wall Count - Outside Corners | X |  | Count | n/a |
|  | Curtain Wall Count - Inside Corners | X |  | Count | n/a |
|  | Curtain Wall Frame Depth | X |  | Real | m |
|  | Curtain Wall Frame Thickness | X |  | Real | m |
|  | Curtain Wall Gross Area | X |  | Real | m2 |
| Door | The following properties should be included: |  |  |  |  |
|  | Identification |  | X | String | n/a |
|  | Construction type (i.e. door type) | X |  | String | n/a |
|  | Classification - UniFormat |  | X | String | n/a |
|  | Exterior or Interior Element (i.e. Is Exterior) | X |  | Boolean | n/a |
|  | Fire Rating |  | X | String | n/a |
|  | Door Width | X |  | Real | m |
|  | Door Height | X |  | Real | m |
|  | Door Frame Depth |  | X | Real | m |
|  | Door Frame Thickness |  | X | Real | m |
|  | Door Leaf Thickness |  | X | Real | m |
|  | Door Perimeter |  | X | Real | m |
|  | Door Gross Area | X |  | Real | m2 |
| Equipment | The following properties should be included: |  |  |  |  |
|  | Identification |  | X | String | n/a |
|  | Construction type (i.e. equipment type) | X |  | String | n/a |
|  | Classification - UniFormat |  | X | String | n/a |
| Opening | The following properties should be included: |  |  |  |  |
|  | Identification |  | X | String | n/a |
|  | Opening Width | X |  | Real | m |
|  | Opening Height | X |  | Real | m |
|  | Opening Depth |  | X | Real | m |
|  | Opening Gross Area |  | X | Real | m2 |
|  | Opening Gross Area |  | X | Real | m3 |
| Plumbing Fixture | The following properties should be included: |  |  |  |  |
|  | Identification |  | X | String | n/a |
|  | Construction type (i.e. plumbing fixture type) | X |  | String | n/a |
|  | Classification - UniFormat |  | X | String | n/a |
| Ramp Flight | The following properties should be included: |  |  |  |  |
|  | Identification |  | X | String | n/a |
|  | Construction type (i.e. ramp flight type) | X |  | String | n/a |
|  | Classification - UniFormat |  | X | String | n/a |
|  | Ramp Flight Length | X |  | Real | m |
|  | Ramp Flight Width | X |  | Real | m |
|  | Ramp Flight Rise | X |  | Real | m |
|  | Ramp Flight Gross Area - Tread Faces | X |  | Real | m2 |
|  | Ramp Flight Gross Area - Riser Faces |  | X | Real | m2 |
| Slab (Floor, Roof, Landing) | The following properties should be included: |  |  |  |  |
|  | Identification |  | X | String | n/a |
|  | Construction type (i.e. slab type) | X |  | String | n/a |
|  | Classification - UniFormat |  | X | String | n/a |
|  | Slab Thickness | X |  | Real | m |
|  | Slab Perimeter | X |  | Real | m |
|  | Slab Gross Area | X |  | Real | m2 |
|  | Slab Net Area | X |  | Real | m2 |
|  | Slab Gross Volume | X |  | Real | m3 |
|  | Slab Net Volume | X |  | Real | m3 |
| Stair Flight | The following properties should be included: |  |  |  |  |
|  | Identification |  | X | String | n/a |
|  | Construction type (i.e. stair flight type) | X |  | String | n/a |
|  | Classification - UniFormat |  | X | String | n/a |
|  | Stair Flight Length | X |  | Real | m |
|  | Stair Flight Width | X |  | Real | m |
|  | Stair Flight Rise | X |  | Real | m |
|  | Stair Flight Gross Area - Tread Faces | X |  | Real | m2 |
|  | Stair Flight Gross Area - Riser Faces |  | X | Real | m2 |
| Wall | The following properties should be included: |  |  |  |  |
|  | Identification |  | X | String | n/a |
|  | Construction type (i.e. wall type) | X |  | String | n/a |
|  | Classification - UniFormat |  | X | String | n/a |
|  | Exterior or Interior Element (i.e. Is Exterior) | X |  | Boolean | n/a |
|  | Fire Rating |  | X | String | n/a |
|  | 3D Geometry | X |  | IFC Geometry | varies |
|  | Wall Length | X |  | Real | m |
|  | Wall Height | X |  | Real | m |
|  | Wall Thickness | X |  | Real | m |
|  | Wall Gross Side Area | X |  | Real | m2 |
|  | Wall Net Side Area | X |  | Real | m2 |
|  | Wall Gross Volume | X |  | Real | m3 |
|  | Wall Net Volume | X |  | Real | m3 |
| Window | The following properties should be included: |  |  |  |  |
|  | Identification |  | X | String | n/a |
|  | Construction type (i.e. window type) | X |  | String | n/a |
|  | Classification - UniFormat |  | X | String | n/a |
|  | Exterior or Interior Element (i.e. Is Exterior) | X |  | Boolean | n/a |
|  | Fire Rating |  | X | String | n/a |
|  | 3D Geometry | X |  | IFC Geometry | varies |
|  | Door Width | X |  | Real | m |
|  | Door Height | X |  | Real | m |
|  | Door Frame Depth |  | X | Real | m |
|  | Door Frame Thickness |  | X | Real | m |
|  | Door Leaf Thickness |  | X | Real | m |
|  | Door Perimeter |  | X | Real | m |
|  | Door Gross Area | X |  | Real | m2 |
| HVAC System | The following properties should be included: |  |  |  |  |
|  | Identification |  | X | String | n/a |
|  | Description |  | X | String | n/a |
|  | Classification - UniFormat (reference to a classification = system type) |  | X | String | n/a |
| Electrical System | The following properties should be included: |  |  |  |  |
|  | Identification |  | X | String | n/a |
|  | Description |  | X | String | n/a |
|  | Classification - UniFormat (reference to a classification = system type) |  | X | String | n/a |
| Hot Water System | The following properties should be included: |  |  |  |  |
|  | Identification |  | X | String | n/a |
|  | Description |  | X | String | n/a |
|  | Classification - UniFormat (reference to a classification = system type) |  | X | String | n/a |
| Cold Water System | The following properties should be included: |  |  |  |  |
|  | Identification |  | X | String | n/a |
|  | Description |  | X | String | n/a |
|  | Classification - UniFormat (reference to a classification = system type) |  | X | String | n/a |
| Vertical Circulation System | The following properties should be included: |  |  |  |  |
|  | Identification |  | X | String | n/a |
|  | Description |  | X | String | n/a |
|  | Classification - UniFormat (reference to a classification = system type) |  | X | String | n/a |

# Exchange Requirements for Quantity Take-Off Results to Design

| Name | Exchange of Quantity Take-Off Results to Design |
| --- | --- |

| Identifier | ER_QTO_to_Design |
| --- | --- |

| Change Log |
| --- |
| 5-Jan-09 | Initial creation of version 0.01, draft for internal review | Tom Wiggins |
| 4-Feb-09 | Edits creating version 0.02 | Tom Wiggins |
| 11-Feb-09 | Edits creating version 0.03 | Tom Wiggins |
| 12-FEB-2009 | Adding CPD elements for mapping communications (social networking analysis) model interactions across processes [associative link analysis both internal to QTO decisions and cross-disciplinary adding interaction effects with BPEA] | Phillip Cousins |
| 18-Feb-09 | Edits for version 0.5 - adding 'ER QTO to Design' to the process diagram, expanding table for 'ER Design to QTO' | Richard See |
| 20 FEB 2009 | Edits for version 0.6 to extract and map CPD elements from QTO IDM | Phillip Cousins Diane Downs |
| 23-Mar-09 | Edits for version 1.0 – integrating public comments | Tom Wiggins |

| Project Stage | 0 | Portfolio requirements |  |
| --- | --- | --- | --- |
|  | 1 | Conception of need |  |
|  | 2 | Outline feasibility |  |
|  | 3 | Substantive feasibility |  |
|  | 4 | Outline conceptual design | ( |
|  | 5 | Full conceptual design | ( |
|  | 6 | Coordinated design and procurement |  |
|  | 7 | Production information |  |
|  | 8 | Construction |  |
|  | 9 | Operation and maintenance |  |
|  | 10 | Disposal |  |

## Overview

The scope of this exchange requirement is the exchange of information about quantity and/or cost reports.  The purpose of the exchange requirement is to enable coordination of quantity information with other design roles and to make these reports available to other applications (particularly the design application).  The coordination of roles is based on the application of the NBIMS BIM Capability Maturity Model to candidate standard Enterprise Stakeholder Activity Model developed in prototype form for this testbed.  The exchange requirement assumes that the information provisions outlined in the exchange requirement ER Design to QTO Inputs (concept) have been satisfied. The Enterprise Model will map the changes, gain input from user groups, and return a result to the process.

Information that is provided by this exchange requirement to includes:

Links to reports generated by the QTO/Estimating application

## Exchange Requirements - QTO to Design

| Type of Information | Information Needed | Required | Optional | Data Type | Units |
| --- | --- | --- | --- | --- | --- |
| Project | The following properties should be included: |  |  |  |  |
|  | Identification | X |  | String | n/a |
|  | Owner/Client information (name, address, phone, email address) |  | X | String | n/a |
|  | Model Author (name, address, phone, email address) |  | X | String | n/a |
|  | URL for quantity report |  | X | URL | n/a |
|  | URL for cost estimate report |  | X | URL | n/a |
|  | URL for cost comparison report |  | X | URL | n/a |

# Comments

Field is meant only for project identifier. Field a text or a number.

This is only one string.  Do we need more?  Normally I would map this to IfcPerson&Organization --- which gives you much more information

Let’s leave it flexible.

Same comment/question as for Owner/Client

Let’s leave it flexible.

This is numerical or text field.

Building orientation is typically considered to be the degrees of grid rotation from true north. Building orientation specification, therefore, is somewhat arbitrary for the building could have been modeled in any particular orientation on the original grid.  Determining the direction of the surface normals is the critical component.

Base elevation of ground level floor above sea level.

This is numerical or text field.

This must include both Space Number and Space Name

Space name or number…1,2, mezzanine, etc.

Optional text description.

Space classification is specific to the client/profile.  They may or may not have spatial naming conventions to follow.  Example: GSA Star Space Type. Will be required for the GSA.

Richard, we want to allow for multiple classifications here.  Once mappings are complete between IBC, IEEC, Omniclass, GSA Star Space Type, etc. we may want to include several of these.  Do we need to create a separate line item (classification 1, classification 2, etc.)?