Versions: 00

Network Working Group                                        D. Stanley

Internet Draft                                           Aruba Networks

Intended status: Proposed Standard                            S. McCann

Expires: April 19, 2010                              Research in Motion

Gabor Bajko

Nokia

Allan Thomson

Cisco Systems

October 19, 2009

# Interior Location Extensions

# draft-stanley-geopriv-int-ext-00.txt

Status of this Memo

This Internet-Draft is submitted to IETF in full conformance with the

provisions of BCP 78 and BCP 79.

Internet-Drafts are working documents of the Internet Engineering

Task Force (IETF), its areas, and its working groups.  Note that

other groups may also distribute working documents as Internet-

Drafts.

Internet-Drafts are draft documents valid for a maximum of six months

and may be updated, replaced, or obsoleted by other documents at any

time.  It is inappropriate to use Internet-Drafts as reference

material or to cite them other than as "work in progress."

The list of current Internet-Drafts can be accessed at

http://www.ietf.org/ietf/1id-abstracts.txt

The list of Internet-Draft Shadow Directories can be accessed at

http://www.ietf.org/shadow.html

This Internet-Draft will expire on April 19, 2010.

Copyright Notice

Copyright (c) 2009 IETF Trust and the persons identified as the

document authors. All rights reserved.

This document is subject to BCP 78 and the IETF Trust's Legal

Provisions Relating to IETF Documents in effect on the date of

publication of this document (http://trustee.ietf.org/license-info).

Please review these documents carefully, as they describe your rights

and restrictions with respect to this document.

Stanley, et al.         Expires April 19, 2010                 [Page 1]

Internet-Draft         INT Location Extensions             October 2009

Abstract

This document extends the definition of Interior Location defined in

draft-rosen-geopriv-pidf-interior to include a set of registered

elements that allow for the expression of relative location.  The

expression of relative location enables LAN technologies that have such

capability to provide a more accurate location description than normally

allowed using [RFC4776] [RFC5139].  By registering the elements

described here, interoperability between applications and vendors is

enabled.

Table of Contents

1. Introduction.......................................................2

1.1. Requirements Notation..........................................3

1.2. Motivation for Interior Location...............................3

2. INT Elements.......................................................4

2.1. Measurement Uncertainty........................................4

2.2. Reference Location.............................................4

3. Shapes.............................................................5

3.1. Point........................................................5

3.2. Circle.......................................................6

3.3 Arcband.......................................................7

3.4. Polygon......................................................9

4. Security Considerations...........................................11

5. IANA Considerations...............................................11

5.1. INT Name Registry.............................................11

6. References........................................................12

6.1. Normative References..........................................12

7. Acknowledgments...................................................12

Authors' Addresses...................................................12

## 1. Introduction

This extension to the definition of interior locations is a set of

registered elements that provide a common method to express

additional location information in the form of a relative location

from a reference location.

Stanley, et al.         Expires April 19, 2010                 [Page 2]

Internet-Draft         INT Location Extensions             October 2009

The relative location information could be produced by LAN

technologies and used in environments such as large campus networks,

large public buildings, hot spots, etc.

Using geodetic coordinates to describe the location of an entity has

limitations that restrict its usability, especially in indoor

environments. In these cases, describing the determined location of

the entity using civic and relative addressing may be both more

feasible and easier for human consumption than using geodetic

coordinates.

### 1.1. Requirements Notation

The key words "MUST", "MUST NOT", "REQUIRED", "SHALL", "SHALL NOT",

"SHOULD", "SHOULD NOT", "RECOMMENDED", "MAY", and "OPTIONAL" in this

document are to be interpreted as described in RFC-2119.

### 1.2. Motivation for Interior Location

Current civic addressing [RFC4776],[RFC5139] is neither granular nor

accurate enough to be able to describe an arbitrary indoor position

of a network device with precision. This document proposes to extend

civic addressing with a reference point, an offset and relative

location from these points using shapes in the Cartesian coordinate

system to describe the position of a network device. The data

included within the relative position parameters is supplementary to,

not exclusive of the existing civic location data expressed in PIDF-

LO [RFC4119] and the DHCP Civic Location option [RFC4776] [RFC5139].

An example of this may be a 4-story campus building belonging to a

company that has wireless LAN technology deployed throughout the

building. The building has complete RF coverage and the wireless

network architecture for the building can locate network devices

within that building to within a few meters using RF measurements or

other technologies. The supplementary data provided by relative

location would enable a more granular location expression for a

located device. In addition to "34 Some Street, Anytown, PA, USA,

Building 10, Floor 4", a relative position "within X meters of the

point which is 10 meters south and 15 meters east of the main

elevator on Floor 4" is possible.

Another example of this may be a popular wireless hotspot located at

234 N. Main St., Anytown, PA. USA.  It is reasonable to expect that

Stanley, et al.         Expires April 19, 2010                 [Page 3]

Internet-Draft         INT Location Extensions             October 2009

234 N. Main St. covers a geographic area that encompasses several

hundred square meters.  The wireless network architecture for this

hotspot could include several wireless infrastructure access points.

The supplementary data provided via relative location would enable a

more granular location expression.  In addition to providing 234 N.

Main St., Anytown, PA. USA, a relative position like "within X meters

from the main entrance" could be added.

## 2. INT Elements

Included in the interior relative location architecture below is a

set of INT elements and corresponding attributes that are registered

with the namespace to enable interoperability between various vendors

and devices.  Included are 4 shapes: point, circle, arcband, and

polygon.  Mixing the use of these registered INT elements with any

quantity of local, or private, INT elements is allowed. Please note

that all INT elements are supplementary to Civic location elements in

PIDF-LO.  The order in which these new elements appear in PIDF-LO is

significant based on the text for each shape below.

### 2.1. Measurement Uncertainty

When calculating a network device's location using the technology

described above, there is an area of uncertainty associated with the

measurement techniques.  The method of expressing a calculated

position and separately expressing the area of uncertainty has been

debated as to its usefulness.  Hence, there is no facility included

here to allow the expression of an area of uncertainty separate from

the shape.  It is expected that the expressed shape will include the

area of uncertainty, to yield a result that the device is contained

within the shape to a 95% confidence level.

### 2.2. Reference Location

Measurement from the reference is provided by using the labels of X,

Y and Z.  The east-west dimension is labeled X and north-south

dimension is labeled Y.  A positive Y value is considered north of

the reference, a negative Y value south of the reference, a positive

X value for east of the reference and a negative X value indicates

west of the reference. The height value, Z, is optional.  A positive

Z value would indicate the height above the floor level at the

reference whereas a negative Z value would indicate a height below

the reference.  The absence of a Z value indicates the shape is at

the floor level of the reference or unknown.  All position values are

in meters.

Stanley, et al.         Expires April 19, 2010                 [Page 4]

Internet-Draft         INT Location Extensions             October 2009

## 3. Shapes

The different shapes are described by first declaring a mandatory

reference element, which is the starting location for the offset

positions.  Next is a mandatory declaration of the shape type, which

includes point, circle, arcband, or polygon.  Following the shape

declaration element are the shape specific offset measurement

elements as outlined below.

### 3.1. Point

The point shape includes the reference, the shape type, and offset

measurement values for X, Y, and optionally Z. See Figure 1.

<INT N='Reference'>Front Door</INT>

<INT N='Point'/>

<INT N='SHAPE-OFFSET-X'>+25</INT>

<INT N='SHAPE-OFFSET-Y'>+10</INT>

<INT N='SHAPE-OFFSET-Z'>+10</INT>  (optional)

+--------------------------------------x

|              SHAPE-OFFSET-X

|

|

|

| SHAPE-OFFSET-Y

|

|

REF

Figure 1 - Point Shape

#### 3.1.1 Point Example

An example of a point shape included in the whole of the civic

location elements would be:

<country>US</country>

<A1>Florida</A1>

<A3>Miami</A3>

<HNO>8200</HNO>

<PRD>NW</PRD>

<RD>41st</RD>

<STS>Street</STS>

<PC>33166</PC>

<FLR>4</FLR>

<INT N='Suite'>400</INT>

Stanley, et al.         Expires April 19, 2010                 [Page 5]

Internet-Draft         INT Location Extensions             October 2009

<INT N='Reference'>Front Door</INT>

<INT N='Point'/>

<INT N='SHAPE-OFFSET-X'>+25</INT>

<INT N='SHAPE-OFFSET-Y'>+10</INT>

<INT N='SHAPE-OFFSET-Z'>+10</INT>

### 3.2. Circle

The circle shape includes the reference, shape type, offset

measurement values for the X, Y, and optionally Z of the center point

of the circle, and a radius value. See Figure 2.

<INT N='Reference'>Front Door</INT>

<INT N='Circle'/>

<INT N='SHAPE-OFFSET-X'>+34</INT>

<INT N='SHAPE-OFFSET-Y'>-9</INT>

<INT N='SHAPE-OFFSET-Z'>+5</INT>  (optional)

<INT N='Radius'>4</INT>

REF

|

|

|

|

| SHAPE-OFFSET-Y                     _,...._

|                                 ,-'       `-.

|                               ,'          --,`. RADIUS

|                              /            ,'|  \

|                             .'           /     '.

|                             |          ,'       |

+-----------------------------+---------x         |

SHAPE-OFFSET-X     \                   /

\                 /

`.             ,'

`.         ,'

`--...--'

Figure 2 - Circle Shape

#### 3.2.2. Circle Example

An example of a circle shape included in the whole of the civic

location elements would be:

Stanley, et al.         Expires April 19, 2010                 [Page 6]

Internet-Draft         INT Location Extensions             October 2009

<country>US</country>

<A1>Florida</A1>

<A3>Miami</A3>

<HNO>8200</HNO>

<PRD>NW</PRD>              st        <RD>41 </RD>

<STS>Street</STS>

<PC>33166</PC>

<FLR>4</FLR>

<INT N='Suite'>400</INT>

<INT N='Reference'>Front Door</INT>

<INT N='Circle'/>

<INT N='SHAPE-OFFSET-X'>+34</INT>

<INT N='SHAPE-OFFSET-Y'>-9</INT>

<INT N='SHAPE-OFFSET-Z'>+5</INT>

<INT N='Radius'>4</INT>

### 3.3 Arcband

The arcband shape includes the reference, shape type, offset

measurement value of the central point, the optional Z value, the

inner and outer radius values, the start angle, and the opening

angle. See Figure 3.

<INT N='Reference'>Front Door</INT>

<INT N='Arcband'/>

<INT N='SHAPE-OFFSET-X'>+17</INT>

<INT N='SHAPE-OFFSET-Y'>-2</INT>

<INT N='SHAPE-OFFSET-Z'>+2</INT> (optional)

<INT N='InnerRadius'>8</INT>

<INT N='OuterRadius'>18</INT>

<INT N='StartAngle'>329</INT>

<INT N='Opening'>82</INT>

Stanley, et al.         Expires April 19, 2010                 [Page 7]

Internet-Draft         INT Location Extensions             October 2009

_,,..,--------....__

''                    `--..

\                         ``-.

REF                       \                            `-._

|                         \                                `.

|                          \                                 ;>

|                           \                              ,'

|                           \    __......__              ,'

|                            .-''          `--._       ,'

|                             \                 `.    / OuterRadius

|                             `.                  `.,'

|  SHAPE-OFFSET-Y              |    Opening       ,'

|                               |    Angle      ,'

|                               `.             /

|                                |           ,'

|                                 |        ,'

|                         Start   `.     ,'  InnerRadius

|                         Angle    |    /

|                                   | ,'

+------------------------------------x

SHAPE-OFFSET-X

Figure 3 - Arcband Shape

#### 3.3.1 Arcband Example

An example of an arcband shape included in the whole of the civic

location elements would be:

<country>US</country>

<A1>Florida</A1>

<A3>Miami</A3>

<HNO>8200</HNO>

<PRD>NW</PRD>

<RD>41st</RD>

<STS>Street</STS>

<PC>33166</PC>

<FLR>4</FLR>

<INT N='Suite'>400</INT>

<INT N='Reference'>Front Door</INT>

<INT N='Arcband'/>

Stanley, et al.         Expires April 19, 2010                 [Page 8]

Internet-Draft         INT Location Extensions             October 2009

<INT N='SHAPE-OFFSET-X'>+17</INT>

<INT N='SHAPE-OFFSET-Y'>-2</INT>

<INT N='SHAPE-OFFSET-Z'>+2</INT>

<INT N='InnerRadius'>8</INT>

<INT N='OuterRadius'>18</INT>

<INT N='StartAngle'>329</INT>

<INT N='Opening'>82</INT>

### 3.4. Polygon

The polygon shape includes the reference, the shape type, the number

of polygon points, the offset measurement value for each point,

optionally a calculated geo center point of the polygon, and the

optional Z value. This example shows a single Z value for the entire

shape. See Figure 4.

<INT N='Reference'>Front Door</INT>

<INT N='Polygon'/>

<INT N='PolygonPoints'>5</INT>

<INT N='SHAPE-OFFSET-X'>-18</INT> <!-A-X-->

<INT N='SHAPE-OFFSET-Y'>-8</INT> <!-A-Y-->

<INT N='SHAPE-OFFSET-X'>-20</INT> <!-B-X-->

<INT N='SHAPE-OFFSET-Y'>-5</INT> <!-B-Y-->

<INT N='SHAPE-OFFSET-X'>-25</INT> <!-C-X-->

<INT N='SHAPE-OFFSET-Y'>-6</INT> <!-C-Y-->

<INT N='SHAPE-OFFSET-X'>-25</INT> <!-D-X-->

<INT N='SHAPE-OFFSET-Y'>-10</INT> <!-D-Y-->

<INT N='SHAPE-OFFSET-X'>-20</INT> <!-E-X-->

<INT N='SHAPE-OFFSET-Y'>-13</INT> <!-E-Y-->

<INT N='SHAPE-OFFSET-X'>-18</INT> <!-A-X-->

<INT N='SHAPE-OFFSET-Y'>-8</INT> <!-A-Y-->

<INT N='SHAPE-GEOCENTER-X'>-10</INT> <!-Center-X--> (optional)

<INT N='SHAPE-GEOCENTER-Y'>-20</INT> <!-Center-Y--> (optional)

<INT N='SHAPE-OFFSET-Z'>+10</INT>  (optional)

Stanley, et al.         Expires April 19, 2010                 [Page 9]

Internet-Draft         INT Location Extensions             October 2009

REF

|

|

|

|

| SHAPE-

| OFFSET-Y(A)

|

|

|

SHAPE-OFFSET-X(A)  |

_,.-------------------------------------+ SHAPE-

_,,-'    `.                                  | OFFSET-Y(B)

_,.-''           \              SHAPE-OFFSET-X(B)  |

'------------------\--------------------------------+

|                   \                               | SHAPE-

|                     `.                             | OFFSET-Y(C)

|                       \                            |

|                        \        SHAPE-OFFSET-X(C)  |

|                          ;--------------------------+ SHAPE-

|                       ,-'                           | OFFSET-Y(D)

|                     ,'           SHAPE-OFFSET-X(D)  |

':----------------;----------------------------------+

`-.           ,'                                   | SHAPE-

`.      ,-'                                     | OFFSET-Y(E)

`-. ,'                     SHAPE-OFFSET-X(E)  |

'------------------------------------------+

Figure 4 - Polygon Shape

#### 3.4.1 Polygon Example

An example of a polygon shape included in the whole of the civic

location elements would be:

<country>US</country>

<A1>Florida</A1>

<A3>Miami</A3>

<HNO>8200</HNO>

<PRD>NW</PRD>

<RD>41st</RD>

<STS>Street</STS>

<PC>33166</PC>

Stanley, et al.         Expires April 19, 2010                [Page 10]

Internet-Draft         INT Location Extensions             October 2009

<FLR>4</FLR>

<INT N='Suite'>400</INT>

<INT N='Reference'>Front Door</INT>

<INT N='Polygon'/>

<INT N='PolygonPoints'>5</INT>

<INT N='SHAPE-OFFSET-X'>-18</INT> <!-A-X-->

<INT N='SHAPE-OFFSET-Y'>-8</INT> <!-A-Y-->

<INT N='SHAPE-OFFSET-X'>-20</INT> <!-B-X-->

<INT N='SHAPE-OFFSET-Y'>-5</INT> <!-B-Y-->

<INT N='SHAPE-OFFSET-X'>-25</INT> <!-C-X-->

<INT N='SHAPE-OFFSET-Y'>-6</INT> <!-C-Y-->

<INT N='SHAPE-OFFSET-X'>-25</INT> <!-D-X-->

<INT N='SHAPE-OFFSET-Y'>-10</INT> <!-D-Y-->

<INT N='SHAPE-OFFSET-X'>-20</INT> <!-E-X-->

<INT N='SHAPE-OFFSET-Y'>-13</INT> <!-E-Y-->

<INT N='SHAPE-OFFSET-X'>-18</INT> <!-A-X-->

<INT N='SHAPE-OFFSET-Y'>-8</INT> <!-A-Y-->

<INT N='SHAPE-GEOCENTER-X'>-10</INT> <!-Center-X-->

<INT N='SHAPE-GEOCENTER-Y'>-20</INT> <!-Center-Y-->

## 4. Security Considerations

The XML representation described in this document is designed for

inclusion in a PIDF-LO document.  As such, it is subject to the same

security considerations as are described in [RFC4119]. Considerations

relating to the inclusion of this representation in other XML documents

are outside the scope of this document.

## 5. IANA Considerations

### 5.1. INT Name Registry

This document adds new values to the registry managed by IANA called

"INT Names". The new values are listed below:

Reference

Point

Circle

Arcband

Polygon

SHAPE-OFFSET-X

SHAPE-OFFSET-Y

SHAPE-OFFSET-Z

Radius

InnerRadius

Stanley, et al.         Expires April 19, 2010                [Page 11]

Internet-Draft         INT Location Extensions             October 2009

OuterRadius

StartAngle

Opening

PolygonPoints

SHAPE-GEOCENTER-X

SHAPE-GEOCENTER-Y

SHAPE-OFFSET-Z

## 6. References

### 6.1. Normative References

[RFC2119]  Bradner, S., "Key words for use in RFCs to Indicate

Requirement Levels", BCP 14, RFC 2119, March 1997.

[RFC4119]  Peterson, J., "A Presence-based GEOPRIV Location Object

Format", RFC 4119, December 2005.

[RFC5139]  Thomson, M. and J. Winterbottom, "Revised Civic Location

Format for Presence Information Data Format Location

Object (PIDF-LO)", RFC 5139, February 2008.

[RFC4776]  H. Schulzrinne, "DHCPv4 and DHCPv6 Option for Civic

Addresses Configuration Information", RFC4776, November

2006.

## 7. Acknowledgments

The authors would like to acknowledge James Polk and Marc Linsner for

their contributions to this document.

This document was prepared using 2-Word-v2.0.template.dot and "JavE"

from http://www.jave.de without whom those radii would not have been.

Authors' Addresses

Dorothy Stanley

Aruba Networks

1322 Crossman Ave

Sunnyvale, CA 94089 USA

Stanley, et al.         Expires April 19, 2010                [Page 12]

Internet-Draft         INT Location Extensions             October 2009

+1 630-363-1389

Email: dstanley@arubanetworks.com

Stephen McCann

Research in Motion

200 Bath Road

Slough

Berkshire, SL1 3XE, UK

+44 1753 667099

Email: smccann@rim.com

Gabor Bajko

Nokia

323 Fairchild Drive

Mountain View, CA, 94043 USA

Email: gabor.bajko@nokia.com

Allan Thomson

Cisco Systems, Inc.

170 West Tasman Drive

San Jose, California, 95134 USA

Email: althomso@cisco.com

Stanley, et al.         Expires April 19, 2010                [Page 13]

Html markup produced by rfcmarkup 1.85a, available from http://tools.ietf.org/tools/rfcmarkup/