Open Geospatial Consortium

Date:   2011-07-02

Reference number of this OGC® project document:    OGC 11-052r3

Version: 1.0

Category: OGC® Implementation Standard

Editors:   Matthew Perry and John Herring

OGC GeoSPARQL - A Geographic Query Language for RDF Data

Copyright notice

Copyright © 2011 Open Geospatial Consortium, Inc. All Rights Reserved.
To obtain additional rights of use, visit http://www.opengeospatial.org/legal/.

Warning

This document is not an OGC Standard. It is distributed for review and comment. It is subject to change without notice and may not be referred to as an OGC Standard.

Document type:   		OGC® Candidate Standard

Document subtype:   	Encoding

Document stage:   	Draft

Document language: 	English

Recipients of this document are invited to submit, with their comments, notification of any relevant patent rights of which they are aware and to provide supporting documentation.

Contents

i.	Preface	ix

ii.	Submitting organizations	ix

iii.	Submission contact points	ix

iv.	Revision history	x

v.	Changes to the OGC® Abstract Specification	xi

Foreword	xii

Introduction	xiii

1	Scope	1

2	Conformance	1

3	Normative references	3

4	Terms and definitions	4

5	Conventions	4

5.1	Symbols (and abbreviated terms)	4

5.2	XML Namespaces	5

5.3	Placeholder URIs	5

6	Core	5

6.1	SPARQL Protocol	6

6.2	Classes	6

6.2.1	Class: geo:SpatialObject	6

6.2.2	Class: geo:Feature	6

7	Topology Vocabulary Extension (relation_family)	7

7.1	Parameters	7

7.2	Requirements for Simple Features Relation Family	7

7.3	Requirements for Egenhofer Relation Family	8

7.4	Requirements for RCC8 Relation Family	9

7.5	Equivalent RCC8, Egenhofer and Simple Features Topological Relations	10

8	Geometry Extension (serialization, version)	11

8.1	Parameters	11

8.2	Geometry Classes and Properties	11

8.2.1	Class: geo:Geometry	11

8.3	Standard Properties for geo:Feature	12

8.4	Standard Properties for geo:Geometry	13

8.4.1	Property: geo:dimension	14

8.4.2	Property: geo:coordinateDimension	14

8.4.3	Property: geo:spatialDimension	15

8.4.4	Property: geo:isEmpty	15

8.4.5	Property: geo:isSimple	15

8.4.6	Property: geo:is3D	16

8.5	Requirements for WKT Serialization	16

8.5.1	Geometry Class Hierarchy	16

8.5.2	RDFS Datatypes	17

8.5.3	Serialization Properties	18

8.6	Requirements for GML Serialization	19

8.6.1	Geometry Class Hierarchy	19

8.6.2	RDFS Datatypes	20

8.6.3	Serialization Properties	21

8.7	Non-topological Query Functions	21

8.7.1	Function: geof:distance	22

8.7.2	Function: geof:buffer	22

8.7.3	Function: geof:convexHull	23

8.7.4	Function: geof:intersection	23

8.7.5	Function: geof:union	23

8.7.6	Function: geof:difference	23

8.7.7	Function: geof:symDifference	23

8.7.8	Function: geof:envelope	23

8.7.9	Function: geof:boundary	24

9	Geometry Topology Extension (relation_family, serialization, version)	24

9.1	Parameters	24

9.2	Common Query Functions	24

9.3	Requirements for Simple Features Relation Family	25

9.4	Requirements for Egenhofer Relation Family	26

9.5	Requirements for RCC8 Relation Family	27

10	Query Rewrite Extension (relation_family, serialization, version)	28

10.1	Requirements for Simple Features Relation Family	29

10.2	Requirements for Egenhofer Relation Family	30

10.3	Requirements for RCC8 Relation Family	30

11	Future Work	31

Annex A (normative)  Abstract Test Suite	32

Annex B (informative)  Equivalent URIs in GeoSPARQL	46

Annex C (informative)  GeoSPARQL Examples	48

Bibliography	55

Table of Requirements

Req 1	Implementations shall support the SPARQL Protocol for RDF [W3C SPARQL PROTOCOL] and the SPARQL Query Results XML Format [W3C SPARQL RESULT FORMAT].	6

Req 2	Implementations shall support transitivity of rdfs:subClassOf so that all feature and geometry objects subtype from the root class geo:SpatialObject.	6

Req 3	Implementations shall support transitivity of rdfs:subClassOf so that all feature objects subtype from the class geo:Feature.	7

Req 4	Implementations shall allow the properties geo:sf-equals, geo:sf-disjoint, geo:sf-intersects, geo:sf-touches, geo:sf-crosses, geo:sf-within, geo:sf-contains, geo:sf-overlaps to be used directly in SPARQL triple patterns to test for existence of asserted binary spatial relations between instances of geo:SpatialObject.	7

Req 5	Each of the properties referenced in Req 4 shall have rdfs:domain geo:SpatialObject, rdfs:range geo:SpatialObject, rdf:type rdf:Propery, and rdf:type owl:ObjectProperty.	8

Req 6	Implementations shall allow the properties geo:eh-equals, geo:eh-disjoint, geo:eh-meet, geo:eh-overlap, geo:eh-covers, geo:eh-coveredBy, geo:eh-inside, geo:eh-contains to be used directly in SPARQL triple patterns to test for existence of asserted binary spatial relations between instances of geo:SpatialObject.	8

Req 7	Each of the properties referenced in Req 6 shall have rdfs:domain geo:SpatialObject, rdfs:range geo:SpatialObject, rdf:type rdf:Propery, and rdf:type owl:ObjectProperty.	9

Req 8	Implementations shall allow the properties geo:rcc8-eq, geo:rcc8-dc, geo:rcc8-ec, geo:rcc8-po, geo:rcc8-tppi, geo:rcc8-tpp, geo:rcc8-ntpp, geo:rcc8-ntppi to be used directly in SPARQL triple patterns to test for existence of asserted binary spatial relations between instances of geo:SpatialObject.	9

Req 9	Each of the properties referenced in Req 8 shall have rdfs:domain geo:SpatialObject, rdfs:range geo:SpatialObject, rdf:type rdf:Propery, and rdf:type owl:ObjectProperty.	10

Req 10	Implementations shall support transitivity of rdfs:subClassOf so that all feature objects subtype from the class geo:Geometry.	12

Req 11	Implementations shall allow the properties geo:hasGeometry and geo:defaultGeometry to be used directly in SPARQL triple patterns to retrieve information about instances of geo:Feature.	12

Req 12	Implementations shall allow the properties geo:dimension, geo:coordinateDimension, geo:spatialDimension, geo:isEmpty, geo:isSimple and geo:is3D to be used directly in SPARQL triple patterns to retrieve information about instances of geo:Geometry.	13

Req 13	Implementations shall support transitivity of rdfs:subClassOf for an RDFS/OWL class hierarchy of geometry types consistent with the one in the specified version of Simple Features.	17

Req 14	All RDFS Literals of type WKTLiteral shall consist of an optional URI identifying the coordinate reference system followed by Simple Features Well Known Text (WKT) describing a geometric value.	17

Req 15	The URI <http://www.opengis.net/def/crs/OGC/1.3/CRS84> shall be used to denote the spatial reference system for WKTLiterals that do not specify an explicit spatial reference system URI.	18

Req 16	Coordinate tuples within WKTLiterals shall be interpreted using the axis order defined in the spatial reference system used.	18

Req 17	An empty RDFS Literal of type WKTLiteral shall be interpreted as an empty geometry.	18

Req 18	Implementations shall allow the RDF property geo:asWKT to be used directly in GeoSPARQL triple patterns to retrieve a WKTLiteral for elements of type geo:Geometry.	18

Req 19	Implementations shall support transitivity of rdfs:subClassOf for an RDFS/OWL class hierarchy of geometry types consistent with the GML schema that implements GM_Object using the specified version of GML.	20

Req 20	All GMLLiterals shall consist of a valid element from the GML schema that implements a subtype of GM_Object.	20

Req 21	An empty GMLLiteral shall be interpreted as an empty geometry.	20

Req 22	Implementations shall document supported GML profiles.	21

Req 23	Implementations shall allow the RDF property geo:asGML to be used directly in GeoSPARQL triple patterns to retrieve a GMLLiteral for elements of type geo:Geometry.	21

Req 24	Compliant implementations shall support the SPARQL functions geof:distance, geof:buffer, geof:convexHull, geof:intersection, geof:union, geof:difference, geof:symDifference, geof:envelope and geof:boundary, consistent with the serialization used.	21

Req 25	Implementations shall support the query function geof:relate.	24

Req 26	Implementations shall support the query functions geof:sf-equals, geof:sf-disjoint, geof:sf-intersects, geof:sf-touches, geof:sf-crosses, geof:sf-within, geof:sf-contains, geof:sf-overlaps.	25

Req 27	Implementations shall support the query functions geof:eh-equals, geof:eh-disjoint, geof:eh-meet, geof:eh-overlap, geof:eh-covers, geof:eh-coveredBy, geof:eh-inside, geof:eh-contains.	26

Req 28	Implementations shall support the query functions geof:rcc8-eq, geof:rcc8-dc, geof:rcc8-ec, geof:rcc8-po, geof:rcc8-tppi, geof:rcc8-tpp, geof:rcc8-ntpp, geof:rcc8-nttpi.	27

Req 29	Implementations shall support the query rewrite rules geor:sf-equals, geor:sf-disjoint, geor:sf-intersects, geor:sf-touches, geor:sf-crosses, geor:sf-within, geor:sf-contains, geor:sf-overlaps.	29

Req 30	Implementations shall support the query rewrite rules geor:eh-equals, geor:eh-disjoint, geor:eh-meet, geor:eh-overlap, geor:eh-covers, geor:eh-coveredBy, geor:eh-inside, geor:eh-contains.	30

Req 31	Implementations shall support the query rewrite rules geor:rcc8-eq, geor:rcc8-dc, geor:rcc8-ec, geor:rcc8-po, geor:rcc8-tppi, geor:rcc8-tpp, geor:rcc8-ntpp, geor:rcc8-ntppi.	30

Table of Requirements by URI

req/core/SPARQL	6

req/core/SpatialObjectClass	6

req/core/FeatureClass	7

req/topologyVocabExtension/SFSpatialRelations	8

req/topologyVocabExtension/SFSpatialRelationDefs	8

req/topologyVocabExtension/EHSpatialRelations	9

req/topologyVocabExtension/EHSpatialRelationDefs	9

req/topologyVocabExtension/RCC8SpatialRelations	10

req/topologyVocabExtension/RCC8SpatialRelationDefs	10

req/geometryExtension/GeometryClass	12

req/geometryExtension/FeatureProperties	12

req/geometryExtension/GeometryProperties	14

req/geometryExtension/WKTGeometyTypes	17

req/geometryExtension/WKTLiteral	17

req/geometryExtension/WKTLiteralDefaultSRS	18

req/geometryExtension/WKTAxisOrder	18

req/geometryExtension/WKTLiteralEmpty	18

req/geometryExtension/GeometryAsWKTLiteral	19

req/geometryExtension/GMLGeometyTypes	20

req/geometryExtension/GMLLiteral	20

req/geometryExtension/GMLLiteralEmpty	21

req/geometryExtension/GMLProfile	21

req/geometryExtension/GeometryAsGMLLiteral	21

req/geometryExtension/QueryFunctions	21

req/geometryTopologyExtension/RelateQueryFunction	24

req/geometryTopologyExtension/SFQueryFunctions	25

req/geometryTopologyExtension/EHQueryFunctions	26

req/geometryTopologyExtension/RCC8QueryFunctions	27

req/queryRewriteExtension/SFQueryRewrite	29

req/queryRewriteExtension/EHQueryRewrite	30

req/queryRewriteExtension/RCC8QueryRewrite	30

Preface

This draft standard defines a core RDF vocabulary for geographic information based on the General Feature Model [ISO 19109], Simple Features [ISO 19125-1], Feature Geometry [ISO 19107] and SQL MM [ISO/IEC 13249-3].

Submitting organizations

The following organizations submitted this Implementation Specification to the Open Geospatial Consortium Inc. as a Request For Comment (RFC):

Australian Bureau of Meteorology

Bentley Systems, Inc.

CSIRO

Defence Geospatial Information Working Group (DGIWG)

GeoConnections - Natural Resources Canada

Interactive Instruments GmbH

Oracle America

Ordnance Survey

Raytheon Company

Traverse Technologies, Inc.

US Geological Survey (USGS)

Submission contact points

All questions regarding this submission should be directed to the editor or the submitters:

| CONTACT | COMPANY |
| --- | --- |
| Matthew Perry | Oracle America |
| John Herring | Oracle America |

Revision history

| Date | Release | Author | Paragraph modified | Description |
| --- | --- | --- | --- | --- |
| 27 Oct. 2009 | Draft | Matthew Perry | Clause 6 | Technical Draft |
| 11 Nov. 2009 | Draft | John R. Herring | All | Creation |
| 6 Jan. 2010 | Draft | John R. Herring | All | Comment responses |
| 30 March 2010 | Draft | Matthew Perry | All | Comment responses |
| 26 Oct. 2010 | Draft | Matthew Perry | All | Revision based on working group discussion |
| 28 Jan. 2011 | Draft | Matthew Perry | All | Revision based on working group discussion |
| 18 April 2011 | Draft | Matthew Perry | All | Restructure with multiple conformance classes |
| 02 May 2011 | Draft | Matthew Perry | Clause 6 and Clause 8 | Move Geometry Class from core to geometryExtension |
| 05 May 2011 | Draft | Matthew Perry | All | Update URIs |

Changes to the OGC® Abstract Specification

The OGC® Abstract Specification does not require changes to accommodate this OGC® standard.

Foreword

Attention is drawn to the possibility that some of the elements of this document may be the subject of patent rights. Open Geospatial Consortium shall not be held responsible for identifying any or all such patent rights. However, to date, no such rights have been claimed or identified.

Recipients of this document are requested to submit, with their comments, notification of any relevant patent claims or other intellectual property rights of which they may be aware that might be infringed by any implementation of the specification set forth in this document, and to provide supporting documentation.

Introduction

The W3C Semantic Web activity is defining a collection of technologies that enables a “web of data” where information is easily shared and reused across applications. Some key pieces of this technology stack are the RDF (Resource Description Framework) data model, the OWL (Web Ontology Language) ontology language and the SPARQL protocol and RDF query language.

RDF is, among other things, a data model built on edge-node "graphs." Each link in a graph consists of three things (with many aliases depending on the mapping from other types of data models):

Subject (start node, instance (OOPL), feature, blank node)

Predicate (verb, property, attribute, relation, member (OOPL), link, reference)

Object (value, end node, values can be used as a Subject)

Any of the three values in a single triple can be represented via an URI (with an optional fragment identifier). Subjects and objects are called nodes and can be represented as a blank node (usually with a local identifier with no meaning). Objects can also be represented as a literal value. Note that the same node may play the role of a Subject in some edges, and the role of the Object in others.

: RDF Triple

Almost all data can be presented or represented in RDF. In particular, it is an easy match to the (feature-instance-by-id, attribute, value) tuples of the General Feature Model (ISO 19109), and for the relational model as (table primary key, column, value).

From http://dbpedia.org/page/SPARQL:

SPARQL is an RDF query language; its name is a recursive acronym that stands for SPARQL Protocol and RDF Query Language. It was standardized by the RDF Data Access Working Group (DAWG) of the World Wide Web Consortium, and is considered a key semantic web technology. On 15 January 2008, SPARQL became an official W3C Recommendation. SPARQL allows [a] query to consist of triple patterns, conjunctions, disjunctions, and optional patterns.

SPARQL queries work on RDF representations of data by finding patterns that match templates in the query, in effect finding information graphs in the RDF data based on the templates and filters (constraints on nodes and edges) expressed in the query. This query template is represented in the SPARQL query by a set of parameterized “query variables” appearing in a sequence of RDF triples and filters. If the query processor finds a set of triples in the data (converted to an RDF graph in some predetermined standard manner) then the values that the “query variables” take on in those triples become a solution to the query request. The values of the variables are returned in the query result in a format based on the “SELECT” clause of the query (similar to SQL).

In addition to predicates defined in this manner, the SPARQL query may contain filter functions that can be used to further constrain the query. Several mechanisms are available to extend filter functions to allow for predicates calculated directly on data values. The SPARQL specification [W3C SPARQL] in section 11.6 (http://www.w3.org/TR/rdf-sparql-query/#extensionFunctions) describes the mechanism for invocation of such a filter function. Complex information can often be expressed as graphs, or lexically as list of triples using common identifiers for nodes used in common, having the same value or identifier.

The OGC GeoSPARQL standard supports representing and querying geospatial data on the Semantic Web. GeoSPARQL defines a vocabulary for representing geospatial data in RDF, and it defines an extension to the SPARQL query language for processing geospatial data.

The GeoSPARQL standard follows a modular design; it comprises several different components. A core component defines top-level RDFS/OWL classes for spatial objects. A geometry component defines RDFS data types for serializing geometry data, RDFS/OWL classes for geometry object types, geometry-related RDF properties, and non-topological spatial query functions for geometry objects. A geometry topology component defines topological query functions. A topological vocabulary component defines RDF properties for asserting topological relations between spatial objects, and a query rewrite component defines rules for transforming a simple triple pattern that tests a topological relation between two features into an equivalent query involving concrete geometries and topological query functions.

Each of the components described above forms a requirements class for GeoSPARQL. Implementations can provide various levels of functionality by choosing which requirements classes to support. For example, a system based purely on qualitative spatial reasoning may support only the core and topological vocabulary components.

GeoSPARQL is designed to accommodate systems based on qualitative spatial reasoning and systems based on quantitative spatial computations. Systems based on qualitative spatial reasoning, (e.g. those based on the Region Connection Calculus [1, 4]) do not usually model explicit geometries, so queries in such systems will likely test for binary spatial relationships between features rather than between explicit geometries. To allow queries for spatial relations between features in quantitative systems, GeoSPARQL defines a series of query transformation rules that expand a feature-only query into a geometry-based query. With these transformation rules, queries about spatial relations between features will have the same specification in both qualitative systems and quantitative systems. The qualitative system will likely evaluate the query with a backward-chaining spatial “reasoner”, and the quantitative system can transform the query into a geometry-based query that can be evaluated with computational geometry.

OGC GeoSPARQL – A Geographic Query Language for RDF Data

# Scope

This document defines GeoSPARQL: a spatial extension to the SPARQL query language for geographic information as defined in OGC. GeoSPARQL provides the following features:

An RDF/OWL vocabulary for representing spatial information

A set of functions for spatial computations

A set of query transformation rules

# Conformance

Conformance with this specification shall be checked using all the relevant tests specified in Annex A (normative). The framework, concepts, and methodology for testing, and the criteria to be achieved to claim conformance are specified in ISO 19105: Geographic information — Conformance and Testing.

This document establishes several requirements classes and corresponding conformance classes. Any GeoSPARQL implementation claiming conformance with one of the conformance classes shall pass all the tests in the associated abstract test suite. Requirements and conformance test URIs defined in this document are relative to http://www.opengis.net/spec/GeoSPARQL/1.0/. Table 1 summarizes the conformance classes in GeoSPARQL.

-- Conformance Classes

| Conformance class | Description | Subclause of the abstract test suite |
| --- | --- | --- |
| Core | Defines top-level spatial vocabulary components | A.1 |
| Topology Vocabulary Extension (relation_family) | Defines topological relation vocabulary | A.2 |
| Geometry Extension (serialization, version) | Defines geometry vocabulary and non-topological query functions | A.3 |
| Geometry Topology Extension (serialization, version, relation_family) | Defines topological query functions for geometry objects | A.4 |
| Query Rewrite Extension (serialization, version, relation_family) | Defines query transformation rules for computing spatial relations between spatial objects based on their associated geometries | A.5 |

Dependencies between each GeoSPARQL requirements class are shown in Figure 2 below. To support a requirements class for a given set of parameter values, an implementation must support each dependent requirements class with the same set of parameter values.

: Requirements Class Dependency Graph

# Normative references

The following normative documents contain provisions which, through reference in this text, constitute provisions of this document. For dated references, subsequent amendments to, or revisions of, any of these publications do not apply. However, parties to agreements based on this document are encouraged to investigate the possibility of applying the most recent editions of the normative documents indicated below. For undated references, the latest edition of the normative document referred to applies.

ISO/IEC 13249-3:2006, Information technology — Database languages — SQL multimedia and application packages — Part 3: Spatial

ISO 19107:2003, Geographic information — Spatial schema

ISO 19109:2005, Geographic information — Rules for application schemas

ISO 19125-1:2004, Geographic information — Simple feature access — Part 1: Common architecture

OGC 07-036, Geography Markup Language (GML) Encoding Standard, version 3.2.1

W3C RDF XML, RDF/XML Syntax Specification (Revised). W3C Recommendation 10 February 2004

W3C RDF Semantics, RDF Semantics. W3C Recommendation, 10 February 2004

W3C RDF, Resource Description Framework (RDF): Concepts and Abstract Syntax. W3C Recommendation 10 February 2004

W3C RIF Overview, RIF Overview. W3C Working Group Note 22 June 2010

W3C RIF Core, RIF Core Dialect. W3C Recommendation 22 June 2010

W3C SPARQL PROTOCOL, SPARQL Protocol for RDF. W3C Recommendation 15 January 2008

W3C SPARQL, SPARQL Query Language for RDF. W3C Recommendation 15 January 2008

W3C SPARQL RESULT FORMAT, SPARQL Query Results XML Format. W3C Recommendation 15 January 2008

W3C OWL2, OWL 2 Web Ontology Language Document Overview. W3C Recommendation 27 October 2009

W3C XML, Extensible Markup Language (XML) 1.0 (Second Edition), W3C Recommendation 6 October 2000

W3C XML Namespaces, Namespaces in XML. W3C Recommendation 14 January 1999

W3C XML Schema Part 1, XML Schema Part 1: Structures. W3C Recommendation 2 May 2001

W3C XML Schema Part 2, XML Schema Part 2: Datatypes. W3C Recommendation 2 May 2001

# Terms and definitions

For the purposes of this document, the terms and definitions given in the above references apply.

# Conventions

## Symbols (and abbreviated terms)

In this draft candidate standard, the following common acronyms are used:

GeoJSON		Geographic JavaScript Object Notation

GFM			General Feature Model (as defined in ISO 19109)

GML			Geography Markup Language

KML			Keyhole Markup Language

OWL			Web Ontology Language

RCC			Region Connection Calculus

RDF			Resource Description Framework

RDFS			RDF Schema

RIF				Rule Interchange Format

SPARQL		SPARQL Protocol and RDF Query Language

WKT			Well Known Text (as defined by Simple Features or ISO 19125)

W3C			World Wide Web Consortium (http://www.w3.org/)

XML			eXtended Markup Language

## XML Namespaces

The following XML namespace prefixes are used throughout this document.

ogc:		http://www.opengis.net/

geo:		http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/

geoot:	http://www.opengis.net/def/objectType/OGC-GeoSPARQL/1.0/

geoft:	http://www.opengis.net/def/featureType/OGC-GeoSPARQL/1.0/

geogt:	http://www.opengis.net/def/geometryType/OGC-GeoSPARQL/1.0/

geop:	http://www.opengis.net/def/property/OGC-GeoSPARQL/1.0/

geof:	http://www.opengis.net /def/queryLanguage/OGC-GeoSPARQL/1.0/function/

geor:	http://www.opengis.net /def/queryLanguage/OGC-GeoSPARQL/1.0/rule/

my:		http://somewhere/ApplicationSchema#

xsd:		http://www.w3.org/2001/XMLSchema#

rdf:		http://www.w3.org/1999/02/22-rdf-syntax-ns#

rdfs:	http://www.w3.org/2000/01/rdf-schema#

owl:		http://www.w3.org/2002/07/owl#

## Placeholder URIs

The URI ogc:GeomLiteral is used in requirement specifications as a placeholder for the geometry literal serialization used in a fully-qualified conformance class, e.g. <http://www.opengis.net/def/dataType/OGC-SF/1.0/WKTLiteral>.

The URI ogc:asGeomLiteral is used in requirement specifications as a placeholder for the geometry literal serialization property used in a fully-qualified conformance class, e.g. geo:asWKT.

# Core

This clause establishes the core requirements class, with URI /req/core, which has a single corresponding conformance class, core, with URI /conf/core. This requirements class defines a set of classes and properties for representing geospatial data. The resulting vocabulary can be used to construct SPARQL graph patterns for querying appropriately modeled geospatial data. RDFS and OWL vocabulary have both been used so that the vocabulary can be understood by systems that support only RDFS entailment and by systems that support OWL-based reasoning.

## SPARQL Protocol

Implementations shall support the SPARQL Protocol for RDF [W3C SPARQL PROTOCOL] and the SPARQL Query Results XML Format [W3C SPARQL RESULT FORMAT].

/req/core/SPARQL

## Classes

Two main classes are defined: geo:SpatialObject and geo:Feature.

### Class: geo:SpatialObject

The class geo:SpatialObject is defined by the following:

<rdf:Description rdf:about=

"http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/SpatialObject">

<rdf:type rdf:resource=

"http://www.w3.org/2000/01/rdf-schema#Class"/>

<rdf:type rdf:resource=

"http://www.w3.org/2002/07/owl#Class"/>

<rdfs:isDefinedBy rdf:resource=

"http://www.opengis.net/spec/GeoSPARQL/1.0"/>

<rdfs:label>SpatialObject</rdfs:label>

<rdfs:comment>

The class SpatialObject, superclass of everything feature

or geometry that can have a spatial representation.

</rdfs:comment>

</rdf:Description>

Implementations shall support transitivity of rdfs:subClassOf so that all feature and geometry objects subtype from the root class geo:SpatialObject.

/req/core/SpatialObjectClass

### Class: geo:Feature

The class geo:Feature is defined by the following:

<rdf:Description rdf:about=

"http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/Feature">

<rdf:type rdf:resource=

"http://www.w3.org/2000/01/rdf-schema#Class"/>

<rdf:type rdf:resource=

"http://www.w3.org/2002/07/owl#Class"/>

<rdfs:isDefinedBy rdf:resource=

"http://www.opengis.net/spec/GeoSPARQL/1.0"/>

<rdfs:label>Feature</rdfs:label>

<rdfs:subClassOf rdf:resource=

"http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/SpatialObject"/>

<rdfs:comment>

The class Feature, superclass of everything

feature.

</rdfs:comment>

</rdf:Description>

Implementations shall support transitivity of rdfs:subClassOf so that all feature objects subtype from the class geo:Feature.

/req/core/FeatureClass

# Topology Vocabulary Extension (relation_family)

This clause establishes the Topology Vocabulary Extension (relation_family) parameterized requirements class, with URI /req/topologyVocabExtension, which has a single corresponding conformance class Topology Vocabulary Extension (relation_family), with URI /conf/topologyVocabExtension. This requirements class defines a vocabulary for asserting topological relations between spatial objects. The class is parameterized so that different families of topological relations may be used, e.g. RCC8, Egenhofer. These relations are generalized so that they may connect features as well as geometries.

A DE-9IM pattern that specifies the intersections of the interiors, boundaries and exteriors of two geometric objects is used to describe each spatial relation. Possible pattern values are T – true, F – false, * – don’t care. Consult the Simple Features specification [ISO 19125-1:2004] for a more detailed description DE-9IM intersection patterns.

## Parameters

The following parameter is defined for the Topology Vocabulary Extension requirements class.

relation_family: Specifies the set of topological spatial relations to support.

## Requirements for Simple Features Relation Family

This clause defines requirements for the Simple Features relation family.

Implementations shall allow the properties geo:sf-equals, geo:sf-disjoint, geo:sf-intersects, geo:sf-touches, geo:sf-crosses, geo:sf-within, geo:sf-contains, geo:sf-overlaps to be used directly in SPARQL triple patterns to test for existence of asserted binary spatial relations between instances of geo:SpatialObject.

/req/topologyVocabExtension/SFSpatialRelations

Each of the properties referenced in Req 4 shall have rdfs:domain geo:SpatialObject, rdfs:range geo:SpatialObject, rdf:type rdf:Propery, and rdf:type owl:ObjectProperty.

/req/topologyVocabExtension/SFSpatialRelationDefs

Topological relations in the Simple Features family are summarized in Table 1. Note that multi-row intersection patterns should be interpreted as a logical OR of each row.

- – Simple Features Topological Relations

| Relation Name | Relation URI | DE-9IM Intersection Pattern |
| --- | --- | --- |
| equals | geo:sf-equals | TFFFTFFFT |
| disjoint | geo:sf-disjoint | FF*FF**** |
| intersects | geo:sf-intersects | T******** *T******* ***T***** ****T**** |
| touches | geo:sf-touches | FT******* F**T***** F***T**** |
| within | geo:sf-within | T*F**F*** |
| contains | geo:sf-contains | T*****FF* |
| overlaps | geo:sf-overlaps | T*T***T** |
| crosses | geo:sf-crosses | T*T****** |

## Requirements for Egenhofer Relation Family

This clause defines requirements for the Egenhofer relation family. For a more detailed discussion of the Egenhofer relations, consult references [2] and [3].

Implementations shall allow the properties geo:eh-equals, geo:eh-disjoint, geo:eh-meet, geo:eh-overlap, geo:eh-covers, geo:eh-coveredBy, geo:eh-inside, geo:eh-contains to be used directly in SPARQL triple patterns to test for existence of asserted binary spatial relations between instances of geo:SpatialObject.

/req/topologyVocabExtension/EHSpatialRelations

Each of the properties referenced in Req 6 shall have rdfs:domain geo:SpatialObject, rdfs:range geo:SpatialObject, rdf:type rdf:Propery, and rdf:type owl:ObjectProperty.

/req/topologyVocabExtension/EHSpatialRelationDefs

Topological relations in the Egenhofer family are summarized in Table 2. Note that multi-row intersection patterns should be interpreted as a logical OR of each row.

- – Egenhofer Topological Relations

| Relation Name | Relation URI | DE-9IM Intersection Pattern |
| --- | --- | --- |
| equals | geo:eh-equals | TFFFTFFFT |
| disjoint | geo:eh-disjoint | FF*FF**** |
| meet | geo:eh-meet | FT******* F**T***** F***T**** |
| overlap | geo:eh-overlap | T*T***T** |
| covers | geo:eh-covers | T*TFT*FF* |
| covered by | geo:eh-coveredBy | TFF*TFT** |
| inside | geo:eh-inside | TFF*FFT** |
| contains | geo:eh-contains | T*TFF*FF* |

## Requirements for RCC8 Relation Family

This clause defines requirements for the RCC8 relation family. For a more detailed discussion of RCC8 relations, consult references [1] and [4].

Implementations shall allow the properties geo:rcc8-eq, geo:rcc8-dc, geo:rcc8-ec, geo:rcc8-po, geo:rcc8-tppi, geo:rcc8-tpp, geo:rcc8-ntpp, geo:rcc8-ntppi to be used directly in SPARQL triple patterns to test for existence of asserted binary spatial relations between instances of geo:SpatialObject.

/req/topologyVocabExtension/RCC8SpatialRelations

Each of the properties referenced in Req 8 shall have rdfs:domain geo:SpatialObject, rdfs:range geo:SpatialObject, rdf:type rdf:Propery, and rdf:type owl:ObjectProperty.

/req/topologyVocabExtension/RCC8SpatialRelationDefs

Topological relations in the Egenhofer family are summarized in Table 3.

- – RCC8 Topological Relations

| Relation Name | Relation URI | DE-9IM Intersection Pattern (for non-empty regions) |
| --- | --- | --- |
| equals | geo:rcc8-eq | TFFFTFFFT |
| disconnected | geo:rcc8-dc | FFTFFTTTT |
| externally connected | geo:rcc8-ec | FFTFTTTTT |
| partially overlapping | geo:rcc8-po | TTTTTTTTT |
| tangential proper part inverse | geo:rcc8-tppi | TTTFTTFFT |
| tangential proper part | geo:rcc8-tpp | TFFTTFTTT |
| non-tangential proper part | geo:rcc8-ntpp | TFFTFFTTT |
| non-tangential proper part inverse | geo:rcc8-ntppi | TTTFFTFFT |

## Equivalent RCC8, Egenhofer and Simple Features Topological Relations

Table 4 summarizes the equivalences between Egenhofer, RCC8 and Simple Features spatial relations for closed, non-empty regions.

- -- Equivalent Simple Features, RCC8 and Egenhofer relations

| Simple Features | RCC8 | Egenhofer |
| --- | --- | --- |
| equals | EQ | equal |
| disjoint | DC | disjoint |
| intersects | ¬ DC | ¬ disjoint |
| touches | EC | meet |
| within | NTPP + TPP | inside + coveredBy |
| contains | NTPPi + TPPi | contains + covers |
| overlaps | PO | overlap |

# Geometry Extension (serialization, version)

This clause establishes the Geometry Extension (serialization, version) parameterized requirements class, with URI /req/geometryExtension, which has a single corresponding conformance class Geometry Extension (serialization, version), with URI /conf/geometryExtension. This requirements class defines a vocabulary for asserting information about geometry data, and it defines query functions for operating on geometry data.

As part of the vocabulary, an RDFS dataype is defined for encoding detailed geometry information as a literal value. A literal representation of a geometry is needed so that geometric values may be treated as a single unit. Such a representation allows geometries to be passed to external functions for computations and to be returned from a query.

## Parameters

The following parameters are defined for the Geometry Extension requirements class.

serialization: Specifies the serialization standard to use when generating geometry literals and also determines the taxonomy of geo:Geometry subclasses that is supported.

version: Specifies the version of the serialization format used.

## Geometry Classes and Properties

A single root geometry class is defined: geo:Geometry. In addition, properties are defined for describing geometry data and for associating geometries with features.

### Class: geo:Geometry

The class geo:Geometry is defined by the following:

<rdf:Description rdf:about=

"http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/Geometry">

<rdf:type rdf:resource=

"http://www.w3.org/2000/01/rdf-schema#Class"/>

<rdf:type rdf:resource=

"http://www.w3.org/2002/07/owl#Class"/>

<rdfs:isDefinedBy rdf:resource=

"http://www.opengis.net/spec/GeoSPARQL/1.0"/>

<rdfs:label>Geometry</rdfs:label>

<rdfs:subClassOf rdf:resource=

"http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/SpatialObject"/>

<rdfs:comment>

The class Geometry, superclass of everything

geometry.

</rdfs:comment>

</rdf:Description>

Implementations shall support transitivity of rdfs:subClassOf so that all feature objects subtype from the class geo:Geometry.

/req/geometryExtension/GeometryClass

## Standard Properties for geo:Feature

Properties are defined for associating geometries with features.

Implementations shall allow the properties geo:hasGeometry and geo:defaultGeometry to be used directly in SPARQL triple patterns to retrieve information about instances of geo:Feature.

/req/geometryExtension/FeatureProperties

#### Property: geo:hasGeometry

The property geo:hasGeometry is used to link a feature with a geometry that represents its spatial extent. A given feature may have many associated geometries.

<rdf:Description rdf:about=

"http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/hasGeometry">

<rdf:type rdf:resource=

"http://www.w3.org/1999/02/22-rdf-syntax-ns#Property"/>

<rdf:type rdf:resource=

"http://www.w3.org/2002/07/owl#ObjectProperty"/>

<rdfs:isDefinedBy rdf:resource=

"http://www.opengis.net/spec/GeoSPARQL/1.0"/>

<rdfs:label>hasGeometry</rdfs:label>

<rdfs:comment>

A spatial representation for a given feature.

</rdfs:comment>

<rdfs:domain rdf:resource=

"http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/Feature"/>

<rdfs:range rdf:resource=

"http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/Geometry"/>

</rdf:Description>

#### Property: geo:defaultGeometry

The property geo:defaultGeometry is used to link a feature with its default geometry. The default geometry is the geometry that should be used for spatial calculations in the absence of a request for a specific geometry (e.g. in the case of query rewrite).

<rdf:Description rdf:about=

"http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/defaultGeometry">

<rdf:type rdf:resource=

"http://www.w3.org/1999/02/22-rdf-syntax-ns#Property"/>

<rdf:type rdf:resource=

"http://www.w3.org/2002/07/owl#ObjectProperty"/>

<rdfs:isDefinedBy rdf:resource=

"http://www.opengis.net/spec/GeoSPARQL/1.0"/>

<rdfs:label>defaultGeometry</rdfs:label>

<rdfs:comment>

The default geometry to be used in spatial calculations

</rdfs:comment>

<rdfs:subPropertyOf rdf:resource=

"http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/hasGeometry"/>

<rdfs:domain rdf:resource=

"http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/Feature"/>

<rdfs:range rdf:resource=

"http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/Geometry"/>

</rdf:Description>

GeoSPARQL does not restrict the cardinality of the geo:defaultGeometry property. It is thus possible for a feature to have more than one distinct default geometry. This situation does not result in a query processing error; SPARQL graph pattern matching simply proceeds as normal. Certain queries may, however, give logically inconsistent results. For example, given a feature my:f1 with two distinct default geometries, the query below could have a non-empty result.

PREFIX geo: <http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/>

PREFIX geof:
    <http://www.opengis.net /def/queryLanguage/OGC-GeoSPARQL/1.0/function/>

SELECT ?f2

WHERE { :f1 geo:defaultGeometry ?g1

?g1 geo:asWKT ?w1 .

?f2 geo:defaultGeometry ?g2 .

?g2 geo:asWKT ?w2

FILTER (geof:sf-within(?w1, ?w2) &&

geof:sf-contains(?w1, ?w2)) }

Such cases are application-specific data modeling errors and are therefore outside of the scope of the GeoSPARQL specification.

## Standard Properties for geo:Geometry

Properties are defined for describing geometry metadata.

Implementations shall allow the properties geo:dimension, geo:coordinateDimension, geo:spatialDimension, geo:isEmpty, geo:isSimple and geo:is3D to be used directly in SPARQL triple patterns to retrieve information about instances of geo:Geometry.

/req/geometryExtension/GeometryProperties

### Property: geo:dimension

The dimension is the topological dimension of this geometric object, which must be less than or equal to the coordinate dimension. In non-homogeneous collections, this will return the largest topological dimension of the contained objects.

<rdf:Description rdf:about=

"http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/dimension">

<rdf:type rdf:resource=

"http://www.w3.org/1999/02/22-rdf-syntax-ns#Property"/>

<rdf:type rdf:resource=

"http://www.w3.org/2002/07/owl#DatatypeProperty"/>

<rdfs:isDefinedBy rdf:resource=

"http://www.opengis.net/spec/GeoSPARQL/1.0"/>

<rdfs:label>dimension</rdfs:label>

<rdfs:comment>

The topological dimension of this geometric object, which

must be less than or equal to the coordinate dimension.

In non-homogeneous collections, this will return the largest

topological dimension of the contained objects.

</rdfs:comment>

<rdfs:domain rdf:resource=

"http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/Geometry"/>

<rdfs:range rdf:resource=

"http://www.w3.org/2001/XMLSchema#integer"/>

</rdf:Description>

### Property: geo:coordinateDimension

The coordinate dimension is dimension of direct position (coordinate tuples) used in the definition of this geometric object.

<rdf:Description rdf:about=

"http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/coordinateDimension">

<rdf:type rdf:resource=

"http://www.w3.org/1999/02/22-rdf-syntax-ns#Property"/>

<rdf:type rdf:resource=

"http://www.w3.org/2002/07/owl#DatatypeProperty"/>

<rdfs:isDefinedBy rdf:resource=

"http://www.opengis.net/spec/GeoSPARQL/1.0"/>

<rdfs:label>coordinateDimension</rdfs:label>

<rdfs:domain rdf:resource=

"http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/Geometry"/>

<rdfs:range rdf:resource=

"http://www.w3.org/2001/XMLSchema#integer"/>

</rdf:Description>

### Property: geo:spatialDimension

The spatial dimension is dimension of the spatial portion of the direct positions (coordinate tuples) used in the definition of this geometric object. If the direct positions do not carry a measure coordinate, this will be equal to the coordinate position.

<rdf:Description rdf:about=

"http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/spatialDimension">

<rdf:type rdf:resource=

"http://www.w3.org/1999/02/22-rdf-syntax-ns#Property"/>

<rdf:type rdf:resource=

"http://www.w3.org/2002/07/owl#DatatypeProperty"/>

<rdfs:isDefinedBy rdf:resource=

"http://www.opengis.net/spec/GeoSPARQL/1.0"/>

<rdfs:label>spatialDimension</rdfs:label>

<rdfs:domain rdf:resource=

"http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/Geometry"/>

<rdfs:range rdf:resource=

"http://www.w3.org/2001/XMLSchema#integer"/>

</rdf:Description>

### Property: geo:isEmpty

The geo:isEmpty Boolean will be set to TRUE, only if the geometry contains no points.

<rdf:Description rdf:about=

"http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/isEmpty">

<rdf:type rdf:resource=

"http://www.w3.org/1999/02/22-rdf-syntax-ns#Property"/>

<rdf:type rdf:resource=

"http://www.w3.org/2002/07/owl#DatatypeProperty"/>

<rdfs:isDefinedBy rdf:resource=

"http://www.opengis.net/spec/GeoSPARQL/1.0"/>

<rdfs:label>isEmpty</rdfs:label>

<rdfs:comment>

(TRUE) if this geometric object is the empty Geometry. If

true, then this geometric object represents the empty point

set for the coordinate space.

</rdfs:comment>

<rdfs:domain rdf:resource=

"http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/Geometry"/>

<rdfs:range rdf:resource=

"http://www.w3.org/2001/XMLSchema#boolean"/>

</rdf:Description>

### Property: geo:isSimple

The geo:isSimple Boolean will be set to TRUE, only if the geometry contains no self-intersections, with the possible exception of its boundary.

<rdf:Description rdf:about=

"http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/isSimple">

<rdf:type rdf:resource=

"http://www.w3.org/1999/02/22-rdf-syntax-ns#Property"/>

<rdf:type rdf:resource=

"http://www.w3.org/2002/07/owl#DatatypeProperty"/>

<rdfs:isDefinedBy rdf:resource=

"http://www.opengis.net/spec/GeoSPARQL/1.0"/>

<rdfs:label>isSimple</rdfs:label>

<rdfs:comment>

(TRUE) if this geometric object has no anomalous geometric

points, such as self intersection or self tangency.

</rdfs:comment>

<rdfs:domain rdf:resource=

"http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/Geometry"/>

<rdfs:range rdf:resource=

"http://www.w3.org/2001/XMLSchema#boolean"/>

</rdf:Description>

### Property: geo:is3D

The geo:is3D Boolean will be set to TRUE, only if the geometry uses three spatial dimensions. This should be consistent with the spatial reference system, which would have to reference three spatial dimensions.

<rdf:Description rdf:about=

"http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/is3D">

<rdf:type rdf:resource=

"http://www.w3.org/1999/02/22-rdf-syntax-ns#Property"/>

<rdf:type rdf:resource=

"http://www.w3.org/2002/07/owl#DatatypeProperty"/>

<rdfs:isDefinedBy rdf:resource=

"http://www.opengis.net/spec/GeoSPARQL/1.0"/>

<rdfs:label>is3D</rdfs:label>

<rdfs:comment>

(TRUE) if this geometric object has z coordinate

values.

</rdfs:comment>

<rdfs:domain rdf:resource=

"http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/Geometry"/>

<rdfs:range rdf:resource=

"http://www.w3.org/2001/XMLSchema#boolean"/>

</rdf:Description>

## Requirements for WKT Serialization

This section establishes the requirements for representing geometry data in RDF based on WKT as defined by Simple Features or ISO 19125.

### Geometry Class Hierarchy

The Simple Features specification presents a geometry class hierarchy. It is straightforward to represent this class hierarchy in RDFS and OWL by constructing URIs for geometry classes using the following pattern: http://www.opengis.net/def/geometryType/OGC-SF/{version}/{geometry class} and by asserting appropriate rdfs:subClassOf statements.

The example RDF snippet below encodes the Polygon class from Simple Features 1.0.

<rdf:Description rdf:about=

"http://www.opengis.net/def/geometryType/OGC-SF/1.0/Polygon">

<rdf:type rdf:resource=

"http://www.w3.org/2000/01/rdf-schema#Class"/>

<rdf:type rdf:resource=

"http://www.w3.org/2002/07/owl#Class"/>

<rdfs:isDefinedBy rdf:resource=

"http://www.opengis.net/spec/GeoSPARQL/1.0"/>

<rdfs:label>Polygon</rdfs:label>

<rdfs:subClassOf rdf:resource=

"http://www.opengis.net/def/geometryType/OGC-SF/1.0/Surface"/>

<rdfs:comment>

A planar surface defined by 1 exterior boundary and 0 or more

interior boundaries.

</rdfs:comment>

</rdf:Description>

Implementations shall support transitivity of rdfs:subClassOf for an RDFS/OWL class hierarchy of geometry types consistent with the one in the specified version of Simple Features.

/req/geometryExtension/WKTGeometyTypes

### RDFS Datatypes

This section defines one RDFS Datatype: http://www.opengis.net/def/dataType/OGC-SF/{version}/WKTLiteral.

RDFS Datatype:  WKTLiteral

<rdfs:Datatype rdf:about=

"http://www.opengis.net/def/dataType/OGC-SF/{version}/WKTLiteral">

<rdfs:isDefinedBy rdf:resource="http://www.opengis.net/spec/GeoSPARQL/1.0"/>

<rdfs:label>Well-known Text Literal</rdfs:label>

<rdfs:comment>

A Well-known Text serialization of a geometry object.

</rdfs:comment>

</rdfs:Datatype>

All RDFS Literals of type WKTLiteral shall consist of an optional URI identifying the coordinate reference system followed by Simple Features Well Known Text (WKT) describing a geometric value.

/req/geometryExtension/WKTLiteral

Valid WKTLiterals are formed by concatenating a valid URI as defined in [W3C SPARQL],  one or more spaces (Unicode U+0020 character) as a separator,  and a WKT string as defined in [ISO 19125-1]. The beginning URI identifies the spatial reference system for the geometry. This leading spatial reference system URI is optional. In the absence of a leading spatial reference system URI, the following default spatial reference system URI will be used: 
<http://www.opengis.net/def/crs/OGC/1.3/CRS84>
This URI denotes WGS 84 longitude-latitude.

The URI <http://www.opengis.net/def/crs/OGC/1.3/CRS84> shall be used to denote the spatial reference system for WKTLiterals that do not specify an explicit spatial reference system URI.

/req/geometryExtension/WKTLiteralDefaultSRS

Coordinate tuples within WKTLiterals shall be interpreted using the axis order defined in the spatial reference system used.

/req/geometryExtension/WKTAxisOrder

The example WKTLiteral below encodes a point geometry using the default WGS 84 geodetic longitude-latitude spatial reference system for Simple Features 1.0:

"Point(-83.38 33.95)"^^<http://www.opengis.net/def/dataType/OGC-SF/1.0/WKTLiteral>

A second example below encodes the same point using <http://www.opengis.net/def/crs/EPSG/0/4326>: a WGS 84 geodetic latitude-longitude spatial reference system (note that this spatial reference system defines a different axis order):

"<http://www.opengis.net/def/crs/EPSG/0/4326>

Point(33.95 -83.38)"^^<http://www.opengis.net/def/dataType/OGC-SF/1.0/WKTLiteral>

An empty RDFS Literal of type WKTLiteral shall be interpreted as an empty geometry.

/req/geometryExtension/WKTLiteralEmpty

### Serialization Properties

The geo:asWKT property is defined to link a geometry with its WKT serialization.

Property: geo:asWKT

Implementations shall allow the RDF property geo:asWKT to be used directly in GeoSPARQL triple patterns to retrieve a WKTLiteral for elements of type geo:Geometry.

/req/geometryExtension/GeometryAsWKTLiteral

The property geo:asWKT is used to link a geometric element with its WKT serialization.

<rdf:Description rdf:about=

"http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/asWKT">

<rdf:type rdf:resource=

"http://www.w3.org/1999/02/22-rdf-syntax-ns#Property"/>

<rdf:type rdf:resource=

"http://www.w3.org/2002/07/owl#DatatypeProperty"/>

<rdfs:isDefinedBy rdf:resource="http://www.opengis.net/spec/GeoSPARQL/1.0"/>

<rdfs:label>asWKT</rdfs:label>

<rdfs:comment>

The WKT serialization of a geometry

</rdfs:comment>

<rdfs:domain rdf:resource=

"http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/Geometry"/>

<rdfs:range rdf:resource=

"http://www.opengis.net/def/dataType/OGC-SF/{version}/WKTLiteral"/>

</rdf:Description>

## Requirements for GML Serialization

This section establishes requirements for representing geometry data in RDF based on GML as defined by Geography Markup Language Encoding Standard [OGC 07-036].

### Geometry Class Hierarchy

An RDF/OWL class hierarchy can be generated from the GML schema that implements GM_Object by constructing URIs for geometry classes using the following pattern: http://www.opengis.net/def/geometryType/OGC-GML/{version}/{GML Element} and by asserting appropriate rdfs:subClassOf statements.

The example RDF snippet below encodes the Polygon class from GML 3.2.

<rdf:Description rdf:about=

"http://www.opengis.net/def/geometryType/OGC-GML/3.2/Polygon">

<rdf:type rdf:resource=

"http://www.w3.org/2000/01/rdf-schema#Class"/>

<rdf:type rdf:resource=

"http://www.w3.org/2002/07/owl#Class"/>

<rdfs:isDefinedBy rdf:resource=

"http://www.opengis.net/spec/GeoSPARQL/1.0"/>

<rdfs:label>Polygon</rdfs:label>

<rdfs:subClassOf rdf:resource=

"http://www.opengis.net/def/geometryType/OGC-GML/3.2/SurfacePatch"/>

<rdfs:comment>

A planar surface defined by 1 exterior boundary and 0 or more

interior boundaries.

</rdfs:comment>

</rdf:Description>

Implementations shall support transitivity of rdfs:subClassOf for an RDFS/OWL class hierarchy of geometry types consistent with the GML schema that implements GM_Object using the specified version of GML.

/req/geometryExtension/GMLGeometyTypes

### RDFS Datatypes

This section defines one RDFS Datatype: http://www.opengis.net/def/dataType/OGC-GML/{version}/GMLLiteral.

RDFS Datatype: GMLLiteral

<rdfs:Datatype rdf:about=

"http://www.opengis.net/def/dataType/OGC-GML/{version}/GMLLiteral">

<rdfs:isDefinedBy rdf:resource=

"http://www.opengis.net/spec/GeoSPARQL/1.0"/>

<rdfs:label>GML Literal</rdfs:label>

<rdfs:comment>

The datatype of GML literal values.

</rdfs:comment>

</rdfs:Datatype>

Valid GMLLiterals are formed by encoding geometry information as a valid element from the GML schema that implements a subtype of GM_Object. For example, in GML 3.2.1 this is every element directly or indirectly in the substitution group of the element {http://www.opengis.net/gml/3.2}AbstractGeometry. In GML 3.1.1 and GML 2.1.2 this is every element directly or indirectly in the substitution group of the element {http://www.opengis.net/gml}_Geometry.

All GMLLiterals shall consist of a valid element from the GML schema that implements a subtype of GM_Object.

/req/geometryExtension/GMLLiteral

The example GMLLiteral below encodes a point geometry in the WGS 84 geodetic longitude-latitude spatial reference system using GML version 3.2:

"<gml:Point

srsName=\"http://www.opengis.net/def/crs/OGC/1.3/CRS84\"

xmlns:gml=\"http://www.opengis.net/gml\">

<gml:posList srsDimension=\"2\">-83.38 33.95</gml:posList>

</gml:Point>"^^<http://www.opengis.net/def/dataType/OGC-GML/3.2/GMLLiteral>

An empty GMLLiteral shall be interpreted as an empty geometry.

/req/geometryExtension/GMLLiteralEmpty

Implementations shall document supported GML profiles.

/req/geometryExtension/GMLProfile

### Serialization Properties

This document defines the geo:asGML property to link a geometry with its serialization.

Property: geo:asGML

Implementations shall allow the RDF property geo:asGML to be used directly in GeoSPARQL triple patterns to retrieve a GMLLiteral for elements of type geo:Geometry.

/req/geometryExtension/GeometryAsGMLLiteral

The property geo:asGML is used to link a geometric element with its GML serialization.

<rdf:Description rdf:about=

"http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/asGML">

<rdf:type rdf:resource=

"http://www.w3.org/1999/02/22-rdf-syntax-ns#Property"/>

<rdf:type rdf:resource=

"http://www.w3.org/2002/07/owl#DatatypeProperty"/>

<rdfs:isDefinedBy rdf:resource=

"http://www.opengis.net/spec/GeoSPARQL/1.0"/>

<rdfs:label>asGML</rdfs:label>

<rdfs:comment>

The GML serialization of a geometry

</rdfs:comment>

<rdfs:domain rdf:resource=

"http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/Geometry"/>

<rdfs:range rdf:resource=

"http://www.opengis.net/def/dataType/OGC-GML/{version}/GMLLiteral"/>

</rdf:Description>

## Non-topological Query Functions

This clause defines SPARQL functions for performing non-topological spatial operations.

Compliant implementations shall support the SPARQL functions geof:distance, geof:buffer, geof:convexHull, geof:intersection, geof:union, geof:difference, geof:symDifference, geof:envelope and geof:boundary, consistent with the serialization used.

/req/geometryExtension/QueryFunctions

An invocation of any of the following functions with invalid arguments produces an error. An invalid argument includes any of the following:

An argument of an unexpected type

An invalid geometry literal value

A geometry literal from a spatial reference system that is incompatible with the spatial reference system used for calculations

An invalid units URI

For further discussion of the effects of errors during FILTER evaluation, consult Section 11 of the SPARQL specification [W3C SPARQL] (http://www.w3.org/TR/rdf-sparql-query/#tests).

An extended implementation of GeoSPARQL may not raise errors in all of these cases. For example, a system that supports WKTLiteral serializations may also support GMLLiteral serializations and consequently would not raise an error if it encounters multiple geometry datatypes while processing a given query.

Several non-topological query functions use a unit of measure URI. The OGC has defined some standard units of measure URIs under the http://www.opengis.net/def/uom/OGC/1.0/ namespace, for example <http://www.opengis.net/def/uom/OGC/1.0/metre>.

### Function: geof:distance

geof:distance (geom1: ogc:GeomLiteral, geom2: ogc:GeomLiteral,

units: xsd:anyURI): xsd:double

Returns the shortest distance in units between any two Points in the two geometric objects as calculated in the spatial reference system of geom1.

### Function: geof:buffer

geof:buffer (geom: ogc:GeomLiteral, radius: xsd:double,

units: xsd:anyURI): ogc:GeomLiteral

This function returns a geometric object that represents all Points whose distance from geom1 is less than or equal to the radius measured in units. Calculations are in the spatial reference system of geom1.

### Function: geof:convexHull

geof:convexHull (geom1: ogc:GeomLiteral): ogc:GeomLiteral

This function returns a geometric object that represents all Points in the convex hull of geom1. Calculations are in the spatial reference system of geom1.

### Function: geof:intersection

geof:intersection (geom1: ogc:GeomLiteral,

geom2: ogc:GeomLiteral): ogc:GeomLiteral

This function returns a geometric object that represents all Points in the intersection of geom1 with geom2. Calculations are in the spatial reference system of geom1.

### Function: geof:union

geof:union (geom1: ogc:GeomLiteral, geom2: ogc:GeomLiteral,

): ogc:GeomLiteral

This function returns a geometric object that represents all Points in the union of geom1 with geom2. Calculations are in the spatial reference system of geom1.

### Function: geof:difference

geof:difference (geom1: ogc:GeomLiteral, geom2: ogc:GeomLiteral,

): ogc:GeomLiteral

This function returns a geometric object that represents all Points in the set difference of geom1 with geom2. Calculations are in the spatial reference system of geom1.

### Function: geof:symDifference

geof:symDifference (geom1: ogc:GeomLiteral,

geom2: ogc:GeomLiteral,

): ogc:GeomLiteral

This function returns a geometric object that represents all Points in the set symmetric difference of geom1 with geom2. Calculations are in the spatial reference system of geom1.

### Function: geof:envelope

geof:envelope (geom1: ogc:GeomLiteral): ogc:GeomLiteral

This function returns the minimum bounding box of geom1. Calculations are in the spatial reference system of geom1.

### Function: geof:boundary

geof:boundary (geom1: ogc:GeomLiteral): ogc:GeomLiteral

This function returns the closure of the boundary of geom1. Calculations are in the spatial reference system of geom1.

# Geometry Topology Extension (relation_family, serialization, version)

This clause establishes the Geometry Topology Extension (relation_family, serialization, version) parameterized requirements class, with URI /req/geometryTopologyExtension, which defines a collection of topological query functions that operate on geometry literals. This class is parameterized to give implementations flexibility in the topological relation families and geometry serializations that they choose to support. This requirements class has a single corresponding conformance class Geometry Topology Extension (relation_family, serialization, version), with URI /conf/geometryTopologyExtension.

## Parameters

relation_family: Specifies the set of topological spatial relations to support.

serialization: Specifies the serialization standard to use for geometry literals.

version: Specifies the version of the serialization format used.

## Common Query Functions

Implementations shall support the query function geof:relate.

/req/geometryTopologyExtension/RelateQueryFunction

geof:relate (geom1: ogc:GeomLiteral, geom2: ogc:GeomLiteral,

patternMatrix: xsd:String): xsd:boolean

Returns true if the spatial relationship between geom1 and geom2 corresponds to one with acceptable values for the specified patternMatrix. Otherwise, this function returns false.  patternMatrix represents a DE-9IM intersection pattern. Consult Section 6.1.15.2 of Geographic information — Simple feature access — Part 1: Common architecture [ISO 19125-1] for a description of valid DE-9IM intersection pattern values. The spatial reference system for geom1 is used for spatial calculations.

## Requirements for Simple Features Relation Family

This clause establishes requirements for the Simple Features relation family.

Implementations shall support the query functions geof:sf-equals, geof:sf-disjoint, geof:sf-intersects, geof:sf-touches, geof:sf-crosses, geof:sf-within, geof:sf-contains, geof:sf-overlaps.

/req/geometryTopologyExtension/SFQueryFunctions

Boolean query functions defined for the Simple Features relation family are shown in Table 5 below. Each function accepts two arguments (geom1 and geom2) of the geometry literal serialization type specified by serialization and version. Each function returns an xsd:boolean value of true if the specified relation exists between geom1 and geom2 and returns false otherwise. In each case, the spatial reference system of geom1 is used for spatial calculations. Relations identified in Table 5 refer to those defined in Table 1.

- -- Simple Features Query Functions

| Query Function | Relation Tested |
| --- | --- |
| geof:sf-equals(geom1: ogc:GeomLiteral, geom2: ogc:GeomLiteral ): xsd:boolean | equals |
| geof:sf-disjoint(geom1: ogc:GeomLiteral, geom2: ogc:GeomLiteral ): xsd:boolean | disjoint |
| geof:sf-intersects(geom1: ogc:GeomLiteral, geom2: ogc:GeomLiteral ): xsd:boolean | intersects |
| geof:sf-touches(geom1: ogc:GeomLiteral, geom2: ogc:GeomLiteral ): xsd:boolean | touches |
| geof:sf-crosses(geom1: ogc:GeomLiteral, geom2: ogc:GeomLiteral ): xsd:boolean | crosses |
| geof:sf-within(geom1: ogc:GeomLiteral, geom2: ogc:GeomLiteral ): xsd:boolean | within |
| geof:sf-contains(geom1: ogc:GeomLiteral, geom2: ogc:GeomLiteral ): xsd:boolean | contains |
| geof:sf-overlaps(geom1: ogc:GeomLiteral, geom2: ogc:GeomLiteral ): xsd:boolean | overlaps |

## Requirements for Egenhofer Relation Family

This clause establishes requirements for the Egenhofer relation family.

Implementations shall support the query functions geof:eh-equals, geof:eh-disjoint, geof:eh-meet, geof:eh-overlap, geof:eh-covers, geof:eh-coveredBy, geof:eh-inside, geof:eh-contains.

/req/geometryTopologyExtension/EHQueryFunctions

Boolean query functions defined for the Egenhofer relation family are shown in Table 6 below. Each function accepts two arguments (geom1 and geom2) of the geometry literal serialization type specified by serialization and version. Each function returns an xsd:boolean value of true if the specified relation exists between geom1 and geom2 and returns false otherwise. In each case, the spatial reference system of geom1 is used for spatial calculations. Relations identified in Table 6 refer to those defined in Table 2.

- -- Egenhofer Query Functions

| Query Function | Relation Tested |
| --- | --- |
| geof:eh-equals(geom1: ogc:GeomLiteral, geom2: ogc:GeomLiteral ): xsd:boolean | equals |
| geof:eh-disjoint(geom1: ogc:GeomLiteral, geom2: ogc:GeomLiteral ): xsd:boolean | disjoint |
| geof:eh-meet(geom1: ogc:GeomLiteral, geom2: ogc:GeomLiteral ): xsd:boolean | meet |
| geof:eh-overlap(geom1: ogc:GeomLiteral, geom2: ogc:GeomLiteral ): xsd:boolean | overlap |
| geof:eh-covers(geom1: ogc:GeomLiteral, geom2: ogc:GeomLiteral ): xsd:boolean | covers |
| geof:eh-coveredBy(geom1: ogc:GeomLiteral, geom2: ogc:GeomLiteral ): xsd:boolean | covered by |
| geof:eh-inside(geom1: ogc:GeomLiteral, geom2: ogc:GeomLiteral ): xsd:boolean | inside |
| geof:eh-contains(geom1: ogc:GeomLiteral, geom2: ogc:GeomLiteral ): xsd:boolean | contains |

## Requirements for RCC8 Relation Family

This clause establishes requirements for the RCC8 relation family.

Implementations shall support the query functions geof:rcc8-eq, geof:rcc8-dc, geof:rcc8-ec, geof:rcc8-po, geof:rcc8-tppi, geof:rcc8-tpp, geof:rcc8-ntpp, geof:rcc8-nttpi.

/req/geometryTopologyExtension/RCC8QueryFunctions

Boolean query functions defined for the RCC8 relation family are shown in Table 7 below. Each function accepts two arguments (geom1 and geom2) of the geometry literal serialization type specified by serialization and version. Each function returns an xsd:boolean value of true if the specified relation exists between geom1 and geom2 and returns false otherwise. In each case, the spatial reference system of geom1 is used for spatial calculations. Relations identified in Table 7 refer to those defined in Table 3.

- -- RCC8 Query Functions

| Query Function | Relation Tested |
| --- | --- |
| geof:rcc8-eq(geom1: ogc:GeomLiteral, geom2: ogc:GeomLiteral ): xsd:boolean | equals |
| geof:rcc8-dc(geom1: ogc:GeomLiteral, geom2: ogc:GeomLiteral ): xsd:boolean | disconnected |
| geof:rcc8-ec(geom1: ogc:GeomLiteral, geom2: ogc:GeomLiteral ): xsd:boolean | externally connected |
| geof:rcc8-po(geom1: ogc:GeomLiteral, geom2: ogc:GeomLiteral ): xsd:boolean | partially overlapping |
| geof:rcc8-tppi(geom1: ogc:GeomLiteral, geom2: ogc:GeomLiteral ): xsd:boolean | tangential proper part inverse |
| geof:rcc8-tpp(geom1: ogc:GeomLiteral, geom2: ogc:GeomLiteral ): xsd:Boolean | tangential proper part |
| geof:rcc8-ntpp(geom1: ogc:GeomLiteral, geom2: ogc:GeomLiteral ): xsd:boolean | non-tangential proper part |
| geof:rcc8-ntppi(geom1: ogc:GeomLiteral, geom2: ogc:GeomLiteral ): xsd:boolean | non-tangential proper part inverse |

# Query Rewrite Extension (relation_family, serialization, version)

This clause establishes the Query Rewrite Extension (relation_family, serialization, version) parameterized requirements class, with URI /req/queryRewriteExtension, which has a single corresponding conformance class Query Rewrite Extension (relation_family, serialization, version), with URI /conf/queryRewriteExtension. This requirements class defines a set of query transformation rules that are used to expand a triple pattern involving a direct spatial predicate into a series of triple patterns and an invocation of the corresponding Boolean query function.

The following RIF rule is used as a template to describe query transformation rules in the remainder of this clause. ogc:relation is used as a placeholder for the spatial relation URIs defined in Clause 7, and ogc:function is used as a placeholder for the spatial functions defined in Clause 9.

Forall ?f1 ?f2 ?g1 ?g2 ?g1Serial ?g2Serial

(?f1[ogc:relation->?f2] :-

Or(

And

# feature – feature rule

(?f1[geo:defaultGeometry->?g1]

?f2[geo:defaultGeometry->?g2]

?g1[ogc:asGeomLiteral->?g1Serial]

?g2[ogc:asGeomLiteral->?g2Serial]

External(ogc:function (?g1Serial,?g2Serial)))

And

# feature – geometry rule

(?f1[geo:defaultGeometry->?g1]

?g1[ogc:asGeomLiteral->?g1Serial]

?f2[ogc:asGeomLiteral->?g2Serial]

External(ogc:function (?g1Serial,?g2Serial)))

And

# geometry - feature rule

(?f2[geo:defaultGeometry->?g2]

?f1[ogc:asGeomLiteral->?g1Serial]

?g2[ogc:asGeomLiteral->?g2Serial]

External(ogc:function (?g1Serial,?g2Serial)))

And

# geometry - geometry rule

(?f1[ogc:asGeomLiteral->?g1Serial]

?f2[ogc:asGeomLiteral->?g2Serial]

External(ogc:function (?g1Serial,?g2Serial)))

)

)

## Requirements for Simple Features Relation Family

This clause defines requirements for the Simple Features relation family. Table 8 specifies the function and property substitutions for each query transformation rule in the Simple Features relation family.

Implementations shall support the query rewrite rules geor:sf-equals, geor:sf-disjoint, geor:sf-intersects, geor:sf-touches, geor:sf-crosses, geor:sf-within, geor:sf-contains, geor:sf-overlaps.

/req/queryRewriteExtension/SFQueryRewrite

- -- Simple Features Query Transformation Rules

| Rule | ogc:relation | ogc:function |
| --- | --- | --- |
| geor:sf-equals | geo:sf-equals | geof:sf-equals |
| geor:sf-disjoint | geo:sf-disjoint | geof:sf-disjoint |
| geor:sf-intersects | geo:sf-intersects | geof:sf-intersects |
| geor:sf-touches | geo:sf-touches | geof:sf-touches |
| geor:sf-crosses | geo:sf-crosses | geof:sf-crosses |
| geor:sf-within | geo:sf-within | geof:sf-within |
| geor:sf-contains | geo:sf-contains | geof:sf-contains |
| geor:sf-overlaps | geo:sf-overlaps | geof:sf-overlaps |

## Requirements for Egenhofer Relation Family

This clause defines requirements for the Egehofer relation family. Table 9 specifies the function and property substitutions for each query transformation rule in the Egenhofer relation family.

Implementations shall support the query rewrite rules geor:eh-equals, geor:eh-disjoint, geor:eh-meet, geor:eh-overlap, geor:eh-covers, geor:eh-coveredBy, geor:eh-inside, geor:eh-contains.

/req/queryRewriteExtension/EHQueryRewrite

- -- Egehnofer Query Transformation Rules

| Rule | ogc:relation | ogc:function |
| --- | --- | --- |
| geor:eh-equals | geo:eh-equals | geof:eh-equals |
| geor:eh-disjoint | geo:eh-disjoint | geof:eh-disjoint |
| geor:eh-meet | geo:eh-meet | geof:eh-meet |
| geor:eh-overlap | geo:eh-overlap | geof:eh-overlap |
| geor:eh-covers | geo:eh-covers | geof:eh-covers |
| geor:eh-coveredBy | geo:eh-coveredBy | geof:eh-coveredBy |
| geor:eh-inside | geo:eh-inside | geof:eh-inside |
| geor:eh-contains | geo:eh-contains | geof:eh-contains |

## Requirements for RCC8 Relation Family

This clause defines requirements for the RCC8 relation family. Table 10 specifies the function and property substitutions for each query transformation rule in the RCC8 relation family.

Implementations shall support the query rewrite rules geor:rcc8-eq, geor:rcc8-dc, geor:rcc8-ec, geor:rcc8-po, geor:rcc8-tppi, geor:rcc8-tpp, geor:rcc8-ntpp, geor:rcc8-ntppi.

/req/queryRewriteExtension/RCC8QueryRewrite

- -- RCC8 Query Transformation Rules

| Rule | ogc:relation | ogc:function |
| --- | --- | --- |
| geor:rcc8-eq | geo:rcc8-eq | geof:rcc8-eq |
| geor:rcc8-dc | geo:rcc8-dc | geof:rcc8-dc |
| geor:rcc8-ec | geo:rcc8-ec | geof:rcc8-ec |
| geor:rcc8-po | geo:rcc8-po | geof:rcc8-po |
| geor:rcc8-tppi | geo:rcc8-tppi | geof:rcc8-tppi |
| geor:rcc8-tpp | geo:rcc8-tpp | geof:rcc8-tpp |
| geor:rcc8-ntpp | geo:rcc8-ntpp | geof:rcc8-ntpp |
| geor:rcc8-ntppi | geo:rcc8-ntppi | geof:rcc8-ntppi |

# Future Work

Many future extensions of this standard are possible. Obvious extensions are to define new conformance classes for other standard serializations of geometry data (e.g. KML, GeoJSON). In addition, significant work remains in developing vocabularies for spatial data, and expanding the GeoSPARQL vocabularies with OWL axioms to aid in logical spatial reasoning would be a valuable contribution. There are also large amounts of existing feature data represented either in a GML file (or similar serialization) or in a datastore supporting the general feature model. It would be beneficial to develop standard processes for converting (or virtually converting and exposing) this data to RDF.

(normative)

Abstract Test Suite

Conformance Class: Core

Conformance Class URI: /conf/core

/conf/core/SPARQL

Requirement: /req/core/SPARQL
Implementations shall support the SPARQL Protocol for RDF [W3C SPARQL PROTOCOL] and the SPARQL Query Results XML Format [W3C SPARQL RESULT FORMAT].

a.)	Test purpose: check conformance with this requirement

b.)	Test method: verify that the implementation accepts SPARQL queries and returns results in the correct format according to the SPARQL Protocol for RDF and SPARQL Query Results XML Format W3C specifications.

c.)	Reference: Clause 6.1 Req 1

d.)	Test Type: Capabilities

/conf/core/SpatialObjectClass

Requirement: /req/core/SpatialObjectClass
Implementations shall support transitivity of rdfs:subClassOf so that all feature and geometry objects subtype from the root class geo:SpatialObject.

a.)	Test purpose: check conformance with this requirement

b.)	Test method: verify that queries testing transitivity of rdfs:subClassOf for feature and geometry objects return the correct result on a test dataset.

c.)	Reference: Clause 6.2.1 Req 2

d.)	Test Type: Capabilities

/conf/core/FeatureClass

Requirement: /req/core/FeatureClass
Implementations shall support transitivity of rdfs:subClassOf so that all feature objects subtype from the class geo:Feature.

a.)	Test purpose: check conformance with this requirement

b.)	Test method: verify that a queries testing transitivity of rdfs:subClassOf for feature objects return the correct result on a test dataset.

c.)	Reference: Clause 6.2.2 Req 3

d.)	Test Type: Capabilities

Conformance Class: Topology Vocabulary Extension (relation_family)

Conformance Class URI: /conf/topologyVocabExtension

relation_family = Simple Features

/conf/topologyVocabExtension/SFSpatialRelations

Requirement: /req/topologyVocabExtension/SFSpatialRelations
Implementations shall allow the properties geo:sf-equals, geo:sf-disjoint, geo:sf-intersects, geo:sf-touches, geo:sf-crosses, geo:sf-within, geo:sf-contains, geo:sf-overlaps to be used directly in SPARQL triple patterns to test for existence of asserted binary spatial relations between instances of geo:SpatialObject.

a.)	Test purpose: check conformance with this requirement

b.)	Test method: Verify that queries involving these properties return the correct result for a test dataset.

c.)	Reference: Clause 7.2 Req 4

d.)	Test Type: Capabilities

/conf/topologyVocabExtension/SFSpatialRelationDefs

Requirement: /req/topologyVocabExtension/SFSpatialRelationDefs
Each of the properties referenced in Req 4 shall have rdfs:domain geo:SpatialObject, rdfs:range geo:SpatialObject, rdf:type rdf:Propery, and rdf:type owl:ObjectProperty.

a.)	Test purpose: check conformance with this requirement

b.)	Test method: Verify that queries involving these properties return the correct result for a test dataset.

c.)	Reference: Clause 7.2 Req 5

d.)	Test Type: Capabilities

relation_family = Egenhofer

/conf/topologyVocabExtension/EHSpatialRelations

Requirement: /req/topologyVocabExtension/EHSpatialRelations
Implementations shall allow the properties geo:eh-equals, geo:eh-disjoint, geo:eh-meet, geo:eh-overlap, geo:eh-covers, geo:eh-coveredBy, geo:eh-inside, geo:eh-contains to be used directly in SPARQL triple patterns to test for existence of asserted binary spatial relations between instances of geo:SpatialObject.

a.)	Test purpose: check conformance with this requirement

b.)	Test method: Verify that queries involving these properties return the correct result for a test dataset.

c.)	Reference: Clause 7.3 Req 6

d.)	Test Type: Capabilities

/conf/topologyVocabExtension/EHSpatialRelationDefs

Requirement: /req/topologyVocabExtension/EHSpatialRelationDefs
Each of the properties referenced in Req 6 shall have rdfs:domain geo:SpatialObject, rdfs:range geo:SpatialObject, rdf:type rdf:Propery, and rdf:type owl:ObjectProperty.

a.)	Test purpose: check conformance with this requirement

b.)	Test method: Verify that queries involving these properties return the correct result for a test dataset.

c.)	Reference: Clause 7.3 Req 7

d.)	Test Type: Capabilities

relation_family = RCC8

/conf/topologyVocabExtension/RCC8SpatialRelations

Requirement: /req/topologyVocabExtension/RCC8SpatialRelations
Implementations shall allow the properties geo:rcc8-eq, geo:rcc8-dc, geo:rcc8-ec, geo:rcc8-po, geo:rcc8-tppi, geo:rcc8-tpp, geo:rcc8-ntpp, geo:rcc8-ntppi to be used directly in SPARQL triple patterns to test for existence of asserted binary spatial relations between instances of geo:SpatialObject.

a.)	Test purpose: check conformance with this requirement

b.)	Test method: Verify that queries involving these properties return the correct result for a test dataset.

c.)	Reference: Clause 7.4 Req 8

d.)	Test Type: Capabilities

/conf/topologyVocabExtension/RCC8SpatialRelationDefs

Requirement: /req/topologyVocabExtension/RCC8SpatialRelationDefs
Each of the properties referenced in Req 8 shall have rdfs:domain geo:SpatialObject, rdfs:range geo:SpatialObject, rdf:type rdf:Propery, and rdf:type owl:ObjectProperty.

a.)	Test purpose: check conformance with this requirement

b.)	Test method: Verify that queries involving these properties return the correct result for a test dataset.

c.)	Reference: Clause 7.4 Req 9

d.)	Test Type: Capabilities

Conformance Class: Geometry Extension (serialization, version)

Conformance Class URI: /conf/geometryExtension

Tests for all Serializations

/conf/geometryExtension/GeometryClass

Requirement: /req/geometryExtension/GeometryClass
Implementations shall support transitivity of rdfs:subClassOf so that all feature objects subtype from the class geo:Geometry.

a.)	Test purpose: check conformance with this requirement

b.)	Test method: verify that a queries testing transitivity of rdfs:subClassOf for geometry objects return the correct result on a test dataset.

c.)	Reference: Clause 8.2 Req 10

d.)	Test Type: Capabilities

/conf/geometryExtension/FeatureProperties

Requirement: /req/geometryExtension/FeatureProperties
Implementations shall allow the properties geo:hasGeometry and geo:defaultGeometry to be used directly in SPARQL triple patterns to retrieve information about instances of geo:Feature.

a.)	Test purpose: check conformance with this requirement

b.)	Test method: Verify that queries involving these properties return the correct result for a test dataset.

c.)	Reference: Clause 8.3 Req 11

d.)	Test Type: Capabilities

/conf/geometryExtension/GeometryProperties

Requirement: /req/geometryExtension/GeometryProperties
Implementations shall allow the properties geo:dimension, geo:coordinateDimension, geo:spatialDimension, geo:isEmpty, geo:isSimple and geo:is3D to be used directly in SPARQL triple patterns to retrieve information about instances of geo:Geometry.

a.)	Test purpose: check conformance with this requirement

b.)	Test method: Verify that queries involving these properties return the correct result for a test dataset.

c.)	Reference: Clause 8.4 Req 12

d.)	Test Type: Capabilities

/conf/geometryExtension/QueryFunctions

Requirement: /req/geometryExtension/QueryFunctions
Compliant implementations shall support the SPARQL functions geof:distance, geof:buffer, geof:convexHull, geof:intersection, geof:union, geof:difference, geof:symDifference, geof:envelope and geof:boundary, consistent with the serialization used.

a.)	Test purpose: check conformance with this requirement

b.)	Test method: Verify that a set of SPARQL queries involving each of the following functions returns the correct result for a test dataset when using the specified serialization and version: geof:distance, geof:buffer, geof:convexHull, geof:intersection, geof:union, geof:difference, geof:symDifference, geof:envelope and geof:boundary.

c.)	Reference: Clause 8.7 Req 24

d.)	Test Type: Capabilities

serialization = WKT

/conf/geometryExtension/WKTGeometyTypes

Requirement: /req/geometryExtension/WKTGeometyTypes
Implementations shall support transitivity of rdfs:subClassOf for an RDFS/OWL class hierarchy of geometry types consistent with the one in the specified version of Simple Features.

a.)	Test purpose: check conformance with this requirement

b.)	Test method: verify that a queries testing transitivity of rdfs:subClassOf for geometry objects return the correct result on a test dataset for the appropriate geometry class hierarchy.

c.)	Reference: Clause 8.5.1 Req 13

d.)	Test Type: Capabilities

/conf/geometryExtension/WKTLiteral

Requirement: /req/geometryExtension/WKTLiteral
All RDFS Literals of type WKTLiteral shall consist of an optional URI identifying the coordinate reference system followed by Simple Features Well Known Text (WKT) describing a geometric value.

a.)	Test purpose: check conformance with this requirement

b.)	Test method: verify that queries involving WKTLiteral values return the correct result for a test dataset.

c.)	Reference: Clause 8.5.2 Req 14

d.)	Test Type: Capabilities

/conf/geometryExtension/WKTLiteralDefaultSRS

Requirement: /req/geometryExtension/WKTLiteralDefaultSRS
The URI <http://www.opengis.net/def/crs/OGC/1.3/CRS84> shall be used to denote the spatial reference system for WKTLiterals that do not specify an explicit spatial reference system URI.

a.)	Test purpose: check conformance with this requirement

b.)	Test method: verify that queries involving WKTLiteral values without an explicit encoded spatial reference system URI return the correct result for a test dataset.

c.)	Reference: Clause 8.5.2 Req 15

d.)	Test Type: Capabilities

/conf/geometryExtension/WKTAxisOrder

Requirement: /req/geometryExtension/WKTAxisOrder
Coordinate tuples within WKTLiterals shall be interpreted using the axis order defined in the spatial reference system used.

a.)	Test purpose: check conformance with this requirement

b.)	Test method: verify that queries involving WKTLiteral values return the correct result for a test dataset.

c.)	Reference: Clause 8.5.2 Req 16

d.)	Test Type: Capabilities

/conf/geometryExtension/WKTLiteralEmpty

Requirement: /req/geometryExtension/WKTLiteralEmpty
An empty RDFS Literal of type WKTLiteral shall be interpreted as an empty geometry.

a.)	Test purpose: check conformance with this requirement

b.)	Test method: verify that queries involving empty WKTLiteral values return the correct result for a test dataset.

c.)	Reference: Clause 8.5.2 Req 17

d.)	Test Type: Capabilities

/conf/geometryExtension/GeometryAsWKTLiteral

Requirement: /req/geometryExtension/GeometryAsWKTLiteral
Implementations shall allow the RDF property geo:asWKT to be used directly in GeoSPARQL triple patterns to retrieve a WKTLiteral for elements of type geo:Geometry.

a.)	Test purpose: check conformance with this requirement

b.)	Test method: verify that queries involving the geo:asWKT property return the correct result for a test dataset.

c.)	Reference: Clause 8.5.3 Req 18

d.)	Test Type: Capabilities

serialization = GML

/conf/geometryExtension/GMLGeometyTypes

Requirement: /req/geometryExtension/GMLGeometyTypes
Implementations shall support transitivity of rdfs:subClassOf for an RDFS/OWL class hierarchy of geometry types consistent with the GML schema that implements GM_Object using the specified version of GML.

a.)	Test purpose: check conformance with this requirement

b.)	Test method: verify that a queries testing transitivity of rdfs:subClassOf for geometry objects return the correct result on a test dataset for the appropriate geometry class hierarchy.

c.)	Reference: Clause 8.6.1 Req 19

d.)	Test Type: Capabilities

/conf/geometryExtension/GMLLiteral

Requirement: /req/geometryExtension/GMLLiteral
All GMLLiterals shall consist of a valid element from the GML schema that implements a subtype of GM_Object.

a.)	Test purpose: check conformance with this requirement

b.)	Test method: verify that queries involving GMLLiteral values return the correct result for a test dataset.

c.)	Reference: Clause 8.6.1 Req 20

d.)	Test Type: Capabilities

/conf/geometryExtension/GMLLiteralEmpty

Requirement: /req/geometryExtension/GMLLiteralEmpty
An empty GMLLiteral shall be interpreted as an empty geometry.

a.)	Test purpose: check conformance with this requirement

b.)	Test method: verify that queries involving empty GMLLiteral values return the correct result for a test dataset.

c.)	Reference: Clause 8.6.1 Req 21

d.)	Test Type: Capabilities

/conf/geometryExtension/GMLProfile

Requirement: /req/geometryExtension/GMLProfile
Implementations shall document supported GML profiles.

a.)	Test purpose: check conformance with this requirement

b.)	Test method: Examine the implementation’s documentation to verify that the supported GML profiles are documented.

c.)	Reference: Clause 8.6.1 Req 22

d.)	Test Type: Documentation

/conf/geometryExtension/GeometryAsGMLLiteral

Requirement: /req/geometryExtension/GeometryAsGMLLiteral
Implementations shall allow the RDF property geo:asGML to be used directly in GeoSPARQL triple patterns to retrieve a GMLLiteral for elements of type geo:Geometry.

a.)	Test purpose: check conformance with this requirement

b.)	Test method: verify that queries involving the geo:asGML property return the correct result for a test dataset.

c.)	Reference: Clause 8.6.3 Req 23

d.)	Test Type: Capabilities

Conformance Class: Geometry Topology Extension (relation_family, serialization, version)

Conformance Class URI: /conf/geometryTopologyExtension

Tests for all relation families

/conf/geometryTopologyExtension/RelateQueryFunction

Requirement: /req/geometryTopologyExtension/RelateQueryFunction
Implementations shall support the query function geof:relate.

a.)	Test purpose: check conformance with this requirement

b.)	Test method: Verify that a set of SPARQL queries involving the geof:relate function returns the correct result for a test dataset when using the specified serialization and version.

c.)	Reference: Clause 9.2 Req 25

d.)	Test Type: Capabilities

relation_family = Simple Features

/conf/geometryTopologyExtension/SFQueryFunctions

Requirement: /req/geometryTopologyExtension/SFQueryFunctions
Implementations shall support the query functions geof:sf-equals, geof:sf-disjoint, geof:sf-intersects, geof:sf-touches, geof:sf-crosses, geof:sf-within, geof:sf-contains, geof:sf-overlaps.

a.)	Test purpose: check conformance with this requirement

b.)	Test method: Verify that a set of SPARQL queries involving each of the following functions returns the correct result for a test dataset when using the specified serialization and version: geof:sf-equals, geof:sf-disjoint, geof:sf-intersects, geof:sf-touches, geof:sf-crosses, geof:sf-within, geof:sf-contains, geof:sf-overlaps.

c.)	Reference: Clause 9.3 Req 26

d.)	Test Type: Capabilities

relation_family = Egenhofer

/conf/geometryTopologyExtension/EHQueryFunctions

Requirement: /req/geometryTopologyExtension/EHQueryFunctions
Implementations shall support the query functions geof:eh-equals, geof:eh-disjoint, geof:eh-meet, geof:eh-overlap, geof:eh-covers, geof:eh-coveredBy, geof:eh-inside, geof:eh-contains.

a.)	Test purpose: check conformance with this requirement

b.)	Test method: Verify that a set of SPARQL queries involving each of the following functions returns the correct result for a test dataset when using the specified serialization and version: geof:eh-equals, geof:eh-disjoint, geof:eh-meet, geof:eh-overlap, geof:eh-covers, geof:eh-coveredBy, geof:eh-inside, geof:eh-contains.

c.)	Reference: Clause 9.4 Req 27

d.)	Test Type: Capabilities

relation_family = RCC8

/conf/geometryTopologyExtension/RCC8QueryFunctions

Requirement: /req/geometryTopologyExtension/RCC8QueryFunctions
Implementations shall support the query functions geof:rcc8-eq, geof:rcc8-dc, geof:rcc8-ec, geof:rcc8-po, geof:rcc8-tppi, geof:rcc8-tpp, geof:rcc8-ntpp, geof:rcc8-nttpi.

a.)	Test purpose: check conformance with this requirement

b.)	Test method: Verify that a set of SPARQL queries involving each of the following functions returns the correct result for a test dataset when using the specified serialization and version: geof:rcc8-eq, geof:rcc8-dc, geof:rcc8-ec, geof:rcc8-po, geof:rcc8-tppi, geof:rcc8-tpp, geof:rcc8-ntpp, geof:rcc8-nttpi.

c.)	Reference: Clause 9.5 Req 28

d.)	Test Type: Capabilities

Conformance Class: Query Rewrite Extension (relation_family, serialization, version)

Conformance Class URI: /conf/queryRewriteExtension

relation_family = Simple Features

/conf/queryRewriteExtension/SFQueryRewrite

Requirement: /req/queryRewriteExtension/SFQueryRewrite
Implementations shall support the query rewrite rules geor:sf-equals, geor:sf-disjoint, geor:sf-intersects, geor:sf-touches, geor:sf-crosses, geor:sf-within, geor:sf-contains, geor:sf-overlaps.

a.)	Test purpose: check conformance with this requirement

b.)	Test method: Verify that queries involving the following query transformation rules return the correct result for a test dataset when using the specified serialization and version: geor:sf-equals, geor:sf-disjoint, geor:sf-intersects, geor:sf-touches, geor:sf-crosses, geor:sf-within, geor:sf-contains and geor:sf-overlaps.

c.)	Reference: Clause 10.1 Req 29

d.)	Test Type: Capabilities

relation_family = Egenhofer

/conf/queryRewriteExtension/EHQueryRewrite

Requirement: /req/queryRewriteExtension/EHQueryRewrite
Implementations shall support the query rewrite rules geor:eh-equals, geor:eh-disjoint, geor:eh-meet, geor:eh-overlap, geor:eh-covers, geor:eh-coveredBy, geor:eh-inside, geor:eh-contains.

a.)	Test purpose: check conformance with this requirement

b.)	Test method: Verify that queries involving the following query transformation rules return the correct result for a test dataset when using the specified serialization and version: geor:eh-equals, geor:eh-disjoint, geor:eh-meet, geor:eh-overlap, geor:eh-covers, geor:eh-coveredBy, geor:eh-inside, geor:eh-contains.

c.)	Reference: Clause 10.2 Req 30

d.)	Test Type: Capabilities

relation_family = RCC8

/conf/queryRewriteExtension/RCC8QueryRewrite

Requirement: /req/queryRewriteExtension/RCC8QueryRewrite
Implementations shall support the query rewrite rules geor:rcc8-eq, geor:rcc8-dc, geor:rcc8-ec, geor:rcc8-po, geor:rcc8-tppi, geor:rcc8-tpp, geor:rcc8-ntpp, geor:rcc8-ntppi.

a.)	Test purpose: check conformance with this requirement

b.)	Test method: Verify that queries involving the following query transformation rules return the correct result for a test dataset when using the specified serialization and version: geor:rcc8-eq, geor:rcc8-dc, geor:rcc8-ec, geor:rcc8-po, geor:rcc8-tppi, geor:rcc8-tpp, geor:rcc8-ntpp, geor:rcc8-ntppi.

c.)	Reference: Clause 10.3 Req 31

d.)	Test Type: Capabilities

(informative)

Equivalent URIs in GeoSPARQL

In order to support the existing OGC URI scheme under the http://www.opengis.net/def/ namespace and to allow a minimum number of namespace prefixes for convenient SPARQL query specification, some duplication of URIs was necessary. Table 12 lists GeoSPARQL URIs that represent equivalent resources.

- Namespace Prefixes

| Prefix | Namespace |
| --- | --- |
| geo | http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/ |
| geoot | http://www.opengis.net/def/objectType/OGC-GeoSPARQL/1.0/ |
| geoft | http://www.opengis.net/def/featureType/OGC-GeoSPARQL/1.0/ |
| geogt | http://www.opengis.net/def/geometryType/OGC-GeoSPARQL/1.0/ |
| geop | http://www.opengis.net/def/property/OGC-GeoSPARQL/1.0/ |

- Equivalent Resource URIs

| http://www.opengis.net/def/ Namespace | http://www.opengis.net/ont/ Namespace |
| --- | --- |
| geoot:SpatialObject | geo:SpatialObject |
| geoft:Feature | geo:Feature |
| geogt:Geometry | geo:Geometry |
| geop:hasGeometry | geo:hasGeometry |
| geop:defaultGeometry | geo:defaultGeometry |
| geop:asWKT | geo:asWKT |
| geop:asGML | geo:asGML |
| geop:dimension | geo:dimension |
| geop:coordinateDimension | geo:coordinateDimension |
| geop:spatialDimension | geo:spatialDimension |
| geop:isEmpty | geo:isEmpty |
| geop:isSimple | geo:isSimple |
| geop:is3D | geo:is3D |
| geop:sf-equals | geo:sf-equals |
| geop:sf-disjoint | geo:sf-disjoint |
| geop:sf-intersects | geo:sf-intersects |
| geop:sf-touches | geo:sf-touches |
| geop:sf-crosses | geo:sf-crosses |
| geop:sf-within | geo:sf-within |
| geop:sf-contains | geo:sf-contains |
| geop:sf-overlaps | geo:sf-overlaps |
| geop:eh-equals | geo:eh-equals |
| geop:eh-disjoint | geo:eh-disjoint |
| geop:eh-meet | geo:eh-meet |
| geop:eh-overlap | geo:eh-overlap |
| geop:eh-covers | geo:eh-covers |
| geop:eh-coveredBy | geo:eh-coveredBy |
| geop:eh-inside | geo:eh-inside |
| geop:eh-contains | geo:eh-contains |
| geop:rcc8-eq | geo:rcc8-eq |
| geop:rcc8-dc | geo:rcc8-dc |
| geop:rcc8-ec | geo:rcc8-ec |
| geop:rcc8-po | geo:rcc8-po |
| geop:rcc8-tppi | geo:rcc8-tppi |
| geop:rcc8-tpp | geo:rcc8-tpp |
| geop:rcc8-ntpp | geo:rcc8-ntpp |
| geop:rcc8-ntppi | geo:rcc8-ntppi |

(informative)

GeoSPARQL Examples

Example Data

The following RDF/XML data encodes application-specific spatial data. The resulting spatial data is illustrated in Figure 3. The RDF statements define the feature class my:PlaceOfInterest, and two properties are created for associating geometries with features: my:hasExactGeometry and my:hasPointGeometry. my:hasExactGeometry is designated as the default geometry for the my:PlaceOfInterest feature class.

All the following examples use the parameter values relation_family = Simple Features, serialization = WKT, and version = 1.0.

: Illustration of spatial data

<rdf:RDF

xmlns:rdf="http://www.w3.org/1999/02/22-rdf-syntax-ns#"

xmlns:rdfs="http://www.w3.org/2000/01/rdf-schema#"

xmlns:owl="http://www.w3.org/2002/07/owl#"

xmlns:sfg="http://www.opengis.net/def/geometryType/OGC-SF/1.0/"

xmlns:geo="http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/"

xmlns:my="http://somewhere/ApplicationSchema#">

<!-- Integration with GeoSPARQL classes and properties -->

<rdfs:Class rdf:about=

"http://somewhere/ApplicationSchema#PlaceOfInterest">

<rdfs:subClassOf rdf:resource=

"http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/Feature"/>

</rdfs:Class>

<rdf:Property rdf:about=

"http://somewhere/ApplicationSchema#hasExactGeometry">

<rdfs:subPropertyOf rdf:resource=

"http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/hasGeometry"/>

<rdfs:subPropertyOf rdf:resource=

"http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/defaultGeometry"/>

</rdf:Property>

<rdf:Property rdf:about=

"http://somewhere/ApplicationSchema#hasPointGeometry">

<rdfs:subPropertyOf rdf:resource=

"http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/hasGeometry"/>

</rdf:Property>

<!-- Instance-level statements -->

<!-- A -->

<my:PlaceOfInterest rdf:about="http://somewhere/ApplicationSchema#A">

<my:hasExactGeometry rdf:resource=

"http://somewhere/ApplicationSchema#AExactGeom"/>

<my:hasPointGeometry rdf:resource=

"http://somewhere/ApplicationSchema#APointGeom"/>

</my:PlaceOfInterest>

<sfg:Polygon rdf:about="http://somewhere/ApplicationSchema#AExactGeom">

<geo:asWKT rdf:datatype=

"http://www.opengis.net/def/dataType/OGC-SF/1.0/WKTLiteral">

<![CDATA[

<http://www.opengis.net/def/crs/OGC/1.3/CRS84>

Polygon((-83.6 34.1, -83.2 34.1, -83.2 34.5,

-83.6 34.5, -83.6 34.1))

]]>

</geo:asWKT>

</sfg:Polygon>

<sfg:Point rdf:about="http://somewhere/ApplicationSchema#APointGeom">

<geo:asWKT rdf:datatype=

"http://www.opengis.net/def/dataType/OGC-SF/1.0/WKTLiteral">

<![CDATA[

<http://www.opengis.net/def/crs/OGC/1.3/CRS84>

Point(-83.4 34.3)

]]>

</geo:asWKT>

</sfg:Point>

<!-- B -->

<my:PlaceOfInterest rdf:about="http://somewhere/ApplicationSchema#B">

<my:hasExactGeometry rdf:resource=

"http://somewhere/ApplicationSchema#BExactGeom"/>

<my:hasPointGeometry rdf:resource=

"http://somewhere/ApplicationSchema#BPointGeom"/>

</my:PlaceOfInterest>

<sfg:Polygon rdf:about="http://somewhere/ApplicationSchema#BExactGeom">

<geo:asWKT rdf:datatype=

"http://www.opengis.net/def/dataType/OGC-SF/1.0/WKTLiteral">

<![CDATA[

<http://www.opengis.net/def/crs/OGC/1.3/CRS84>

Polygon((-83.6 34.1, -83.4 34.1, -83.4 34.3,

-83.6 34.3, -83.6 34.1))

]]>

</geo:asWKT>

</sfg:Polygon>

<sfg:Point rdf:about="http://somewhere/ApplicationSchema#BPointGeom">

<geo:asWKT rdf:datatype=

"http://www.opengis.net/def/dataType/OGC-SF/1.0/WKTLiteral">

<![CDATA[

<http://www.opengis.net/def/crs/OGC/1.3/CRS84>

Point(-83.5 34.2)

]]>

</geo:asWKT>

</sfg:Point>

<!-- C -->

<my:PlaceOfInterest rdf:about="http://somewhere/ApplicationSchema#C">

<my:hasExactGeometry rdf:resource=

"http://somewhere/ApplicationSchema#CExactGeom"/>

<my:hasPointGeometry rdf:resource=

"http://somewhere/ApplicationSchema#CPointGeom"/>

</my:PlaceOfInterest>

<sfg:Polygon rdf:about="http://somewhere/ApplicationSchema#CExactGeom">

<geo:asWKT rdf:datatype=

"http://www.opengis.net/def/dataType/OGC-SF/1.0/WKTLiteral">

<![CDATA[

<http://www.opengis.net/def/crs/OGC/1.3/CRS84>

Polygon((-83.2 34.3, -83.0 34.3, -83.0 34.5,

-83.2 34.5, -83.2 34.3))

]]>

</geo:asWKT>

</sfg:Polygon>

<sfg:Point rdf:about="http://somewhere/ApplicationSchema#CPointGeom">

<geo:asWKT rdf:datatype=

"http://www.opengis.net/def/dataType/OGC-SF/1.0/WKTLiteral">

<![CDATA[

<http://www.opengis.net/def/crs/OGC/1.3/CRS84>

Point(-83.1 34.4)

]]>

</geo:asWKT>

</sfg:Point>

<!-- D -->

<my:PlaceOfInterest rdf:about="http://somewhere/ApplicationSchema#D">

<my:hasExactGeometry rdf:resource=

"http://somewhere/ApplicationSchema#DExactGeom"/>

<my:hasPointGeometry rdf:resource=

"http://somewhere/ApplicationSchema#DPointGeom"/>

</my:PlaceOfInterest>

<sfg:Polygon rdf:about="http://somewhere/ApplicationSchema#DExactGeom">

<geo:asWKT rdf:datatype=

"http://www.opengis.net/def/dataType/OGC-SF/1.0/WKTLiteral">

<![CDATA[

<http://www.opengis.net/def/crs/OGC/1.3/CRS84>

Polygon((-83.3 34.0, -83.1 34.0, -83.1 34.2,

-83.3 34.2, -83.3 34.0))

]]>

</geo:asWKT>

</sfg:Polygon>

<sfg:Point rdf:about="http://somewhere/ApplicationSchema#DPointGeom">

<geo:asWKT rdf:datatype=

"http://www.opengis.net/def/dataType/OGC-SF/1.0/WKTLiteral">

<![CDATA[

<http://www.opengis.net/def/crs/OGC/1.3/CRS84>

Point(-83.2 34.1)

]]>

</geo:asWKT>

</sfg:Point>

<!-- E -->

<my:PlaceOfInterest rdf:about="http://somewhere/ApplicationSchema#E">

<my:hasExactGeometry rdf:resource=

"http://somewhere/ApplicationSchema#EExactGeom"/>

</my:PlaceOfInterest>

<sfg:LineString rdf:about=

"http://somewhere/ApplicationSchema#EExactGeom">

<geo:asWKT rdf:datatype=

"http://www.opengis.net/def/dataType/OGC-SF/1.0/WKTLiteral">

<![CDATA[

<http://www.opengis.net/def/crs/OGC/1.3/CRS84>

LineString((-83.4 34.0, -83.3 34.3))

]]>

</geo:asWKT>

</sfg:LineString>

<!-- F -->

<my:PlaceOfInterest rdf:about="http://somewhere/ApplicationSchema#F">

<my:hasExactGeometry rdf:resource=

"http://somewhere/ApplicationSchema#FExactGeom"/>

</my:PlaceOfInterest>

<sfg:Point rdf:about="http://somewhere/ApplicationSchema#FExactGeom">

<geo:asWKT rdf:datatype=

"http://www.opengis.net/def/dataType/OGC-SF/1.0/WKTLiteral">

<![CDATA[

<http://www.opengis.net/def/crs/OGC/1.3/CRS84>

Point(-83.4 34.0)

]]>

</geo:asWKT>

</sfg:Point>

</rdf:RDF>

Example Queries

This Section illustrates the use of GeoSPARQL functions through a series of example queries.

Example 1: Find all features that feature my:A contains, where spatial calculations are based on my:hasExactGeometry.

PREFIX my:  <http://somewhere/ApplicationSchema#>

PREFIX geo: <http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/>

PREFIX geof: 
  <http://www.opengis.net/def/queryLanguage/OGC-GeoSPARQL/1.0/function/>

SELECT ?f

WHERE { my:A my:hasExactGeometry ?aGeom .

?aGeom geo:asWKT ?aWKT .

?f my:hasExactGeometry ?fGeom .

?fGeom geo:asWKT ?fWKT .

FILTER (geof:sf-contains(?aWKT, ?fWKT) &&

!sameTerm(?aGeom, ?fGeom))

}

Result:

?f

my:B

my:F

Example 2: Find all features that are within a transient bounding box geometry, where spatial calculations are based on my:hasPointGeometry.

PREFIX my:  <http://somewhere/ApplicationSchema#>

PREFIX geo: <http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/>

PREFIX sfd: <http://www.opengis.net/def/dataType/OGC-SF/1.0/>

PREFIX geof:

<http://www.opengis.net/def/queryLanguage/OGC-GeoSPARQL/1.0/function/>

SELECT ?f

WHERE { ?f my:hasPointGeometry ?fGeom .

?fGeom geo:asWKT ?fWKT .

FILTER (geof:sf-within(?fWKT,

"<http://www.opengis.net/def/crs/OGC/1.3/CRS84>

Polygon ((-83.4 34.0, -83.1 34.0,

-83.1 34.2, -83.4 34.2,

-83.4 34.0))"^^sfd:WKTLiteral))

}

Result:

?f

my:D

Example 3: Find all features that touch the union of feature my:A and feature my:D, where computations are based on my:hasExactGeometry.

PREFIX my:  <http://somewhere/ApplicationSchema#>

PREFIX geo: <http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/>

PREFIX geof:

<http://www.opengis.net/def/queryLanguage/OGC-GeoSPARQL/1.0/function/>

SELECT ?f

WHERE { ?f my:hasExactGeometry ?fGeom .

?fGeom geo:asWKT ?fWKT .

my:A my:hasExactGeometry ?aGeom .

?aGeom geo:asWKT ?aWKT .

?my:D my:hasExactGeometry ?dGeom .

?dGeom geo:asWKT ?dWKT .

FILTER (geof:sf-touches(?fWKT,

geof:union(?aWKT, ?dWKT)))

}

Result:

?f

my:C

Example 4: Find the 3 closest features to feature my:C, where computations are based on my:hasExactGeometry.

PREFIX uom:  <http://www.opengis.net/def/uom/OGC/1.0/>

PREFIX my:   <http://somewhere/ApplicationSchema#>

PREFIX geo:  <http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/>

PREFIX geof:

<http://www.opengis.net/def/queryLanguage/OGC-GeoSPARQL/1.0/>

SELECT ?f

WHERE { my:C my:hasExactGeometry ?cGeom .

?cGeom geo:asWKT ?cWKT .

?f my:hasExactGeometry ?fGeom .

?fGeom geo:asWKT ?fWKT .

FILTER (?fGeom != ?cGeom) }

ORDER BY ASC (geof:distance(?cWKT, ?fWKT,

uom:metre))

LIMIT 3

Result:

?f

my:A

my:D

my:E

Example Rule Application

This section illustrates the application of a query rewrite rule to a GeoSPARQL query.

Example 5: Find all features or geometries that overlap feature my:A.

Original Query:

PREFIX geo:  <http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/>

SELECT ?f

WHERE { ?f geo:overlaps my:A }

Transformed Query (application of transformation rule geor:sf-overlaps):

PREFIX my:   <http://somewhere/ApplicationSchema#>

PREFIX geo: <http://www.opengis.net/ont/OGC-GeoSPARQL/1.0/>

PREFIX geof:

<http://www.opengis.net/def/queryLanguage/OGC-GeoSPARQL/1.0/function/>

SELECT ?f

WHERE { { # check for asserted statement

?f geo:sf-overalps my:A }

UNION

{ # feature – feature

?f geo:defaultGeometry ?fGeom .

?fGeom geo:asWKT ?fSerial .

my:A geo:defaultGeometry ?aGeom .

?aGeom geo:asWKT ?aSerial .

FILTER (geof:sf-overlaps(?fSerial, ?aSerial)) }

UNION

{ # feature – geometry

?f geo:defaultGeometry ?fGeom .

?fGeom geo:asWKT ?fSerial .

my:A geo:asWKT ?aSerial .

FILTER (geof:sf-overlaps(?fSerial, ?aSerial)) }

UNION

{ # geometry – feature

?f geo:asWKT ?fSerial .

my:A geo:defaultGeometry ?aGeom .

?aGeom geo:asWKT ?aSerial .

FILTER (geof:sf-overlaps(?fSerial, ?aSerial)) }

UNION

{ # geometry – geometry

?f geo:defaultGeometry ?fGeom .

?fGeom geo:asWKT ?fSerial .

my:A geo:defaultGeometry ?aGeom .

?aGeom geo:asWKT ?aSerial .

FILTER (geof:sf-overlaps(?fSerial, ?aSerial)) }

}

Result:

?f

my:D

my:DExactGeom

my:E

my:EExactGeom

Bibliography

[1]	Cohn, Anthony G., Brandon Bennett, John Gooday, Nicholas Mark Gotts: Qualitative Spatial Representation and Reasoning with the Region Connection Calculus. GeoInformatica, 1, 275–316, 1997.

[2]	Egenhofer Max, A Formal Definition of Binary Topological Relationships, Third International Conference on Foundations of Data Organization and Algorithms (FODO), Paris, France, W. Litwin and H. Schek (eds.), Lecture Notes in Computer Science, Vol. 367, Springer-Verlag, pp. 457-472, June 1989. available at http://www.spatial.maine.edu/~max/RC2.html

[3]	Egenhofer, Max and J. Herring Categorizing Binary Topological Relations Between Regions, Lines, and Points in Geographic Databases, Technical Report, Department of Surveying Engineering, University of Maine, 1990. (revised versions in NCGIA Technical Report 91-7 and NCGIA Technical Report 94-1)

[4]	Randell, D. A., Cui, Z. and Cohn, A. G.: A spatial logic based on regions and connection, Proc. 3rd Int. Conf. on Knowledge Representation and Reasoning, Morgan Kaufmann, San Mateo, pp. 165–176, 1992.

# Text boxes

A

B

D

C

E

F

Core

Topology Vocabulary Extension (relation_family)

Geometry Extension (serialization, version)

Geometry Topology Extension (serialization, version, relation_family)

Query Rewrite Extension (serialization, version, relation_family)