Open Geospatial Consortium	Document OGC 08-017

| CR-Form-v3 |
| --- |
| CHANGE REQUEST |
| ( | WCS | CR | ? | ( rev | - | ( Current version: | 1.1.2 |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |
| Proposed change affects: ( | AS |  | Impl Stand | X | Best Practices Paper |  | Other |  |
| Title: ( | WCS change request - Clarify "none" interpolation |
| Source: ( | Arliss Whiteside, WCS 1.2 SWG |
| Work item code: ( |  |  | Date: ( | 2008-02-12 |
| Category: ( | F | (Add needed information) |  |
|  | Use one of the following categories: F (Critical correction) A (corresponds to a correction in an earlier release) B (Addition of feature), C (Functional modification of feature) D (Editorial modification) |  |
| Reason for change: ( | WCS 1.1 defines “none” as an allowed value of the interpolation method type. However, it is not clear what this means and when it should be used. |
| Summary of change: ( | Modify the specification of the “none” allowed value of the interpolation method type to clarify its meaning and when it should be used. |
| Consequences if ( not approved: | Continued WCS confusion on how to use the “none” allowed value of the interpolation method type |
| Clauses affected: ( | 10.2.1.1, 10.2.1.2, H.3.1 |
| Other specs ( |  | Other core specifications ( |  |
| Affected: |  | Abstract specifications |  |
|  |  | Best Practices Papers |  |
| Supporting Doc. ( |  |
| Other comments: ( | This change request is to the current draft WCS version 1.1.2 [OGC 07-067r3]. I think this suggested change is backwards compatible. |
| Status ( |  |
| Disposition ( |  |

## Edit Tables 24 and 26 in Subclause 10.2.1 of the WCS specification as follows:

Table 24 — Parts of Output data structure

| Names a | Definition | Data type | Multiplicity and use |
| --- | --- | --- | --- |
| gridCRS GridCRS | Definition of Coordinate Reference System in which GetCoverage operation response shall be expressed | GridCRS data structure, see Annex F | Zero or one (optional) Include unless requesting ImageCRS or GridCRS of offered coverage d |
| format Format | Identifier of format in which GetCoverage operation response shall be encoded | CharacterString type b | One (mandatory) |
| store store | ”True” value asks server to store all components of the response coverage in a Web-accessible location, referenced by URL(s) in the GetCoverage response. “False” value asks server to return all components of the response coverage synchronously, bundled with the GetCoverage response. | Boolean type | Zero or one (optional) Default is false c |
| a See Table 1 of [OGC 06-121r3] for UML and XML naming conventions. b The format identifier value shall be among those listed under supportedFormats in the DescribeCoverage XML response. c This parameter should be included only when this parameter is supported by this server, as encoded in the OperationsMetadata section of the Capabilities document. d When this GridCRS is not included, the output coverage shall use the gml:ImageCRS or wcs:GridCRS of the offered coverage, normally with the origin at a different grid point. The client may thus omit this GridCRS in order to request no interpolation (use cases 1-5). Omitting this GridCRS requires output of exactly (some) offered grid points, so no interpolation is required to be performed by the WCS server. Alternately, the “nearest” interpolation method type may be applied by the server, to produce output grid points which are always at the same locations as offered grid points. When included, this wcs:GridCRS specifies the desired grid for the output coverage, including the desired grid spacings, one of many possible origin locations, optional rotation, and optional skewing (angle between the axes) in a base CRS. However, this wcs:GridCRS is NOT required or expected to specify the actual position of the origin in the GetCoverage operation output, so it shall not be interpreted as being different than the origin directly or indirectly specified by the BoundingBox in the DomainSubset. |

Table 26 — Parts of FieldSubset data structure

| Names a | Definition | Data type and value | Multiplicity and use |
| --- | --- | --- | --- |
| identifier Identifier | Name of requested field | Character string, not empty b | One (mandatory) |
| interpolationType InterpolationType | Spatial interpolation method to be used to resample values in this field | InterpolationMethodType, see Table H.3 c | Zero or one (optional) Include to request interpolation method other than default for this field |
| axisSubset AxisSubset | Desired keys in one Axis for one (vector) field | AxisSubset data structure, see Table 27 | Zero or more (optional) Include to request coverage values for only some of keys in an Axis defined for a (vector) field |
| a See Table 1 of [OGC 06-121r3] for UML and XML naming conventions. b This identifier shall be for a Field specified in the CoverageDescription, and shall be unique for this Coverage. c This interpolation method type shall be one that is identified for this Field in the CoverageDescription. When this parameter is omitted, the interpolation type used shall be the default interpolation method specified for this Field, if any. If the GridCRS is omitted in the Output data structure, thus requiring output of exactly offered grid points, the identified or default InterpolationType shall be either “none” or “nearest”. Any other value for the identified or default InterpolationType shall be detected as an error when that GridCRS is omitted. |

## Edit Subclause H.3.1 of the WCS specification as follows:

H.3.1	Interpolation methods contents

The InterpolationMethods data structure lists one or more spatial interpolation methods, which can each be used for interpolation of a range record field in a continuous grid coverage. The InterpolationMethods shall use the data structure described in Figure H.2 and specified in Tables H.1 through Table H.4.

Figure H.2 — Interpolation Methods class diagram

Table H.1 — Parts of the InterpolationMethods data structure

| Names a | Definition | Data type | Multiplicity and use |
| --- | --- | --- | --- |
| default Default | Spatial interpolation method used for this range field when client doesn’t specify one b | InterpolationMethod data structure, see Table H.6 | One (mandatory) |
| interpolationMethod InterpolationMethod | Another spatial Interpolation method that server can apply to this range field | InterpolationMethod data structure, see Table H.6 | Zero or more (optional) Include for each other method supported c |
| a See Table 1 of [OGC 06-121r3] for UML and XML naming conventions. b This default interpolation method should be the recommended or normal method for this coverage range field. c When the default interpolation method is “none”, no other methods should be listed. |

InterpolationMethods has a mandatory Default parameter that identifies the spatial interpolation method used for GetCoverage requests that don’t specify one to be used. InterpolationMethods may also have zero or more InterpolationMethod parameters whose values identify other spatial interpolation methods that the server may use for this coverage range field. However, when the default interpolation method is “none”, no other methods should be listed. When the only listed (default) interpolation method is “none”, clients may only retrieve subsets of this offered coverage in its offered CRS and with its offered resolution and grid positions. That is, the requested output grid points shall lie exactly at some offered grid points. In this case, no interpolation is required to be performed by a WCS server. Alternately, the “nearest” interpolation method type may be applied by the server, to produce output grid points which are always at the same locations as offered grid points.

Table H.2 — Parts of the InterpolationMethod data structure

| Names a | Definition | Data type and value | Multiplicity and use |
| --- | --- | --- | --- |
| Interpolation‌MethodType (anonymous) | Identifier of spatial interpolation method. | CodeList type One of the strings defined in Table H.3 | One (mandatory) |
| nullResistance nullResistance | How server handles null values when spatially interpolating values in this field | CodeList type One of the strings listed in Table H.4. | Zero or one (optional) Include when known |
| a See Table 1 of [OGC 06-121r3] for UML and XML naming conventions. |

For a continuous grid coverage, the normal spatial interpolation types are listed in Table H.3 and in the attached default InterpolationMethods.xml dictionary. Compared to ISO 19123, WCS does not distinguish linear from bilinear, quadratic from biquadratic, and cubic from bicubic interpolation. For WCS, the linear, quadratic, and cubic interpolation methods shall be applicable to coverages of any number of spatial dimensions. Servers may implement and list other interpolation methods, defined in dictionaries other than the default.

NOTE 1	The interpolation methods "lost area" and "barycentric" are not applicable to grid coverages, hence they are not included in this version of WCS.

Table H.3 — Normal spatial interpolation types

| Interpolation type identifier | Interpolation method | Description |
| --- | --- | --- |
| nearest | nearest neighbour | These are defined in ISO 19123 (Schema for Coverage Geometry and Functions), Annex B. |
| linear | bilinear a |  |
| quadratic | biquadratic a |  |
| cubic | bicubic a |  |
| none | none b | No interpolation is available; requests must be for exact grid point locations that are among the original grid point locations. |
| a ISO 19123 specifies two-dimensional bilinear, biquadratic, and bicubic interpolation types. When also interpolating in the elevation dimension of a 3D CRS, the 3D extensions of these interpolation types shall be used. b ISO 19123 does not mention no interpolation, except for a discrete (grid) coverage. The OGC has defined “none” to allow a server to tell clients that no interpolation of range field values is allowed, and allow a client to tell a server that no interpolation of range field values is requested. |

Each InterpolationMethod element has an optional nullResistance summarizing how the server treats null-valued points in interpolation. The normal values for this parameter are listed in Table H.4 and in the default InterpolationMethods.xml dictionary.

NOTE 2	These nullResistance values are sent from a server to a client, to summarize how the server treats null-valued points. These nullResistance values are NOT sent from a client to a server (to indicate how the client wants null-valued points treated).

Table H.4 — Effect of null values in spatial interpolation

| nullResistance | Description |
| --- | --- |
| full | Nulls in the input grid(s) have no effect on interpolated value; resampling uses only non-null valued cells. |
| none | Interpolated value is Null when any one input value is Null. |
| half | Interpolated value is Null when half or more input values are Null. |
| other | Resampling treats nulls differently than any method described above |

# Comments

Enter the AS or Implementation Specification Name and Number in this box. For example, WMS 1.1.1 or GML 3.0. Do not prefix the number with anything, i.e. do not use "OGC", "GSM" or "OGC" etc.

Enter the CR number here. This number is allocated by the OGC support team.

Enter the revision number of the CR here. If it is the first version, use a "-".

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X. AS = Abstract Specification, IS = Implementation Specification, Recom. Paper = Recommendation Paper, Other = DIPR/IPR, etc.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.

Enter the source of the CR. This is either (a) one or more OGC members or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

IF there is one, enter the work item code or issue code that is applicable to the change. These codes will relate to Work Items identified in a WBS associated with a particular OGC initiative. If there is no code, leave blank.

Enter the date on which the CR was last revised.

Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the TC Policies and Procedures".

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. essential correction).

Enter each the number of each clause which contains changes.

Enter an X in the box if any other specifications are affected by this change.

If known, list here the specifications which are affected or the CRs which are linked.

Explanation of Field: If there is associated documentation, such as an lengthy change request or new text for consideration, please reference the OGC document number and document title.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.

This is the status of the change request. For a new submission, please enter “NEW”. Other options as the change request is processed are: Assigned, Verified, Resolved, and Closed.

This field is used to assign the RWG decision for this Change Request. Options include: Deferred, Accepted, and Rejected.