Open Geospatial Consortium	OGC Doc 08-039

| CR-Form-v3 |
| --- |
| CHANGE REQUEST |
| ( | GML | CR | ? 08-136 | ( rev | - | ( Current version: | 3.2.1 | ( |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |
| Proposed change affects: ( | AS |  | Imp Spec | x | Best Practices Paper |  | Other |  |
| Title: ( | GML CR defaultStyle.xsd is broken |
| Source: ( | GMLJP2 V1.1 SWG |
| Work item code: ( |  |  | Date: ( | 2008-08-27 |
| Category: ( | F |  |  |
|  | Use one of the following categories: F (Critical correction) A (corresponds to a correction in an earlier release) B (Addition of feature), C (Functional modification of feature) D (Editorial modification) Detailed explanations of the above categories can be found in the TC Policies and Procedures. |  |
| Reason for change: ( | Requirements of GMLJP2 V1.1 SWG |
| Summary of change: ( | GML JP2 Annotation.xsd depends on defaultStyle.xsd, which is not included in gml.xsd and does not validate. |
| Consequences if ( not approved: | Annotation.xsd cannot be used in GMLJP2 V1.1 The following sentence in Clause 20.6 is currently misleading given that defaultStyle.xsd is not included: “The schema document gml.xsd is an exhaustive superset following the latter approach” |
| Clauses affected: ( | gml.xsd |
| Other specs ( |  | Other core specifications ( |  |
| Affected: |  | Abstract specifications |  |
|  |  | Best Practices Document |  |
| Supporting Doc. ( |  |
| Other comments: ( |  |
| Status ( |  |
| Disposition ( |  |

gml.xsd

GMLJP2 V1.1 SWG suggests including defaultStyle.xsd in gml.xsd and validating smil schemas so that defaultStyle.xsd is valid. Error reports have already been sent to W3C regarding smil schemas:

The information you submitted has been sent to the W3C Webmaster
Thank you for your interest in our web site

Email:                           dburggraf@galdosinc.com
Originating URL:                 http://www.w3.org/2001/SMIL20/xml-mod.xsd
What's wrong:                    XML Parsing Error: prefix must not be bound to one of the reserved namespace names Location: http://www.w3.org/2001/SMIL20/xml-mod.xsd Line Number 1, Column 1:
What it should be:               xmlns:x --> xmlns:xml   plus many other corrections. All corrections have been made to the smil schemas here:  http://schemas.opengis.net/gml/3.1.1/smil/ 
Comments:                        Please correct schemas as in the link above

# Comments

Enter the AS or Implementation Specification Name and Number in this box. For example, WMS 1.1.1 or GML 3.0. Do not prefix the number with anything, i.e. do not use "OGC", "GSM" or "OGC" etc.

Enter the CR number here. This number is allocated by the OGC support team.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR will be applied if it is approved. Make sure that the more recent version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to http://www.opengeospatial.org.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X. AS = Abstract Specification, IS = Implementation Specification, BPD – Best Practices Document, Other = DIPR/IPR, etc.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.

Enter the source of the CR. This is either (a) one or more OGC members or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

IF there is one, enter the work item code or issue code that is applicable to the change. These codes will relate to Work Items identified in a WBS associated with a particular OGC initiative. If there is no code, leave blank.

Enter the date on which the CR was last revised.

Enter a single letter corresponding to the most appropriate category listed below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. essential correction).

Enter each the number of each clause which contains changes.

Enter an X in the box if any other specifications are affected by this change.

If known, list here the specification or best practices documents that are affected or the CRs which are linked.

Explanation of Field: If there is associated documentation, such as an lengthy change request or new text for consideration, please reference the OGC document number and document title.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.

This is the status of the change request. For a new submission, please enter “NEW”. Other options as the change request is processed are: Assigned, Verified, Resolved, and Closed.

This field is used to assign the RWG decision for this Change Request. Options include: Deferred, Accepted, and Rejected.