Open Geospatial Consortium	OGC Doc 08-195

| CR-Form-v3 |
| --- |
| CHANGE REQUEST |
| ( | SOS | CR | 08-195 | ( rev | - | ( Current version: | 06-009r6 | ( |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |
| Proposed change affects: ( | AS |  | Imp Spec | X | Best Practices Paper |  | Other |  |
| Title: ( | Add Time Parameter to DescribeSensor operation |
| Source: ( | University of Muenster, Institute for Geoinformatics (IfGI) |
| Work item code: ( |  |  | Date: ( | 2008-11-24 |
| Category: ( | C |  |  |
|  | Use one of the following categories: F (Critical correction) A (corresponds to a correction in an earlier release) B (Addition of feature), C (Functional modification of feature) D (Editorial modification) Detailed explanations of the above categories can be found in the TC Policies and Procedures. |  |
| Reason for change: ( | Currently, the SOS does not serve a mechanism to query sensor descriptions for a specific time. This causes problems for instance in case of mobile sensors whose properties change over the course of time. |
| Summary of change: ( | Add Time parameter to DescribeSensor operation. |
| Consequences if ( not approved: | Lacking support for sensors that have dynamic properties which change during the course of time. |
| Clauses affected: ( | 8.3 |
| Other specs ( |  | Other core specifications ( |  |
| Affected: |  | Abstract specifications |  |
|  |  | Best Practices Document |  |
| Supporting Doc. ( |  |
| Other comments: ( |  |
| Status ( |  |
| Disposition ( |  |

Edit sub clause 8.3 as follows:

## 8.3	DescribeSensor (mandatory)

### 8.3.1	Introduction

One method of obtaining metadata that describes the characteristics of an observation procedure (sensor or sensor constellation) is to retrieve it from a catalog.  However, a catalog may only contain high-level information about the observable properties, locations, contact information, etc.  Due to the possibly voluminous amounts of sensor related metadata, the “describe” operations support retrieval of the highest level of detail about the platforms and sensors associated with an SOS.

DescribeSensor is designed to request detailed sensor metadata.  Likewise, the response to a GetCapabilities request could provide a list of sensors associated with an SOS.  Sensors are devices for the measurement of physical quantities.  Both Sensor Model Language (SensorML) and Transducer Markup Language (TML) provide a detailed definition of a sensor for In-situ and Remote Sensors specification.

For the purpose of this discussion, there are two main kinds of sensor, in-situ and remote-dynamic.  The DescribeSensor operation is useful for obtaining detailed information of sensor characteristics encoded in either SensorML or TML.  The sensor characteristics can include lists and definitions of observables supported by the sensor. The SensorML and TML specifications detail the response model for the DescribeSensor operation.

### 8.3.2	Request

Figure 8-3 describes the syntax of the SOS DescribeSensor operation.

# Figure 8-3 DescribeSensor Request

# Table 3 Attributes of DescribeSensor Request

| Name a | Definition | Data type and values | Multiplicity and use |
| --- | --- | --- | --- |
| outputFormat | The outputFormat attribute specifies the desired output format of the DescribeSensor operation. This can be a MimeType or QName for example. This is text/xml;subtype=”sensorML/1.0.0” for SensorML or text/xml;subtype=”TML/1.0” for TML. | ows:MimeType | Required |
| procedure | The procedure parameter specifies the sensor for which the description is to be returned. This value must match the value advertised in the xlink:href attribute of a procedure element advertised in the SOS GetCapabilities response. | anyURI | One (mandatory) |
| Time | The Time parameter can be used to specify a period or position in time for which the sensor description(s) shall be requested. | ogc:temporalOps | One (optional) |
| service | Service type identifier | SOS | One (mandatory) |
| version | Specification version for operation | Supported version of SOS. | One (mandatory) |
| a The name capitalization rules being used here are specified in Subclause 11.6.2 of [OGC 06-121r3]. |

### 8.3.3	Response

A list of SensorML or TML documents describing the sensor system in its different states for the requested time frame.

# Comments

Enter the AS or Implementation Specification Name and Number in this box. For example, WMS 1.1.1 or GML 3.0. Do not prefix the number with anything, i.e. do not use "OGC", "GSM" or "OGC" etc.

Enter the CR number here. This number is allocated by the OGC support team.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR will be applied if it is approved. Make sure that the more recent version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to http://www.opengeospatial.org.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X. AS = Abstract Specification, IS = Implementation Specification, BPD – Best Practices Document, Other = DIPR/IPR, etc.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.

Enter the source of the CR. This is either (a) one or more OGC members or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

IF there is one, enter the work item code or issue code that is applicable to the change. These codes will relate to Work Items identified in a WBS associated with a particular OGC initiative. If there is no code, leave blank.

Enter the date on which the CR was last revised.

Enter a single letter corresponding to the most appropriate category listed below.

Enter text which explains why the change is necessary.

Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. essential correction).

Enter each the number of each clause which contains changes.

Enter an X in the box if any other specifications are affected by this change.

If known, list here the specification or best practices documents that are affected or the CRs which are linked.

Explanation of Field: If there is associated documentation, such as an lengthy change request or new text for consideration, please reference the OGC document number and document title.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.

This is the status of the change request. For a new submission, please enter “NEW”. Other options as the change request is processed are: Assigned, Verified, Resolved, and Closed.

This field is used to assign the RWG decision for this Change Request. Options include: Deferred, Accepted, and Rejected.