Open Geospatial Consortium	Document OGC 08-166r1

| CR-Form-v3 |
| --- |
| CHANGE REQUEST |
| ( | WCS | CR | ? | ( rev | - | ( Current version: | 1.1 corr. 2 |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |
| Proposed change affects: ( | AS |  | Imp Spec | X | Best Practices Paper |  | Other |  |
| Title: ( | WCS change request - Expand output coverage metadata |
| Source: ( | Arliss Whiteside, WCS 1.2 SWG |
| Work item code: ( |  |  | Date: ( | 2008-12-20 |
| Category: ( | C |  |  |
|  | Use one of the following categories: F (Critical correction) A (corresponds to a correction in an earlier release) B (Addition of feature), C (Functional modification of feature) D (Editorial modification) |  |
| Reason for change: ( | The metadata required with a WCS output coverage is not sufficient for all client uses, in Subclause 7.3.9 of WCS 1.1 Corrigendum 2 [OGC 07-067r5]. |
| Summary of change: ( | Expand and modify the metadata required with a WCS output coverage, in Subclause 7.3.9 of WCS 1.1 Corrigendum 2, partially based on discussions in the WCS 1.2 SWG, including: Add Range of output coverage Expand domain of output coverage to include temporal domain Add ability to reference additional output coverage metadata Recommend use of wcs:CoverageDescription to combine metadata |
| Consequences if ( not approved: | Continued insufficient and unclear metadata required with a WCS output coverage, leading to more work by clients and confusion by WCS server and client implementers |
| Clauses affected: ( | 10.3.9, 9.3.1.1 |
| Other specs ( |  | Other core specifications ( |  |
| Affected: |  | Abstract specifications |  |
|  |  | Best Practices Papers |  |
| Supporting Doc. ( |  |
| Other comments: ( |  |
| Status ( |  |
| Disposition ( |  |

Edit Subclause 10.3.9 as follows:

10.3.9	Output coverage metadata

The metadata listed in Table 30, or the equivalent information, shall be included with each WCS output coverage. Equivalent metadata may be encoded with the coverage data in some possible coverage formats, as specified by a WCS encoding extension document (see 9.3.2.2 above). A WCS encoding extension document may specify encoding equivalent metadata both within a specialized coverage format and outside that format, but such duplication is discouraged to avoid consistency issues. When any metadata is encoded both with and outside the coverage data, that duplicated metadata shall be as consistent as possible.

Table 30 — Required output coverage metadata

| Names a | Definition | Data structure or type | Multiplicity and use |
| --- | --- | --- | --- |
| domain Domain | Available output coverage locations in space and/or time | Domain data structure, see Table 12 b | One (mandatory) |
| range Range | Available values in output coverage | Range data structure, see Table 17 | One (mandatory) |
| metadata Metadata | Additional metadata about this output coverage | Reference to metadata, or metadata contents, see Table 32 of [OGC 06-121r3] | Zero or more (optional) Include when available c |
| outputFormat OutputFormat | Identifier of format of output coverage | CharacterString type, not empty | One (mandatory) |
| a See Table 1 of [OGC 06-121r3] for UML and XML naming conventions. b The Coordinate Reference System (CRS) of an output coverage may be either a GridCRS or an ImageCRS. This Domain data structure shall include at least the BoundingBox of the output coverage, the GridCRS definition when used by that BoundingBox, and the Transformation when the output coverage is not georectified but is georeferenced. c Additional output coverage metadata that is needed by or useful to some clients is expected to be available in some cases, including data quality metadata for georectified coverages and for previously processed unrectified images. |

NOTE 1	Better definition of the additional output coverage metadata is left to future work.

Such metadata may be XML encoded using the WCS encoding of the data structures and types listed in Table 30. When all the output coverage metadata listed is encoded in XML (inside or outside a specialized coverage encoding format), that data should be encoded within a CoverageDescription data structure as specified in Table 11 through Table 20. That CoverageDescription data shall then be encoded using the wcs:CoverageDescription XML element specified in the wcsDescribeCoverage.xsd file. That wcs:CoverageDescription should also include the other data allowed and required in a CoverageDescription, including other description information.

NOTE 2	Use of the wcs:CoverageDescription XML element is desirable to simplify possible use of a WCS Transaction operation to insert this output coverage into a different (or the same) WCS server.  In that use, the one SupportedCRS will be this GridBaseCRS, and the one SupportedFormat will be this OutputFormat.

Edit Table 11 in Subclause 9.3.1.1 as follows:

Table 11 — Parts of CoverageDescription data structure

| Names a | Definition | Data type | Multiplicity and use |
| --- | --- | --- | --- |
| (Description) b | Description of a coverage | Description data structure, see Subclause 10.6.3 of [OGC 06-121r3] | One (mandatory) b |
| identifier Identifier | Unambiguous identifier of this coverage, unique for this WCS server | Character String type, not empty | One (mandatory) |
| metadata Metadata | More metadata about this coverage | Reference to metadata, or metadata contents,, see Table 32 of [OGC 06-121r3] | Zero or more (optional) Include when available e |
| domain Domain | Available coverage locations in space and/or time | Domain data structure, see Table 12 | One (mandatory) |
| range Range | Available coverage values | Range data structure, see Table 17 | One (mandatory) |
| supportedCRS SupportedCRS | Reference to GridBaseCRS of GridCRSs in which GetCoverage operation outputs may be expressed c | URI | One or more (mandatory) Include one for each GridBaseCRS supported d |
| supportedFormat SupportedFormat | Identifier of format in which GetCoverage operation response can be encoded | CharacterString type, not empty | One or more (mandatory) Include one for each format supported d |
| a See Table 1 of [OGC 06-121r3] for UML and XML naming conventions. b Contents inherited, not included as a named data structure. Normally includes only one Metadata item, but may include more than one when used here, especially for an unrectified but georeferenced image coverage. c A SupportedCRS may be referenced as the GridBaseCRS of a GridCRS specified in the Output part of a GetCoverage request. The GridBaseCRS of the GridCRS of a georectified offered coverage shall be listed as a SupportedCRS. An ImageCRS for an unrectified offered image shall be listed as a SupportedCRS, so that it may be referenced as the GridBaseCRS of a GridCRS. This ImageCRS shall be the ImageCRS of that unrectified offered image, or the ImageCRS that is referenced as the GridBaseCRS of the GridCRS that is used by that unrectified offered image In addition, the GetCoverage operation output maybe expressed in the ImageCRS or GridCRS of an unrectified offered coverage, instead of in a specified GridCRS. These SupportedCRSs can also be referenced in the BoundingBox in the DomainSubset part of a GetCoverage request. d There may be a dependency of a SupportedCRS upon a SupportedFormat: see Subclause 10.3.5. e Additional offered coverage metadata that is needed by or useful to some clients is expected to be available in some cases, including data quality metadata for georectified coverages and for previously processed unrectified images. |

NOTE 2	Better definition of the additional offered coverage metadata is left to future work.

# Comments

Enter the AS or Implementation Specification Name and Number in this box. For example, WMS 1.1.1 or GML 3.0. Do not prefix the number with anything, i.e. do not use "OGC", "GSM" or "OGC" etc.

Enter the CR number here. This number is allocated by the OGC support team.

Enter the revision number of the CR here. If it is the first version, use a "-".

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X. AS = Abstract Specification, IS = Implementation Specification, Recom. Paper = Recommendation Paper, Other = DIPR/IPR, etc.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.

Enter the source of the CR. This is either (a) one or more OGC members or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

IF there is one, enter the work item code or issue code that is applicable to the change. These codes will relate to Work Items identified in a WBS associated with a particular OGC initiative. If there is no code, leave blank.

Enter the date on which the CR was last revised.

Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the TC Policies and Procedures".

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. essential correction).

Enter each the number of each clause which contains changes.

Enter an X in the box if any other specifications are affected by this change.

If known, list here the specifications which are affected or the CRs which are linked.

Explanation of Field: If there is associated documentation, such as an lengthy change request or new text for consideration, please reference the OGC document number and document title.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.

This is the status of the change request. For a new submission, please enter “NEW”. Other options as the change request is processed are: Assigned, Verified, Resolved, and Closed.

This field is used to assign the RWG decision for this Change Request. Options include: Deferred, Accepted, and Rejected.