Open Geospatial Consortium	Document OGC 09-029

| CR-Form-v3 |
| --- |
| CHANGE REQUEST |
| ( | IGM and IGS | CR | ? | ( rev | - | ( Current version: | draft 1.0 |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |
| Proposed change affects: ( | AS |  | Imp Spec | X | Best Practices Paper |  | Other |  |
| Title: ( | IGS-IGM change request: Use new ISO 19130 terms |
| Source: ( | Arliss Whiteside and Stewart Walker |
| Work item code: ( |  |  | Date: ( | 2009-04-30 |
| Category: ( | C | (Change specification names and terms) |  |
|  | Use one of the following categories: F (Critical correction) A (corresponds to a correction in an earlier release) B (Addition of feature), C (Functional modification of feature) D (Editorial modification) |  |
| Reason for change: ( | The proposed IGS and IGM OGC implementation standards should use the same terms as now specified and used in (the near-final draft for) ISO 19130. Some of these terms differ from the terms previously used in draft ISO 19130, and are thus now used in draft IGS and IGM OGC implementation standards |
| Summary of change: ( | Change some terms in the draft IGS and IGM specifications to be consistent with terms with the same meanings now specified in (the near-final draft for) ISO 19130, including: 1) Use ISO 19130 terms with meanings that are intended in IGM and IGS 2) Not use ISO 19130 terms with meanings not intended in IGM and IGS 3) Include definitions of ISO 19130 terms now used in IGM and IGS |
| Consequences if ( not approved: | Failure to use the same terms now used in (the near-final draft for) ISO 19130 causes reader confusion |
| Clauses affected: ( | Most |
| Other specs ( | X | Other core specifications ( | WCS |
| Affected: |  | Abstract specifications |  |
|  |  | Best Practices Papers |  |
| Supporting Doc. ( |  |
| Other comments: ( | This change request is to the draft IGS specification OGC 07-030r2, currently posted at http://portal.opengeospatial.org/files/?artifact_id=25215, and to the draft IGM specification OGC 07-031r2, currently posted at http://portal.opengeospatial.org/files/?artifact_id=25216. |
| Status ( |  |
| Disposition ( |  |

## Change #1: Change IGM and IGS drafts NOT to use the terms formally specified in ISO 19130 to mean anything else in IGM and IGS

Change the current terms listed in the following table:

| Term now used in IGM and/or IGS | Different term defined in ISO 19130 |
| --- | --- |
| georeferencing | georeferencing |
| (none, be careful not to use) | interior coordinate reference system |

## Change #2: Change IGM and IGS drafts to use terms that are formally specified in ISO 19130 when those meanings apply to IGM and IGS

Change the current terms listed in the following table:

| Term now used in IGM and/or IGS | Different term defined in ISO 19130 |
| --- | --- |
| georeferencing transformation | geopositioning transformation |
| georeferencing service | geopositioning service |
| georeferencing metadata | geolocation information geolocation metadata |
| object image transformation | sensor model |
| (none, change to use ISO 19130 term) | physical sensor model |
| (none, change to use ISO 19130 term) | true replacement sensor model (RSM) |
| (none, change to use ISO 19130 term) | correspondence sensor model |
| (none, change to use ISO 19130 term) | external coordinate reference system |
| (none, change to use ISO 19130 term) | platform coordinate reference system |
| adjustable parameters | adjustable model parameters |
| image position | image point |
| control point | ground control point (GCP) |
| identification image | image-identifiable ground control point |
| (none, perhaps change to use ISO 19130 term) | perspective centre projection centre |
| (none, perhaps change to use ISO 19130 term) | calibrated focal length |
| (none, perhaps change to use ISO 19130 term) | image plane |
| (none, perhaps change to use ISO 19130 term) | principle point of autocollimation |
| (none, perhaps change to use ISO 19130 term) | frame sensor |
| (none, perhaps change to use ISO 19130 term) | pushbroom sensor |
| (none, perhaps change to use ISO 19130 term) | whiskbroom sensor |
| (none, perhaps change to use ISO 19130 term) | grid |
| (none, perhaps change to use ISO 19130 term) | grid coordinates |
| (none, perhaps change to use ISO 19130 term) | rectified grid |
| (none, perhaps change to use ISO 19130 term) | image distortion |
| metadata (no change) | metadata (include definition) |
| object point (no change) | object point (include definition) |
| attitude (no change) | attitude (include definition) |
| pixel (no change) | pixel (include definition) |

## Change #3: Change IGM and IGS drafts to include definitions of terms formally defined in ISO 19130 which are now used in IGM and IGS

See above table.  Also copy definitions of terms formally defined in ISO 19111 but now only referenced in IGM and IGS drafts.

## Change #4: Change IGM and IGS drafts to use terms used but not formally defined in ISO 19130 with meanings that apply to IGM and IGS

Change the current terms listed in the following table:

| Term now used in IGM and/or IGS | Different term defined in ISO 19130 |
| --- | --- |
| sensor parameters | interior sensor parameters |
| image parameters | exterior sensor parameters |
| (none, change to use ISO 19130 term) | platform parameters |
| dimension = 3 (of object position) | full GCP |
| dimension = 2 (of object position) | horizontal GCP |
| dimension = 1 (of object position) | vertical GCP |
| position (of sensor or platform) | position (of sensor or platform) |

Several rows in the above table include the word “parameters”.  In addition, IGM and IGS now use the related term “parameter values”.  Other changes being proposed to IGM would change many instances of “parameter values” to “model”.  The ISO 19130 terms listed above as “… parameters” should also be applied to “… parameter values” and “… model”.

## Change #5: Change IGM draft to include formal definitions of the terms used but not formally defined in ISO 19130 which are now used in IGM

See above table.

## Change #6: Change Preface of IGM and IGS to reflect changes in document names

Background: The term “geopositioning” was first used in these drafts because that term is most frequently used by BAE Systems customers.  However, that term is not now used in the OGC Abstract Specification.  Instead, ISO 19123 currently uses the terms “georeferenceable” and “referenceable”with closely related meanings.  Changing the form of “georeferenceable” to name the action, instead of naming the possibility, produces the term “georeferencing”.  That term was already used in WCS 1.1 with the same meaning.

The term “geopositioning” was previously changed to “georeferencing”, because the term “geopositioning” was not then used in the ISO 19130 draft.  However, the current ISO 19130 draft uses the term “geopositioning”, and gives “georeferencing” a meaning limited to correspondence sensor models.

Specific change: Edit following paragraph of Clause “i” “Preface” in both IGM and IGS as follows:

“This specification previously used the term “georeferencing” in the title and elsewhere (in OGC 07-030r2 and its predecessors). The term “georeferencing” was used because the term “geopositioning” was not then used in the ISO 19130 draft.  However, the current later ISO 19130 draft uses the term “geopositioning”, and gives “georeferencing” a meaning limited to approximate correspondence sensor models.”

## Change #7: Add to IGM a normative reference to ISO 19130

## Change #8: Change IGM encoding of ground control point to better match Clause 6.4 of ISO 19130, but not now include encoding of GriddedGCPCollection

Since much of Clause 6.4 of ISO 19130 is based on ISO 19115-2, these changes will be detailed in a separate Change Request.  However, this Change Request proposes leaving the encoding of gridded ground control points to possible future extension(s) of IGM.

# Comments

Enter the AS or Implementation Specification Name and Number in this box. For example, WMS 1.1.1 or GML 3.0. Do not prefix the number with anything, i.e. do not use "OGC", "GSM" or "OGC" etc.

Enter the CR number here. This number is allocated by the OGC support team.

Enter the revision number of the CR here. If it is the first version, use a "-".

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X. AS = Abstract Specification, IS = Implementation Specification, Recom. Paper = Recommendation Paper, Other = DIPR/IPR, etc.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.

Enter the source of the CR. This is either (a) one or more OGC members or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

IF there is one, enter the work item code or issue code that is applicable to the change. These codes will relate to Work Items identified in a WBS associated with a particular OGC initiative. If there is no code, leave blank.

Enter the date on which the CR was last revised.

Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the TC Policies and Procedures".

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. essential correction).

Enter each the number of each clause which contains changes.

Enter an X in the box if any other specifications are affected by this change.

If known, list here the specifications which are affected or the CRs which are linked.

Explanation of Field: If there is associated documentation, such as an lengthy change request or new text for consideration, please reference the OGC document number and document title.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.

This is the status of the change request. For a new submission, please enter “NEW”. Other options as the change request is processed are: Assigned, Verified, Resolved, and Closed.

This field is used to assign the RWG decision for this Change Request. Options include: Deferred, Accepted, and Rejected.