Open Geospatial Consortium	Document OGC 08-188r1

| CR-Form-v3 |
| --- |
| CHANGE REQUEST |
| ( | IGM | CR | ? | ( rev | - | ( Current version: | OGC 07-031r2 |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |
| Proposed change affects: ( | AS |  | Imp Spec | X | Best Practices Paper |  | Other |  |
| Title: ( | IGM change request - Improve covariance matrix encoding |
| Source: ( | Arliss Whiteside, IGS-IGM SWG |
| Work item code: ( |  |  | Date: ( | 2009-05-01 |
| Category: ( | C |  |  |
|  | Use one of the following categories: F (Critical correction) A (corresponds to a correction in an earlier release) B (Addition of feature), C (Functional modification of feature) D (Editorial modification) |  |
| Reason for change: ( | The current encoding of covariance matrices does not allow encoding of only the non-zero sub-matrices, which would often significantly reduce the required data volume. Also, the current encoding specifically and separately supports five forms of covariance matrices, three of which are specialized uses of non-zero sub-matrices. |
| Summary of change: ( | Extensively revise the encoding of covariance matrices to support simple encoding of non-zero sub-matrices. |
| Consequences if ( not approved: | Continued limitations on the data volume required for encoding typical covariance matrices, and continued complexity of implementation by separately specifying encodings for five forms of covariance matrix |
| Clauses affected: ( | 12, igm:CovarianceMatrix.xsd |
| Other specs ( |  | Other core specifications ( |  |
| Affected: |  | Abstract specifications |  |
|  |  | Best Practices Papers |  |
| Supporting Doc. ( |  |
| Other comments: ( | This change request is to the previously proposed, but not accepted, Image georeferencing metadata GML 3.2 Application Schema [OGC 07031r2]. This change request previously specified two alternatives, first specifying one alternative using ISO 19139, and then specifying a second alternative not directly using ISO 19139. This change request now specifies only one alternative, not directly using ISO 19139, based on a decision by the IGS-IGM SWG. |
| Status ( |  |
| Disposition ( |  |

Editor’s Note: The idea for this alternative 2 arose when I realized that alternative 1 did not use very much of ISO 19139, and that all the parts it did use have equivalents in GML 3.2.1.  This alternative thus replaces all references to parts of ISO 19139 in previous alternative 1, with references to the corresponding parts of GML 3.2.1.  By not also referencing (all of) ISO 19139, this alternative 2 is expected to be somewhat easier to implement.

Edit Clause 12 as follows:

# Covariance matrix

## Introduction

The covariance matrix part of the Image georeferencing metadata GML Application Schema records combined absolute and relative position error estimates. The error statistics are in the form of covariance matrices, also called variance-covariance matrices, used with the (most-likely) values to which the covariance matrices apply. These covariance matrices normally represent correlations between the accuracies of different parameters, coordinates, and positions.

These covariance matrices are used to contain the variance of each adjusted value estimated in the triangulation, and the covariances between these values. These estimated values include various parameters in georeferencing coordinate transformations, including the camera 3D position coordinates and 3D orientation angles. The estimated values also include point position coordinates in object CRSs.

NOTE 	Such covariance matrices for single point coordinates are described in Table D.33 of [ISO/TS 19138 draft n1934].

## UML model

The UML class diagram for the GCM_CovarianceMatrix package is shown in Figure 18, together with the ISO 19115 classes that are inherited from. The new classes defined in this GCM_CovarianceMatrix package are described in Table 28 through Table 31.

Figure 18 — GCM_CovarianceMatrix package UML class diagram

NOTE 	This GCM_CovarianceMatrix package class diagram shows all the attributes in the DQ_Element and DQ_QuantitativeResult classes. However, some of the optional attributes in each are not expected to be useful in this application, and are thus prohibited in the GCM_CovarianceMatrix and GCM_FullMatrix classes.

This UML class diagram defines how covariance matrices can be efficiently recorded. The CovarianceMatrix package (for the Image georeferencing metadata GML Application Schema) specializes the DQ_DataQuality package specified in ISO 19115. This is done by defining more-specific subclasses of DQ_PositionalAccuracy and DQ_QuantitativeResult.

The CovarianceMatrix concrete class restricts and extends the DQ_PositionalAccuracy abstract class for combined absolute external and relative internal positional accuracies. This class describes the measure by substituting the size of this covariance matrix and an ordered sequence of references to the variable parameters for this covariance matrix.

The FullMatrix class restricts the DQ_QuantitativeResult class for efficiently recording the values of the non-zero and non-overlapping submatrices in the covariance matrix. Instead of a general record, the “value” attribute is changed to one or more associations to SubMatrix objects, each of which encodes the values of cells in a submatrix that contains one or more non-zero cell values.

The SubMatrix class contains one ordered sequence of values of cells in this submatrix, together with information defining the position and size of this submatrix within the full covariance matrix. That information consists of the submatrixType, firstRow index, firstColumn index, number of “rows”, and number of “columns”. The submatrixType has one of (currently) three values:

diagonal: Only the cells on the diagonal of this square sub-matrix are non-zero, so only the values of these diagonal cells are included.

onDiagonal: The first cell in this sub-matrix lies on the diagonal of the full covariance matrix.

offDiagonal: All the cells, including the first cell, in this sub-matrix lie to the right of  the diagonal of the full covariance matrix.

Table 28 — Defining elements of GCM_CovarianceMatrix class

| Description: Covariance matrix form of error estimates, used for the estimated errors in possibly statistically-correlated sets of parameters. The rows and columns of a covariance matrix correspond to the same ordered list of parameters. |
| --- |
| Stereotype: Type Class attribute: Concrete Inheritance from: DQ_PositionalAccuracy Association roles: coordinateOperationAccuracy from GAG_AdjustedGroup [1] (Composition (TBR) association from adjusted group that determined these error estimates) positionErrorEstimates from GOP_ImagePosition [1] (Association from image position for these absolute and relative position error estimates) positionErrorEstimates from GOP_ObjectPosition [1] (Association from absolute and relative position error estimates for this object position) Public attributes: (The first eight attributes listed below are inherited from DQ_Element through DQ_PositionalAccuracy, with six of these attributes being prohibited here.) |
| Attribute name | UML identifier | Data type | Obligation | Maximum occurrence | Attribute description |
| Name Of Measure | nameOfMeasure | CharacterString | O | 0 a | Name of the test applied to the data. |
| Measure Identification | measureIdentification | MD_Identifier | O | 0 a | Code identifying a registered standard procedure. |
| Measure Description | measureDescription | CharacterString | O | 0 a, b | Description of the measure. |
| Evaluation Method Type | evaluationMethodType | DQ_EvaluationMethodType | O | 0 a | Type of method used to evaluate quality of the dataset. |
| Evaluation Method Description | evaluationMethodDescription | CharacterString | O | 1 | Description of the evaluation method. |
| Evaluation Procedure | evaluationProcedure | CI_Citation | O | 0 a | Reference to the procedure information. |
| Date and Time | dateTime | DateTime | O | 0 a | Date or range of dates on which a data quality measure was applied. |
| Result | result | GCM_FullMatrix | M | 1 | Value (or set of values) obtained from applying a data quality measure. |
| Matrix Size | matrixSize | PositiveInteger | M | 1 | Number or rows and columns in this covariance matrix. |
| Adjusted Parameters | adjustedParameter | <Sequence(URI)> | M | N | Ordered sequence of references to adjusted parameters whose estimated error is represented by one row and one column in covariance matrix. |
| a Inclusion of this attribute is prohibited in this GCM_CovarianceMatrix subclass of the DQ_PositionalAccuracy subclass of the DQ_Element class. b The measureDescription optional element is replaced by the matrixSize and adjustedParameters attributes, which describe the rows and columns of this covariance matrix. |

Table 29 — Defining elements of GCM_FullMatrix class

| Description: Full covariance matrix cell values, encoded as one or more non-zero and non-overlapping sub-matrices, with each sub-matrix encoded as one sequence of cell values. |
| --- |
| Stereotype: Type Class attribute: Concrete Inheritance from: DQ_QuantitativeResult Association roles: subMatrix to GCM_SubMatrix [1..*] Public attributes: (All three listed attributes are inherited from DQ_QuantitativeResult, with two attributes being restricted here.) |
| Attribute name | UML identifier | Data type | Obligation | Maximum occurrence | Attribute description |
| Value Type | valueType | RecordType | 0 | 0 a | Value type for reporting a data quality result. |
| Value Units | valueUnits | Sequence<uom> b | M | 1 | Ordered sequence of references to value units for covariance matrix cells. b |
| Error Statistic | errorStatistic | CharacterString | 0 | 1 a | Statistical method used to determine the value. |
| a Inclusion of the valueType and errorStatistic attributes are prohibited in this FullMatrix subclass of DQ_QuantitativeResult. b In this FullMatrix class, the valueUnit attribute is replaced by valueUnits, which shall contain an ordered sequence of the identifiers to the units for each covariance matrix row, with the same units for each column, and with the unit for each matrix cell being the product of the corresponding row and column units. The referenced units shall be for the corresponding parameters in the adjustedParameters element. The number of valueUnits referenced shall equal the value of the matrixSize. |

Table 30 — Defining elements of GCM_SubMatrix class

Description: Sub-matrix of a covariance matrix encoded as an ordered sequence of cell values, with attributes that specify the position and size of this sub-matrix. Stereotype: Type Class attribute: Concrete Inheritance from: (none) Association roles: subMatrix from GCM_FullMatrix [1] Public attributes: Attribute name UML identifier Data type Obligation Maximum occurrence Attribute description Values List valuesList Sequence<Real> M 1 Ordered sequence of one or more covariance matrix cell values. a Submatrix Type submatrixType GCM_SubmatrixTyp M 1 Type of this sub-matrix. First Row firstRow UnsignedInteger M 1 Index of the first row in this sub-matrix within full covariance matrix. b First Column firstColumn UnsignedInteger M 1 Index of the first column in this sub-matrix within full covariance matrix. c Rows rows PositiveInteger M 1 Number of rows in this sub-matrix of the covariance matrix. Columns columns PositiveInteger M 1 Number of columns in this sub-matrix of the covariance matrix. d a The cell values are ordered from left to right along each matrix row, and then down for successive rows. b The first row in the full covariance matrix has the index value zero. c The first column in the full covariance matrix has the index value zero. d This number of columns shall be equal to or larger than the number of rows in this sub-matrix.

Editor’s Question:	Should the indices of the first row and column be “zero” (as stated above), or should the first indices be changed to “one”?

Table 31 — Defining elements of GCM_SubmatrixType class

| Description: Type of this sub-matrix. |
| --- |
| Stereotype: CodeList Class attribute: Concrete Inheritance from: (none) Association roles: (none) Used by: GOP_SubMatrix Public attributes: |
| Attribute name | UML identifier | Data type | Obligation | Maximum occurrence | Attribute description |
| Diagonal | diagonal | CharacterString | C | 1 | Only the cells on the diagonal of this square sub-matrix are non-zero, so only the values of these diagonal cells shall be included. a |
| On Diagonal | onDiagonal | CharacterString | C | 1 | The first cell in this sub-matrix lies on the diagonal of the full covariance matrix. Values for the cells to the left of the (symmetric) covariance matrix diagonal shall thus not be included. b |
| Off Diagonal | offDiagonal | CharacterString | C | 1 | All the cells, including the first cell, in this sub-matrix lie to the right of the diagonal of the full covariance matrix. Values for all the cells in this sub-matrix shall thus be included. b |
| Condition: One and only one of the listed attributes shall be supplied. a In this case, the numbers of "rows" and "columns" shall be equal. b. This sub-matrix may be either square or contain more columns than rows. |

Editor’s Question:	For the “on diagonal” value of this SubmatrixType, should this sub-matrix be restricted to square (never rectangular)?

## XML encoding

The GCM_CovarianceMatrix UML package is encoded in the igmCovarianceMatrix.xsd XML Schema Document, and normally uses the igmSubmatrixTypes.xml document. The igmCovarianceMatrix.xsd imports only gml/3.2.1/gml.xsd, and does not directly use any XML Schema Documents from ISO 19139. Elements in GML 3.2.1 instead of in ISO 19139 are used to simplify implementation. The contents of the igmCovarianceMatrix.xsd XML Schema Document and igmSubmatrixTypes.xml document shall be as specified in the attached files.

NOTE 	The following examples use “999” as a place holder for specific numerical values.

EXAMPLE 1	An example XML fragment for a 2 by 2 diagonal CovarianceMatrix, suitable for a measured ImagePosition, encoded using one “diagonal” SubMatrix, is:

<CovarianceMatrix>

<matrixSize>2</matrixSize>

<adjustedParameters>row column</adjustedParameters>

<result>

<FullMatrix>

<valueUnits>GridSpacing GridSpacing</valueUnits>

<subMatrix>

<SubMatrix>

<valuesList>0.999 0.999</valuesList>

<submatrixType codeSpace="igmSubmatrixTypes.xml">diagonal</submatrixType>

<firstRow>0</firstRow>

<firstColumn>0</firstColumn>

<rows>2</rows>

<columns>2</columns>

</SubMatrix>

</subMatrix>

</FullMatrix>

</result>

</CovarianceMatrix>

EXAMPLE 2	An example XML fragment for a CovarianceMatrix using a 3 by 3 complete CovarianceMatrix, suitable for a computed ObjectPosition, encoded using one onDiagonal SubMatrix, is:

<CovarianceMatrix>

<matrixSize>3</matrixSize>

<adjustedParameters>Easting Northing Elevation</adjustedParameters>

<result>

<FullMatrix>

<valueUnits>m m m</valueUnits>

<subMatrix>

<SubMatrix>

<valuesList>0.999 0.999 0.999 0.999 0.999 0.999</valuesList>

<submatrixType codeSpace="igmSubmatrixTypes.xml">onDiagonal</submatrixType>

<firstRow>0</firstRow>

<firstColumn>0</firstColumn>

<rows>3</rows>

<columns>3</columns>

</SubMatrix>

</subMatrix>

</FullMatrix>

</result>

</CovarianceMatrix>

EXAMPLE 3	An example XML fragment for a 4 by 4 banded CovarianceMatrix, encoded using four onDiagonal sub-matrices, is:

<CovarianceMatrix>

<matrixSize>4</matrixSize>

<adjustedParameters>X Y Z T</adjustedParameters>

<result>

<FullMatrix>

<valueUnits>m m m s</valueUnits>

<subMatrix>

<SubMatrix>

<valuesList>0.999 0.999</valuesList>

<submatrixType codeSpace="igmSubmatrixTypes.xml">onDiagonal</submatrixType>

<firstRow>0</firstRow>

<firstColumn>0</firstColumn>

<rows>1</rows>

<columns>2</columns>

</SubMatrix>

</subMatrix>

<subMatrix>

<SubMatrix>

<valuesList>0.999 0.999</valuesList>

<submatrixType codeSpace="igmSubmatrixTypes.xml">onDiagonal</submatrixType>

<firstRow>1</firstRow>

<firstColumn>1</firstColumn>

<rows>1</rows>

<columns>2</columns>

</SubMatrix>

</subMatrix>

<subMatrix>

<SubMatrix>

<valuesList>0.999 0.999</valuesList>

<submatrixType codeSpace="igmSubmatrixTypes.xml">onDiagonal</submatrixType>

<firstRow>2</firstRow>

<firstColumn>2</firstColumn>

<rows>1</rows>

<columns>2</columns>

</SubMatrix>

</subMatrix>

<subMatrix>

<SubMatrix>

<valuesList>0.999</valuesList>

<submatrixType codeSpace="igmSubmatrixTypes.xml">onDiagonal</submatrixType>

<firstRow>3</firstRow>

<firstColumn>3</firstColumn>

<rows>1</rows>

<columns>1</columns>

</SubMatrix>

</subMatrix>

</FullMatrix>

</result>

</CovarianceMatrix>

Add new igmSubmatrixTypes.xml dictionary file as follows:

<?xml version="1.0" encoding="UTF-8"?>

<Dictionary xmlns="http://www.opengis.net/gml/3.2"

xmlns:gml="http://www.opengis.net/gml/3.2"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.opengis.net/gml/3.2 ../../gml/3.2.1/gml.xsd"

gml:id="SubmatrixTypes">

<description>This dictionary records the standard values for submatrix types, as specified in IGM 1.0 specification Table 31 titled "Defining elements of GCM_SubmatrixType class". </description>

<identifier codeSpace="">igmSubmatrixTypes</identifier>

<!-- ===================================================== -->

<dictionaryEntry>

<Definition gml:id="diagonal">

<description>Only the cells on the diagonal of this square sub-matrix are non-zero, so only the values of these diagonal cells shall be included. In this case, the numbers of "rows" and "columns" shall be equal. </description>

<identifier codeSpace="igmSubmatrixTypes.xml">diagonal</identifier>

</Definition>

</dictionaryEntry>

<!-- ===================================================== -->

<dictionaryEntry>

<Definition gml:id="onDiagonal">

<description>The first cell in this sub-matrix lies on the diagonal of the full covariance matrix. Values for the cells to the left of the (symmetric) covariance matrix diagonal shall thus not be included. This sub-matrix may be either square or contain more columns than rows. </description>

<identifier codeSpace="igmSubmatrixTypes.xml">onDiagonal</identifier>

</Definition>

</dictionaryEntry>

<!-- ===================================================== -->

<dictionaryEntry>

<Definition gml:id="offDiagonal">

<description>All the cells, including the first cell, in this sub-matrix lie to the right of  the diagonal of the full covariance matrix. Values for all the cells in this sub-matrix shall thus be included. This sub-matrix may be either square or contain more columns than rows. </description>

<identifier codeSpace="igmSubmatrixTypes.xml">offDiagonal</identifier>

</Definition>

</dictionaryEntry>

<!-- ===================================================== -->

</Dictionary>

Replace previous igmCovarianceMatrix.xsd file with the following:

<?xml version="1.0" encoding="UTF-8"?>

<schema targetNamespace="http://www.opengis.net/igm/1.0"

xmlns:igm="http://www.opengis.net/igm/1.0"

xmlns:gml="http://www.opengis.net/gml/3.2"

xmlns="http://www.w3.org/2001/XMLSchema"

elementFormDefault="qualified"

version="1.0.0" xml:lang="en">

<annotation>

<appinfo>igmCovarianceMatrix.xsd 2008-12-08</appinfo>

<documentation>This XML Schema Document encodes the CovarianceMatrix UML package of the "Image georeferencing metadata GML 3.2 application schema". Although that UML package extends ISO 19115, this encoding extends GML 3.2 instead of extending ISO 19139, in order to simplify immplementation.

Copyright (c) 2008 Open Geospatial Consortium, Inc. All Rights Reserved. </documentation>

</annotation>

<!-- ==============================================================

includes and imports

============================================================== -->

<import namespace="http://www.opengis.net/gml/3.2" schemaLocation="../../gml/3.2.1/gml.xsd"/>

<!-- ==============================================================

elements and types

============================================================== -->

<element name="CovarianceMatrix" type="igm:CovarianceMatrixType" substitutionGroup="gml:AbstractObject">

<annotation>

<documentation>Covariance matrix form of error estimates, used for the estimated errors in possibly-statistically-correlated sets of parameters. The rows and columns of a covariance matrix correspond to the same ordered list of parameters. </documentation>

<documentation>This element is based on the DQ_PositionalAccuracy class of ISO 19115, but extends GML 3.2 instead of restricting gco:AbstractDQ_PositionalAccuracy_Type in ISO 19139. The measureDescription optional element is replaced by the matrixSize and adjustedParameters elements, which describe the rows and columns of this covariance matrix. The nameOfMeasure, measureIdentification, measureDescription, evaluationMethodType, and evaluationProcedure optional elements in gco:AbstractDQ_PositionalAccuracy_Type are omitted, since their values are implied by the element name CovarianceMatrix. The dateTime optional element is also omitted, since this information is provided elsewhere. </documentation>

</annotation>

</element>

<!-- =========================================================== -->

<complexType name="CovarianceMatrixType">

<sequence>

<element name="matrixSize" type="positiveInteger">

<annotation>

<documentation>Number of rows and columns in this (symmetric) covariance matrix. </documentation>

</annotation>

</element>

<element name="adjustedParameters" type="gml:QNameList">

<annotation>

<documentation>Ordered sequence of the names of all adjusted parameters included in this covariance matrix. The number of names included shall equal the value of the matrixSize. </documentation>

<documentation>This element might be changed to an ordered sequence of references to lists of the groups of adjusted parameters. </documentation>

</annotation>

</element>

<element name="evaluationMethodDescription" type="string" minOccurs="0">

<annotation>

<documentation>Description of the evaluation method. In a covariance matrix element, this element should indicate whether this matrix was fully computed (with all covariance values) or just estimated (with zero values of some covariance cells). </documentation>

</annotation>

</element>

<element name="result" type="igm:FullMatrixPropertyType">

<annotation>

<documentation>Full covariance matrix cell values. </documentation>

</annotation>

</element>

</sequence>

</complexType>

<!-- =========================================================== -->

<complexType name="CovarianceMatrixPropertyType">

<annotation>

<documentation>Association to a CovarianceMatrix object, often referenced. </documentation>

<documentation>The attribute gml:nilReason is omitted, since a CovarianceMatrix shall not be referenced when it does not exist. </documentation>

</annotation>

<sequence>

<element ref="igm:CovarianceMatrix" minOccurs="0"/>

</sequence>

<attributeGroup ref="gml:AssociationAttributeGroup"/>

</complexType>

<!-- =========================================================== -->

<!-- =========================================================== -->

<element name="FullMatrix" type="igm:FullMatrixType" substitutionGroup="gml:AbstractObject">

<annotation>

<documentation>Full covariance matrix cell values, encoded as one or more non-zero and non-overlapping sub-matrices, with each sub-matrix encoded as one sequence of cell values. The required valueUnit element is replaced by the valueUnits element which references the units for all the rows and columns of this covariance matrix. </documentation>

<documentation>This element is based on the DQ_QuantitativeResult class of ISO 19115, but extends GML 3.2 instead of restricting gco:DQ_QuantitativeResult_Type in ISO 19139. The valueType and errorStatistic optional elements in the DQ_QuantitativeResult_Type are omitted, since their values are implied by the name of the CovarianceMatrix containing element. </documentation>

</annotation>

</element>

<!-- =========================================================== -->

<complexType name="FullMatrixType">

<sequence>

<element name="valueUnits">

<annotation>

<documentation>Ordered sequence of the identifiers of the units for covariance matrix cells. In this FullMatrix element, these units shall be an ordered list of the units for each covariance matrix row, with the same units being used for each column, and with the unit for each matrix cell being the product of the corresponding row and column units. The referenced units shall be for the corresponding parameters in the adjustedParameters element. The number of valueUnits referenced shall equal the value of the matrixSize. </documentation>

<documentation>This element is changed from ISO 19115 to only identify (not define) the units, and to allow referencing a list of units as needed for the many rows and columns of covariance matrix cells. </documentation>

</annotation>

<simpleType>

<list itemType="gml:UomIdentifier"/>

</simpleType>

</element>

<element name="subMatrix" type="igm:subMatrixPropertyType" maxOccurs="unbounded">

<annotation>

<documentation>Unordered list of one or more (non-zero and non-overlapping) sub-matrices encoded within this full covariance matrix. This subMatrix element shall be repeated for each non-zero and non-overlapping sub-matrix used to encode the full covariance matrix. </documentation>

</annotation>

</element>

</sequence>

</complexType>

<!-- =========================================================== -->

<complexType name="FullMatrixPropertyType">

<annotation>

<documentation>Association to a (covariance) FullMatrix object, always encoded in-line. </documentation>

</annotation>

<sequence>

<element ref="igm:FullMatrix"></element>

</sequence>

</complexType>

<!-- =========================================================== -->

<!-- =========================================================== -->

<element name="SubMatrix" type="igm:SubMatrixType" substitutionGroup="gml:AbstractObject">

<annotation>

<documentation>Sub-matrix of a covariance matrix encoded as an ordered sequence of cell values, with property elements that specify the position and size of this sub-matrix. </documentation>

<documentation>An element in the igm:SubMatrix substitutionGroup which binary encodes a SubMatrix could be specified in an IGM extension application schema. </documentation>

</annotation>

</element>

<!-- =========================================================== -->

<complexType name="SubMatrixType">

<sequence>

<element name="valuesList">

<annotation>

<documentation>Ordered sequence of one or more covariance matrix cell values. The cell values are ordered from left to right along each matrix row, and then down for successive rows. Only the number of useful digits in each covariance cell value needs to be included, omitting all less significant digits of the xsd:float mantissa that are either zero or not useful. </documentation>

</annotation>

<simpleType>

<list itemType="float"/>

</simpleType>

</element>

<group ref="igm:submatrixPositionAndSize"/>

</sequence>

</complexType>

<!-- =========================================================== -->

<complexType name="subMatrixPropertyType">

<annotation>

<documentation>Association to a SubMatrix object, always encoded in-line. </documentation>

</annotation>

<sequence>

<element ref="igm:SubMatrix"/>

</sequence>

</complexType>

<!-- =========================================================== -->

<!-- =========================================================== -->

<group name="submatrixPositionAndSize">

<annotation>

<documentation>This group is specified to facilitate defining other elements in the igm:SubMatrix substitutionGroup. </documentation>

</annotation>

<sequence>

<element ref="igm:submatrixType">

<annotation>

<documentation>Type of this sub-matrix. </documentation>

</annotation>

</element>

<element name="firstRow" type="unsignedInt">

<annotation>

<documentation>Index of the first row in this sub-matrix within the full covariance matrix. The first row in the full covariance matrix has the index value zero. </documentation>

</annotation>

</element>

<element name="firstColumn" type="unsignedInt">

<annotation>

<documentation>Index of the first column in this sub-matrix within the full covariance matrix. This firstColumn value shall not be less than the value of the associated firstRow. The first column in the full covariance matrix has the index value zero. </documentation>

</annotation>

</element>

<element name="rows" type="positiveInteger">

<annotation>

<documentation>Number of rows in this sub-matrix of the covariance matrix. </documentation>

</annotation>

</element>

<element name="columns" type="positiveInteger">

<annotation>

<documentation>Number of columns in this sub-matrix of the covariance matrix. This number of columns shall be equal to or larger than the number of rows in this sub-matrix. </documentation>

</annotation>

</element>

</sequence>

</group>

<!-- =========================================================== -->

<element name="submatrixType" type="gml:CodeWithAuthorityType">

<annotation>

<documentation>Type of this sub-matrix. The required codeSpace attribute shall reference a gml:dictionary specifying the values and meanings of all the allowed string values for this property. </documentation>

</annotation>

</element>

<!-- =========================================================== -->

</schema>

# Comments

Enter the AS or Implementation Specification Name and Number in this box. For example, WMS 1.1.1 or GML 3.0. Do not prefix the number with anything, i.e. do not use "OGC", "GSM" or "OGC" etc.

Enter the CR number here. This number is allocated by the OGC support team.

Enter the revision number of the CR here. If it is the first version, use a "-".

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X. AS = Abstract Specification, IS = Implementation Specification, Recom. Paper = Recommendation Paper, Other = DIPR/IPR, etc.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.

Enter the source of the CR. This is either (a) one or more OGC members or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

IF there is one, enter the work item code or issue code that is applicable to the change. These codes will relate to Work Items identified in a WBS associated with a particular OGC initiative. If there is no code, leave blank.

Enter the date on which the CR was last revised.

Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the TC Policies and Procedures".

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. essential correction).

Enter each the number of each clause which contains changes.

Enter an X in the box if any other specifications are affected by this change.

If known, list here the specifications which are affected or the CRs which are linked.

Explanation of Field: If there is associated documentation, such as an lengthy change request or new text for consideration, please reference the OGC document number and document title.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.

This is the status of the change request. For a new submission, please enter “NEW”. Other options as the change request is processed are: Assigned, Verified, Resolved, and Closed.

This field is used to assign the RWG decision for this Change Request. Options include: Deferred, Accepted, and Rejected.