Open Geospatial Consortium	OGC Document 09-091r1

| CR-Form-v3 |
| --- |
| CHANGE REQUEST |
| ( | GML | CR | ? | ( rev | - | ( Current version: | 3.2.1 |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |
| Proposed change affects: ( | AS |  | Imp Spec | X | Best Practices Paper |  | Other |  |
| Title: ( | GML 3.2.1 change request - Add ReferencedGridByTransformation |
| Source: ( | Arliss Whiteside, Max Martinez, Discussions in GML SWG |
| Work item code: ( |  |  | Date: ( | 2009-10-16 |
| Category: ( | B |  |  |
|  | Use one of the following categories: F (Critical correction) A (corresponds to a correction in an earlier release) B (Addition of feature), C (Functional modification of feature) D (Editorial modification) |  |
| Reason for change: ( | Abstract Specification Topic 6 (ISO 19123) specifies CV_ReferenceableGrid, but this class was not previously encoded in GML. GML Change Request 07-112r3 adds an abstract implementation of CV_ReferenceableGrid, plus two concrete subtypes that are designed for irregularly spaced grid points. However, another implementation of CV_ReferenceableGrid is required and will be very frequently used. That implementation uses a CC_Transformation or CC_ConcatenatedOperation (instead of grid points) to specify the relationship between grid coverage positions and positions in another CRS, as suggested in Clause 8.10.1.1 of Topic 6. Although that Transformation could use grid points, it will usually be an analytical Transformation using sensor models such as defined in ISO 19130. Analytical Transformations are normally used for these sensor models, to reduce the required data volume and to simplify least-squares adjustment. |
| Summary of change: ( | Add a ReferencedGridByTransformation element, in the AbstractReferenceableGrid substitutionGroup, which encodes the relationship between grid coverage positions and positions in another CRS using a gml:CoordinateOperation or gml:ConcatenatedOperation. |
| Consequences if ( not approved: | Major limitation in the types of referenceable grids that can be encoded in GML |
| Clauses affected: ( | 19.2.7 (new), 19.2.8 (new), 19.2.2, 19.2.3, 19.2.4, 19.2.6 |
| Other specs ( |  | Other core specifications ( |  |
| Affected: |  | Abstract specifications |  |
|  |  | Best Practices Papers |  |
| Supporting Doc. ( |  |
| Other comments: ( | This change request extends and modifies GML Change Request 07-112r3. |
| Status ( |  |
| Disposition ( |  |

Add Clauses 19.2.7, 19.2.8 to OGC 07-036 as follows:

19.2.7	ReferencedGridByTransformation

<element name="ReferencedGridByTransformation" type="gml:ReferencedGridByTransformationType" substitutionGroup="gml:AbstractReferenceableGrid"/>

<complexType name="ReferencedGridByTransformationType">

<complexContent>

<extension base="gml:AbstractReferenceableGridType">

<sequence>

<element ref="gml:gridCRS" minOccurs="0"/>

<choice maxOccurs="unbounded">

<element name="transformation" type="gml:TransformationPropertyType"/>

<element name="concatenatedOperation" type="gml:ConcatenatedOperationPropertyType"/>

</choice>

</sequence>

</extension>

</complexContent>

</complexType>

ReferencedGridByTransformation encodes one type of CV_ReferenceableGrid as defined in ISO 19123, using a gml:Transformation or gml:ConcatenatedOperation to specify the relationship between positions in the grid and corresponding positions in another CRS. This encoding also generalises CV_ReferenceableGrid to allow including more than one referencing Transformation.

The gridCRS is a composition association to the definition of the “internal” CRS for this extended gml:Grid. This definition shall be the one (optionally) referenced by the gml:srsName attribute in the gml:GridType. This CRS definition shall be included here if its definition is needed by some data receivers and is not otherwise available using that gml:srsName value.

The choice in ReferencedGridByTransformation encodes an unordered list of associations to coordinate Transformations or Concatenated Operations that each (geo)reference this ReferenceableGrid. Each of these Transformations or Concatenated Operations shall reference the internal CRS for this extended gml:Grid, as either its sourceCRS or targetCRS. This association may be repeated when this ReferencedGridByTransformation is referenced to more than one other CRS, and/or is referenced to the same other CRS by multiple Transformation versions.

19.2.8	gridCRS

<element name="gridCRS" type="gml:GridCRSPropertyType"/>

<complexType name="GridCRSPropertyType">

<sequence>

<element ref="gml:AbstractCRS"/>

</sequence>

</complexType>

The gridCRS is a composition association to the definition of the “internal” CRS for this extended gml:Grid. This internal CRS may be a DerivedCRS, EngineeringCRS, ImageCRS, or CompoundCRS. However, proposed OGC Best Practices Paper 09-085r1 recommends that this internal CRS always be a DerivedCRS.

This GML extension expects that the gml:srsName attribute in gml:GridType is used to reference the internal CRS of the grid (NOT the external CRS of the Grid).  This use is expected in order to allow referencing this internal CRS in the gml:domainSet of gml:GridCoverages, so this information is available to clients of WCS 2.0 which will use GML encoding of grid coverages.  This change request thus requires editing parts of approved change request 07-121r3 as follows:

Append new text to 19.2.2 to clarify the use of SRSReferenceGroup with gml:Grid:

Notwithstanding some ambiguity in ISO 19123, a gml:Grid represents a geometry, and is associated with an ‘internal’ grid coordinate reference system (using a coordinate system with a zero origin). A grid that is also defined in an ‘external’ coordinate reference system is a rectified grid (19.2.3) if there is an affine relationship between the internal and external coordinates, or a referenceable grid (19.2.4) otherwise. The internal coordinate reference system for both these subclasses may be provided through the inherited gml:SRSReferenceGroup (including the srsName attribute). The use of gml:SRSReferenceGroup for gml:Grid was not previously defined in GML since it has no analogue in ISO 19123.

NOTE In ISO 19123, the external coordinate reference system for a CV_ReferenceableGrid is defined (ISO 19123 §8.10.2) through an explicit association Coordinate Reference System with role name crs to an ISO 19111 SC_CRS coordinate reference system object. For a CV_RectifiedGrid, it is defined implicitly (ISO 19123 §8.9.2) as the coordinate reference system of the origin.

Insert new text to 19.2.3 just before first ‘NOTE’ to clarify the use of SRSReferenceGroup with gml:RectifiedGrid:

The attribute group gml:SRSReferenceGroup inherited from gml:AbstractGeometry shall optionally link the rectified grid to the internal coordinate reference system. The external coordinate reference system to which it is rectified shall be identified through the coordinate reference system of the origin. When the gml:SRSReferenceGroup in the offsets, also inherited from gml:AbstractGeometry, does not reference the external coordinate reference system, the coordinate reference system of the origin shall be assumed.

19.2.4 AbstractReferenceableGridType, AbstractReferenceableGrid

A referenceable grid is associated with a transformation between grid coordinates and coordinates in an external coordinate reference system. Unlike a rectified grid, this transformation is usually not characterised through an affine transformation. The grid curves in the external coordinate reference system need not be straight or orthogonal, but they should retain a grid topology (i.e. the sets of curves defining the grid network should not intersect within themselves). Grid cells may be of different shapes and sizes.

NOTE	A grid topology is retained automatically through the affine transformation of a RectifiedGrid.

EXAMPLE	Figure 7 shows an example of a referenceable grid.

Figure 7 — ReferenceableGrid example

The transformation between grid coordinates and ‘external’ coordinates may take different forms. It may be described analytically (e.g. through parametrised mathematical image rectification models); or it may be provided in a table, for instance, relating the grid points to coordinates in the external coordinate reference system [ISO 19123, §8.2.1]. The method of transformation is an implementation detail not specified by ISO 19123.

The encoding of CV_ReferenceableGrid therefore uses an abstract element, gml:AbstractReferenceableGrid, as the head of a substitution group that may include various concrete implementations of the transformation.

<complexType abstract="true" name="AbstractReferenceableGridType">
        <annotation>
            <documentation>An encoding of the CV_ReferenceableGrid of ISO 19123.

A referenceable grid is a grid associated with a transformation that can be used to convert grid coordinate values to values of coordinates referenced to an external coordinate reference system [ISO 19123].

The transformation between grid coordinates and ‘external’ coordinates is usually non-affine, and may take different forms. It may be described analytically (e.g. through parametrised mathematical image rectification models); or it may be provided in a table, for instance, relating the grid points to coordinates in the external coordinate reference system [ISO 19123, §8.2.1]. AbstractReferenceableGrid is the head of a substitution group that may include various concrete implementations of the transformation.

The inherited attribute group gml:SRSReferenceGroup shall optionally link the referenceable grid to the internal coordinate reference system of the grid.</documentation>
        </annotation>
        <complexContent>
            <extension base="gml:GridType"> </extension>
        </complexContent>
    </complexType>

<element abstract="true" name="AbstractReferenceableGrid" substitutionGroup="gml:Grid"
        type="gml:AbstractReferenceableGridType"/>

The attribute group gml:SRSReferenceGroup inherited from gml:AbstractGeometry shall optionally link the referenceable grid to the internal coordinate reference system of the grid.

A property type for the gml:AbstractReferenceableGrid is also defined:

<complexType name="ReferenceableGridPropertyType">
        <sequence>
            <element ref="gml:AbstractReferenceableGrid"/>
        </sequence>
        <attributeGroup ref="gml:AssociationAttributeGroup"/>
        <attributeGroup ref="gml:OwnershipAttributeGroup"/>
    </complexType>

<element name="referenceableGridProperty" type="gml:ReferenceableGridPropertyType"/>

EXAMPLE	The referenceable grid of Figure 8 can be represented by specifying an array of grid point locations explicitly as follows (note that coordinates are specified as (Lat, Long) in EPSG 4326):

<ReferenceableGridByArray gml:id="ex" dimension="2">
        <limits>
            <GridEnvelope>
                <low>0 0</low>
                <high>4 3</high>
            </GridEnvelope>
        </limits>
        <axisLabels>x y</axisLabels>
        <posList  srsName="urn:ogc:def:crs:EPSG:6.6:4326">
            2 8	3 10	6 12	8 14	10 18
            4 6	6 8	8 12	10 14	12 16
            6 2	7 4	9 6	10 8	13 12
            8 2	8 3	10 5	11 8	13 10
        </posList>
        <sequenceRule axisOrder="+1 +2">Linear</sequenceRule>
    </ReferenceableGridByArray>

19.2.6 ReferenceableGridByVectorsType, ReferenceableGridByVectors

The gml:ReferenceableGridByVectorsType defines a referenceable grid by specifying an origin and offset vectors, with coefficients that may vary over the grid. This generalises the mechanism used for the RectifiedGrid (19.2.3), which uses offset vectors with implicit scalar (unit) coefficients.

In fact, a hierarchy of grid types may be represented using this mechanism (Figure 9). A RectifiedGrid corresponds to offset vectors with scalar (unit integer) coefficients; an irregular but rectilinear grid corresponds to real-valued coefficient vectors; while a completely irregular (curvilinear) grid corresponds to coefficient arrays.

NOTE	The latter two cases are both examples of an ISO 19123 CV_ReferenceableGrid.

NOTE	The conceptual hierarchy of Figure 9 is not required by the model presented here, and is different from ISO 19123, where CV_RectifiedGrid is not regarded as a specialisation of CV_ReferenceableGrid. There may be merit in revisiting the relationship between these classes in any future revision of ISO 19123.

Figure 9 — Hierarchy of grids with different offset vector coefficients 
(x and y range over the integer grid point indices)

The gml:ReferenceableGridByVectorsType is defined as follows:

<complexType name="ReferenceableGridByVectorsType">
        <annotation>
            <documentation>The ReferenceableGridByVectorsType specifies an origin and a sequence of 'general grid axes'. A general grid axis consists of an offset vector and a list of coefficients. These coefficients may vary along one of the grid axes (a coefficient vector), or over multiple grid axes (a coefficient array). The grid axes over which the coefficients vary is indicated with the 'gridAxesSpanned' property, and the order of the coefficients over those grid axes is indicated using the 'sequenceRule' property.

NOTE: A referenceable grid with each 'general grid axis' having unit coefficients over one general grid axis is equivalent to a RectifiedGrid.

NOTE: A referenceable grid with each 'general grid axis' having a coefficient vector (i.e. coefficients varying over just one axis of the grid) is 'rectilinear' (i.e. parallel grid lines in the external coordinate reference system).</documentation>
        </annotation>
        <complexContent>
            <extension base="gml:AbstractReferenceableGridType">
                <sequence>
                    <element name="origin" type="gml:PointPropertyType"/>
                    <element maxOccurs="unbounded" name="generalGridAxis"
                        type="gml:GeneralGridAxisPropertyType"/>
                </sequence>
            </extension>
        </complexContent>
    </complexType>

<element name="ReferenceableGridByVectors" substitutionGroup="gml:AbstractReferenceableGrid"
        type="gml:ReferenceableGridByVectorsType"/>

The element gml:origin represents the origin of the referenceable grid in the external coordinate reference system. That external coordinate reference system shall be identified through the coordinate reference system of that origin. When the gml:SRSReferenceGroup in the offset vectors, also inherited from gml:AbstractGeometry, does not reference the external coordinate reference system, the coordinate reference system of the gml:origin shall be assumed.

The set of gml:generalGridAxis elements provide offset vectors (with corresponding coefficients) that together span the (sub-)space containing the convex hull of the referenceable grid. A grid point location in the external coordinate reference system is calculated from the sum of the offset vectors from all gml:generalGridAxis elements weighted by their respective coefficients for the grid point concerned.

The gml:GeneralGridAxisType specifies an offset vector and array of coefficients over all grid points. Both an element and property-type are defined in order to allow the GML by-reference pattern (7.2.3.3):

<complexType name="GeneralGridAxisType">
        <sequence>
            <element name="offsetVector" type="gml:VectorType"/>
            <element name="coefficients" type="gml:doubleList"/>
            <element name="gridAxesSpanned" type="gml:NCNameList"/>
            <element name="sequenceRule" type="gml:SequenceRuleType"/>
        </sequence>
    </complexType>

<element name="GeneralGridAxis" type="gml:GeneralGridAxisType"/>

<complexType name="GeneralGridAxisPropertyType">
        <sequence minOccurs="0">
            <element ref="gml:GeneralGridAxis"/>
        </sequence>
        <attributeGroup ref="gml:AssociationAttributeGroup"/>
        <attributeGroup ref="gml:OwnershipAttributeGroup"/>
    </complexType>

The element gml:offsetVector specifies a vector in the external coordinate reference system. The element gml:coefficients specifies a corresponding set of weighting coefficients over the grid points. In some cases these coefficients will be uniform along one or more axes of the grid, and for efficiency reasons the coefficients need only be specified along those axes on which they vary. The grid axes over which the coefficients vary is indicated with the gml:gridAxesSpanned element, and the order of the coefficients over those grid axes is indicated using the gml:sequenceRule element.

NOTE	A referenceable grid with each 'general grid axis' having unit coefficients over one grid axis is equivalent to a RectifiedGrid.

NOTE	A referenceable grid with each 'general grid axis' having a coefficient vector (i.e. coefficients varying over just one axis of the grid) is 'rectilinear' (i.e. parallel grid lines in the external coordinate reference system).

NOTE	Any referenceable grid may be embedded within a space of dimension greater than, or equal to, its grid dimension. For example, a two-dimensional grid may be embedded within a three-dimensional volume – either by lying in an oblique plane (Figure 10), or by lying in a surface curved within three dimensions (Figure 11). The latter case is defined by specifying three offset vectors. In general, the following constraints apply for any referenceable grid (analogous to those for rectified grids, ISO 19123 §8.9.6):

(grid dimension) ≤ (number of offset vectors) ≤ (CRS dimension)

Figure 10 — ReferenceableGrid embedded in oblique plane (two offset vectors)

Figure 11 — ReferenceableGrid embedded in curved surface (three offset vectors)

EXAMPLE 1	The (rectilinear) referenceable grid of Figure 12 requires coefficient vectors along each grid axis. It is represented as follows:

<ReferenceableGridByVectors gml:id="ex1" dimension="2">
        <limits>
            <GridEnvelope>
                <low>0 0</low>
                <high>4 3</high>
            </GridEnvelope>
        </limits>
        <axisLabels>x y</axisLabels>
        <origin>
            <gml:Point gml:id="o1.1" srsName="urn:ogc:def:crs:EPSG:6.6:4326">
                <pos>2 8</pos>
            </gml:Point>
        </origin>
        <generalGridAxis>
            <GeneralGridAxis>
                <offsetVector>1 2</offsetVector>
                <coefficients>0 1 3 6 7</coefficients>
                <gridAxesSpanned>x</gridAxesSpanned>
                <sequenceRule axisOrder="+1">Linear</sequenceRule>
            </GeneralGridAxis>
        </generalGridAxis>
        <generalGridAxis>
            <GeneralGridAxis>
                <offsetVector>1 -1</offsetVector>
                <coefficients>0 1 4 6</coefficients>
                <gridAxesSpanned>y</gridAxesSpanned>
                <sequenceRule axisOrder="+1">Linear</sequenceRule>
            </GeneralGridAxis>
        </generalGridAxis>
    </ReferenceableGridByVectors>

Figure 12 — ReferenceableGridByVectors – rectilinear grid with coefficient vectors

EXAMPLE 2	The (curvilinear) referenceable grid of Figure 8 earlier may be specified using coefficient arrays across both axes of the grid. It is represented as follows (see Figure 13):

<ReferenceableGridByVectors gml:id="ex2" dimension="2">
        <limits>
            <GridEnvelope>
                <low>0 0</low>
                <high>4 3</high>
            </GridEnvelope>
        </limits>
        <axisLabels>x y</axisLabels>
        <origin>
            <gml:Point gml:id="o1.2" srsName="urn:ogc:def:crs:EPSG:6.6:4326">
                <pos>2 8</pos>
            </gml:Point>
        </origin>
        <generalGridAxis>
            <GeneralGridAxis>
                <offsetVector>0.333 0.667</offsetVector>
                <coefficients>
                    0	3	8	12	18
                    0	4	10	14	18
                    -2	1	5	8	15
                    0	1	5	9	13
                </coefficients>
                <gridAxesSpanned>x y</gridAxesSpanned>
                <sequenceRule axisOrder="+1 +2">Linear</sequenceRule>
            </GeneralGridAxis>
        </generalGridAxis>
        <generalGridAxis>
            <GeneralGridAxis>
                <offsetVector>0.667 -0.667</offsetVector>
                <coefficients>
                    0	0	2	3	3
                    3	4	4	5	6
                    7	7	8	8	9
                    9	8.5	9.5	9	10
                </coefficients>
                <gridAxesSpanned>x y</gridAxesSpanned>
                <sequenceRule axisOrder="+1 +2">Linear</sequenceRule>
            </GeneralGridAxis>
        </generalGridAxis>
    </ReferenceableGridByVectors>

Figure 13 — ReferenceableGridByVectors – curvilinear grid with coefficient arrays

Changes to the OGC Abstract Specification

This GML change request requires extension of OGC™ Abstract Specification Topic 6: The Coverage Type and its Subtypes (which includes ISO 19123:2006). Clause 8.10, and the CV_ReferenceableGrid class in Figure 17, of that document assume the existence of only one coordinate transformation operation, as defined by ISO 19111:2003, by which one CV_ReferenceableGrid is referenced. However, the same grid may be, and often is, referenced by a concatenated coordinate operation, as defined by ISO 19111:2003.  Furthermore, multiple coordinate transformation or concatenated operations may exist for the same grid (and the same grid coverage) that are referenced to more than one other CRS, and/or are referenced to the same other CRS by multiple Transformation versions (with different accuracy characteristics).

Possible changes to this change request

The <element ref="gml:gridCRS" minOccurs="0"/> probably should be included in gml:AbstractReferenceableGridType, instead of in gml:ReferencedGridByTransformationType.

In this change request, names for several new XML elements are used when other names that may be better could be used as listed in the following table:

| Current element name | Alternative element names |
| --- | --- |
| ReferencedGridByTransformation | ReferencableGridByTransformation ReferenceableGridByTransformation |
| gridCRS | internalCRS internalGridCRS |

# Attachments

Attached to this change request is a valid XML Schema Document that includes these XML Schema fragments, plus several example and template XML documents.

# Comments

Enter the AS or Implementation Specification Name and Number in this box. For example, WMS 1.1.1 or GML 3.0. Do not prefix the number with anything, i.e. do not use "OGC", "GSM" or "OGC" etc.

Enter the CR number here. This number is allocated by the OGC support team.

Enter the revision number of the CR here. If it is the first version, use a "-".

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X. AS = Abstract Specification, IS = Implementation Specification, Recom. Paper = Recommendation Paper, Other = DIPR/IPR, etc.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.

Enter the source of the CR. This is either (a) one or more OGC members or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

IF there is one, enter the work item code or issue code that is applicable to the change. These codes will relate to Work Items identified in a WBS associated with a particular OGC initiative. If there is no code, leave blank.

Enter the date on which the CR was last revised.

Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the TC Policies and Procedures".

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. essential correction).

Enter each the number of each clause which contains changes.

Enter an X in the box if any other specifications are affected by this change.

If known, list here the specifications which are affected or the CRs which are linked.

Explanation of Field: If there is associated documentation, such as an lengthy change request or new text for consideration, please reference the OGC document number and document title.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.

This is the status of the change request. For a new submission, please enter “NEW”. Other options as the change request is processed are: Assigned, Verified, Resolved, and Closed.

This field is used to assign the RWG decision for this Change Request. Options include: Deferred, Accepted, and Rejected.

# Text boxes

o

origin

Offset Vectors

Grid Points

o

origin

Offset Vectors

Grid Points

v1 = (1,2)

v2 = (1,-1)

8

2

(11,8) = (2,8) + 3 × (1,2) + 6 × (1,-1)

x

y

Long

Lat

x

y

Long

Lat

8

2

v1 = (1/3, 2/3)

v2 = (2/3, -2/3)

(10,5) = (2,8) + 5 × (1/3,2/3) + 9.5 × (2/3,-2/3)